## Slide 1: b1000 Single Cycle CPU
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowledgements
Alyssa Bawgus
Orion Taylor

## Slide 3: Today
Review Growth Characteristics
Intro to Memory and Assembly
The Execution of an Instruction
Intro to Simple CPU Design
Assign Homework & Lab

## Slide 4: Decoder Growth Review
For a decoder with S select bits and D outputs
  D = 2^S
Need
  S Inverters
  D AND Gates with S inputs
Total Size:

## Slide 5: Decoder Growth Review
For a decoder with S select bits and D outputs
  D = 2^S
Need
  S Inverters (S)
  D AND Gates with S inputs (DS)
Total Size: DS+S = +1)=(D+1)log2(D)

## Slide 6: Look Up Table w/Decoder

## Slide 7: Look Up Table w/Decoder

## Slide 8: Growth Characteristics
This has 12 Gate Inputs
  4 AND2 (8)
  1 OR4 (4)
Per decode line:
  1 AND2
  1 input of the OR
(#Decode Lines)*3

## Slide 9: LUT Growth Review
For a LUT with Depth D and Output Width W
Need
  1 Decoder
  W Output Structures
Total Size:

## Slide 10: LUT Growth Review
For a LUT with Depth D and Output Width W
Need
  1 Decoder (D+1)log2(D)
  W Output Structures W(3D)
  Total Size: (D+1)log2(D) + W(3D)

## Slide 11: Adder Comparison
LUT for 32bit + 32bit = 32bit addition
  S = (32+32) = 64
  W = 32
  D=2^S = 18446744073709551616
Total Size = (D+1)log2(D) + W(3D)
  2951479051793528258624

## Slide 12: Adder Comparison
LUT for 32bit + 32bit = 32bit addition
  Size
Chained Full Adder
  9 NAND2 Gates per bit
  Size = 32 * 18 = 576
Apollo Guidance Computer:
  4100 NOR3 ( 12,300 gate inputs)

## Slide 13: Context
We now have almost all of the building blocks of a computer!
  Nearing completion of our first “spiral”
Today we will glance at the important ones
Moving forward we will dive deeper into each of these building blocks to expand capabilities

## Slide 14: Context
You will learn the dark arts of box opacity
Practice thinking hierarchically
So… what does a CPU do?

## Slide 15: CPU Execution Overview
Fetch instruction from memory
Decode instruction into actions/controls
Fetch/Decode operands
Compute result value or status
Push result(s) to storage
Determine next instruction
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 16: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 17: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 18: Processor Overview
Overall Dataflow
PC fetches instructions
Instructions select operand registers, ALU immediate values
ALU computes values
Load/Store addresses computed in ALU
Result goes to register file or Data memory

## Slide 19: Memory
Look Up Table is a very simple memory
  Read One thing at a time
  Write nothing ever
Generically, a memory is defined by:
  Width & Depth
  Number and Type of Ports
    How many simultaneous read / write operations
  Speed (access time)

## Slide 20: Memories
We will devote several lectures entirely to memory
I will treat it as an opaque black box for this lecture, and open it in much more detail later
Your lab is all about one type of memory

## Slide 21: Register File
Very small, very fast multi-ported memory
  Small depth, large silicon area
Each cycle reads 2 words, optionally writes 1
This is the “scratch space” for the processor
This is your lab
Aw Aa Ab Da
Dw Db
Register
WrEn File

## Slide 22: Program/Instruction Memory
Large, single ported read-only memory
  For today
Stores the program the processor executes
Instructions are 4 bytes wide
  For today

## Slide 23: Why 4?
Today we are assuming 4 byte instructions
Why? This is hilarious and I needed an excuse to show it to you.
Notes: Actual Best Slide Ever

## Slide 24: Assembly
The human readable version of the instructions the machine executes
Closely related to “Op Codes” and Instructions
We will go over this in detail next week.

## Slide 25: Instruction Decode
Today we are “black boxing” instructions
Blue Wires come from the Instruction Decoder
  Control signals that tell the CPU what to do
  E.g. ALU Control Lines
  Addresses

## Slide 26: Instruction RTL
RTL is Register Transfer Level
Short Hand for what the instruction should do
Reg[Rd] = Reg[Rs] & Reg[Rt]
Set the memory at location Rd equal to the data at location Rs boolean anded with the data at location Rt.

## Slide 27: Fetch Operands
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Rd Rs Rt
Get Operand Addresses
Pull from Register File

## Slide 28: Execute
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Rd Rs Rt
ALU controls from Instruction Fetch/Decode
Perform actual computation in ALU
Result

## Slide 29: Execute
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Rd Rs Rt
ALU controls from Instruction Fetch/Decode
Perform actual computation in ALU

## Slide 30: Store Results
Instruction
Fetch
Unit
Rs
Rt
Rd
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Rd Rs Rt
Most Instructions store the result back to the register file
Others have other effects

## Slide 31: Using Constants
Sometimes we want to use a constant as an operand instead of a Register.
How do you encode a 32 bit constant AND control signals into a 32 bit instruction?
Side Note: The Cortex has interesting options
  any constant produced by shifting an 8-bit value
  any constant of the form 0x00XY00XY
  any constant of the form 0xXY00XY00
  any constant of the form 0xXYXYXYXY
Side Note: MIPS only has boring 16 bit constants

## Slide 32: Using Constants (Immediates)
Reg[rt] = Reg[rs] + SignExtend(imm);
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16
SignExtnd
Imm16
Rs
Rt
Notes: Note that Aw is now connected to Rt instead of Rd. This is not an error – Rd occupies the same space as part of the immediate in the instruction, and is therefore not available for this instruction. This is resolved soon!

## Slide 33: Data Memory
Big Giant Slow Memory
  Gigabytes!
Read and Write, but only single port
  Write Enable (WrEn) switches between the two modes
Pulling from Data Memory to Register
  Load
Push from Register to Data Memory
  Store
WrEn Addr
Din Dout
Data
Memory

## Slide 34: Hook Up On The Boards
Create simple CPU with 4 types of instructions
  Listed on next Slide
Use the following Components
  ALU, Register File, Data Memory, Sign Extender
Use another marker color for control signals
To make a decision, use a MUX

## Slide 35: Hook Up On The Boards
Math with 2 Variables
Reg[rd] = Reg[rs] op Reg[rt];
Math with 1 variable and 1 constant
Reg[rt] = Reg[rs] op SignExtend(imm);
Load from data memory
Addr = Reg[rs] + SignExtend(imm);
Reg[rt] = Mem[Addr];
Store to data memory
Addr = Reg[rs] + SignExtend(imm);
Mem[Addr] = Reg[rt];

## Slide 36: One Possible Complete Datapath
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 37: Lets Talk Labs
It is all about the process
Please do not make this an ugly competition
Cleverness and Realism!

## Slide 38: With the remaining time
Begin Work on Lab

## Slide 39: Using Constants (Immediates)
SignExtnd
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Data
Memory

## Slide 40: Datapath + Load
Addr = Reg[rs] + SignExtend(imm);
Reg[rt] = Mem[Addr];
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
RegDst
Rd
Rt
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16

## Slide 41: Datapath + Store
Addr = Reg[rs] + SignExtend(imm);
Mem[Addr] = Reg[rt];
Note: State of RegWr, MemToReg?
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16