## Slide 1: b10100 Call Me, Maybe
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Today
Calling Simple/“Leaf” Functions
The Stack
Calling Generic Functions
Calling Conventions
mp3

## Slide 3: What is a function?
A procedure is a stored subroutine that performs a specific task based on the parameters it is provided.
  <Pattersen & Hennessy>
a = f(x,y,z); // You have seen this before
A spy on a secret mission
  Seriously, the textbook we used to use is hilarious.

## Slide 4: What is a function?
A block of code formatted in a way that allows it to be called by other code, and then returns execution to the caller
How is this similar to / different from one of our “GOTO” targets?

## Slide 5: The Life of a Called Function
The caller stores parameters “somewhere”
Control (Execution) is passed to the callee
The callee does some stuff
The callee stores the results “somewhere”
Control is passed back to the caller

## Slide 6: Calling Conventions
A Calling Convention standardizes where those “somewheres” are.
  Registers? Data Memory?
  Return values?
  How do we return control back to the caller?
It is just another type of contract
  The great thing about standards is that there are so many to choose from.

## Slide 7: Execution Flow
Lets work through a simple example
void main()
{
// do some stuff
MyFunction();
// do other stuff
}

## Slide 8: Execution Flow
Idea 1:
Jump to subroutine
Jump back when done
#Caller (main)
#do stuff j MyFunction
returnToMain:
#dootherstuff
#callee
MyFunction:
#code code code j returnToMain

## Slide 9: Execution Flow
Idea 1:
Jump to subroutine
Jump back when done
What if I want to use the function again elsewhere?
#Caller (main)
#do stuff j MyFunction
returnToMain:
#dootherstuff
#callee
MyFunction:
#code code code j returnToMain

## Slide 10: Execution Flow
Idea 2:
Store return address
Jump to subroutine
Jump back when done
#Caller (main)
#do stuff
ReturnAddr = PC+??? j MyFunction
returnToMain:
#dootherstuff
#callee
MyFunction:
#code code code jr ReturnAddr

## Slide 11: Execution Flow
In MIPS, this is called Jump And Link (jal)
jal stores the PC+4 to $31 and then jumps to the target address
$31 is also known as $ra
  Return Address
Jump Register (jr) to get back
#Caller (main)
#do stuff jal MyFunction
#dootherstuff
#callee
MyFunction:
#code code code jr $ra

## Slide 12: Execution Flow
Storing the Return Address in $ra is great!
  but only for Leaf Functions
What if a function calls another function?
  Put it in Data Memory!
  Every function has a dedicated space to shove $ra

## Slide 13: Execution Flow
Storing the Return Address in $ra is great!
  but only for Leaf Functions
What if a function calls another function?
  Put it in Data Memory!
  Every function has a dedicated space to shove $ra
What if… A FUNCTION CALLS ITSELF?!?!
  OMG Inception

## Slide 14: Stack Attack
Dedicating memory per function is limiting
  Wastes space when it isn’t active
  Can’t recurse
Instead, allocate data memory as needed
We use “The Call Stack”
  Last In, First Out
  Push stuff onto the head of the stack
  Pop stuff back off of it

## Slide 15: The Call Stack
Is a Stack of “Frames”
Each active function instantiation has a Frame
Frames hold the instance memory
  Like the return address

## Slide 16: Mechanics of the Call Stack
Architecture Decisions:
  Where is the Stack?
  How do we address it / point to it?
    Linked List? Raw Pointer?
Calling Convention Decisions:
  What stuff is put on it?
  In what order? (Frame Definition)
  By whom? (Caller? Callee?)

## Slide 17: Mechanics of the Stack
Ascending/Descending
  Ascending stacks start at address 0 and grow up
  Descending stacks start at the other end and grow down
Full / Empty
  Empty stack pointers point to the next unallocated address
  Full stack pointers point to the top item in the stack
MIPs uses a “full descending” stack
  With $29 ($sp) as the stack pointer
ARM supports all 4, usually uses full descending
  Procedure Call Standard for the ARM Architecture (AAPCS)

## Slide 18: Why Descending?
There are two dynamic memory spaces
The “Heap” handles memory dynamically allocated at run time
  malloc /free
  new / delete
Traditionally:
  Heap ascends
  Stack descends
Giovanni Gracioli

## Slide 19: Full Descension Example
PUSH $t3, $t4 onto the stack
addi $sp, $sp, -8 #allocate 2 word
sw $t3, 4($sp) #push $t3
sw $t4, 0($sp) #push $t4
What does the stack look like after this push?
Does order of operations matter here?

## Slide 20: Full Descension Example
Pop $t3, $t4 from the stack
lw $t3, 4($sp) #pop $t3
lw $t4, 0($sp) #pop $t4
addi $sp, $sp, 8 #delete 2 words
What does the stack look like after this push?
Two pops, one add

## Slide 21: Factorial Function
int Fact(int n){
if(n>1)
return n* Fact(n-1)
else
return 1

## Slide 22: Factorial Function
int Fact(int n){
if(n<=1) goto end:
return n* Fact(n-1)
end:
return 1

## Slide 23: Factorial Function
$v0 Fact(int n){
if(n<=1) goto end:
$v0 =n* Fact(n-1)
jr $ra
end:
$v0 = 1
jr $ra

## Slide 24: Factorial Function
$v0 Fact ($a0)
ble $a0, 1, end:
$v0 =n* Fact(n-1)
jr $ra
end:
$v0 = 1
jr $ra
We have most of what we need:
  Goto flow control for if
  jr $ra for return
  Registers assigned
Now we need to call Fact
  What do we save?
  What order?
Lets focus on the call site

## Slide 25: Factorial Function Call Site
To Call Fact:
  Push registers I need to save
    $ra
    $a0
  Setup Arguments
    N-1: $a0 = $a0-1
  Jump and Link Fact:
  Restore registers

## Slide 26: Factorial Function Call Site
add $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $a0, $a0, -1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 27: Factorial Function Call Site
add $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $a0, $a0, -1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 28: Factorial Function Call Site
add $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $a0, $a0, -1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 29: Factorial Function Call Site
add $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $a0, $a0, -1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 30: Factorial Function
fact:
;if(N<=1) return 1
ble $a0, 1, end:
;Push $ra, $a0
add $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
;Argument N-1
add $a0, $a0, -1
jal fact
;Pop $ra, $a0
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
;Return N*Fact(N-1)
mul $v0, $v0, $a0
jr $ra
end:
;Return 1
$v0 = 1
jr $ra

## Slide 31: Calling Function
li $a0, 4
jal factorial
move $s0, $v0
li $a0, 2
jal factorial
move $s1, $v0
li $a0, 7
jal factorial
move $s2, $v0
li $v0, 10
syscall
Calls Factorial several times
Stores results in $sN
li is a pseudoinstruction
  What does it assemble to??
The final two lines call a special simulator function to end execution
  10 means exit
  Look up other syscalls in help

## Slide 32: Calling Convention
We have decisions to make for registers:
  Are they used as part of the call?
  Are they preserved across the call?
  Are they reserved for other uses?
… and about passing arguments around
  In registers?
  On the stack?
  In generic data memory?

## Slide 33: Where is the stack frame constructed?
By the Caller
  Right before and after the “jal”
  Preserve own register state “just in case”
By the Callee
  Push after “functionname:”, Pop before “jr”
  Preserve register state so they are usable
Which reduces unnecessary push/pops?

## Slide 34: MIPs Specifics
Uses $vN to store results
  V for Valuetta
Uses $aN to store first 4 arguments
  A is for Argument, that’s good enough for me
  Extra are pushed to the stack

## Slide 35: MIPs Specifics
$sN are Saved Temporaries
  The callee is responsible for saving these if used
  The caller can assume they are unchanged
$tN are Volatile Temporaries
  The callee can do whatever it wants with these
  The caller can’t rely on these across a call
Advantages/Disadvantages to these?

## Slide 36: Lets Do This
Write the “Fibonacci” function recursively:
    int Fibonacci(int x) {
    if (x == 0) return 0; // Stopping conditions
    if (x == 1) return 1;
    return Fibonacci(x - 1) + Fibonacci(x - 2); }
You will have to invent parts of your own calling convention here. Take notes on what you invented.
  Where do you store parameters? Return Values? Return Addresses?
This will be easier if you write in human first
  Drawing your stacks helps too!

## Slide 37: Frame Pointer
$sp can move around during a procedure
  This makes frame contents shift around
    Relative to the stack pointer
  Makes debugging hard
A Frame Pointer stays put during a procedure
  Makes debugging easier!
  Makes compiling easier too, but I don’t care

## Slide 38: Frame Pointer
Isn’t strictly necessary
  But it makes debugging so much easier
Not all implementations use it
  GNU MIPS C Compiler does
  MIPS MIPS C compiler does not

## Slide 39: A MIPS calling convention’s frame
From WinCE 5.0
Arguments at top of previous frame
$ra
Saved nonvolatiles
Locals
http://msdn.microsoft.com/en-us/library/aa448710.aspx

## Slide 40: Vocab
Blowing the Stack / Stack Overflow / Stack Smashing
  Running out of stack space
  Writes over other data! (Heap)
  Possible security vulnerability
Unwind the Stack
  Popping “frames” off the stack
  Usually in the context of exception handling
Walking the Stack
  Looking at the Stack and figuring out where you are
  Usually in the context of Debugging
  Need to be able to “see” where the frames are

## Slide 41: Vocab
Misaligning or Unbalancing the stack
  Pushing or popping a different number of times
  Catastrophic Error!
Stack Dump
  Produced when program crashes
  Helps you understand where you were when stuff went wrong

## Slide 42: Stack Dump Example
Error Message:
Value cannot be null.
Parameter name: value
Exception:
ArgumentNullException
Suggestion:
Contact National Instruments to report this error
Stack Trace:
at System.BitConverter.ToInt32(Byte[] value, Int32 startIndex)
at NationalInstruments.LabVIEW.VI.VirtualMachine.Target.ExecutionHighlighting.ProcessUpdate(Byte[] buffer)
at NationalInstruments.X3.Model.DeviceModel.OnExHighlightReadCompletedEventHandler(Object sender, ReadCompletedEventArgs e)
at NationalInstruments.X3.Model.DeviceModel.<>c__DisplayClass37.<ReadTargetMemory>b__36(Object theSender, RequestCompletedEventArgs theE)

## Slide 43: mp3
Final Lab!
Schedule Stinks 
Try to avoid working over the break

## Slide 44: Final Project
Individually, send in 1 rough idea for a Final Project
Due Wednesday at Noon
  comparch14@gmail.com
  [FP Idea]