## Slide 1: b0110 ALU
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Today
Back to Gates!
Review Timing with Adders
Compare Growth Characteristics
Construct Adder/Subtractor
Construct ALU
Multiply / Divide by R^?

## Slide 3: Full Adder
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
CO
0
0
0
1
0
1
1
1
S
0
1
1
0
1
0
0
1
 | A | B | Cin
Sum |  |  | 
Cout |  |  | 
Calculate Propagation Delays
Multiple Paths? Choose Worst

## Slide 4: Full Adder
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
CO
0
0
0
1
0
1
1
1
S
0
1
1
0
1
0
0
1
 | A | B | Cin
Sum | 6 | 6 | 3
Cout | 5 | 5 | 2
Calculate Propagation Delays
Multiple Paths? Choose Worst

## Slide 5: Multi-Bit Addition
 | A | B | Cin
Sum | 6 | 6 | 3
Cout | 5 | 5 | 2
 | AB0 | AB1 | AB2
S0 |  |  | 
C1 |  |  | 
S1 |  |  | 
C2 |  |  | 
S2 |  |  | 
C3 |  |  | 
Using previous slides’ design, find worst prop delay

## Slide 6: Multi-Bit Addition
 | A | B | Cin
Sum | 6 | 6 | 3
Cout | 5 | 5 | 2
 | AB0 | AB1 | AB2
S0 | 6 | - | -
C1 | 5 | - | -
S1 | 5+3 | 6 | -
C2 | 5+2 | 5 | -
S2 | 5+2+3 | 5+3 | 6
C3 | 5+2+2 | 5+2 | 5
Using previous slides’ design, find worst prop delay

## Slide 7: Full Adder as a LUT in Gates
 | A | B | Cin
Sum |  |  | 
Cout |  |  | 
A B Cin
0
0
0
1
0
1
1
1
Only half, slide too small to show Sum
Area Cost?
Speed?

## Slide 8: Full Adder as a LUT in Gates
 | A | B | Cin
Sum | 3 | 3 | 3
Cout | 3 | 3 | 3
A B Cin
0
0
0
1
0
1
1
1
Only half, slide too small to show Sum
Area Cost?
Speed?
Notes: Each “True” is a 3 input AND
Each output is a 4 input OR
Each input is an inverter
3*4*2 = 24
4*2 = 8
3*1 = 3
=35 GIE
Other solution was 9*2 = 18

## Slide 9: Timing with Alternate Topology
 | A | B | Cin
Sum | 3 | 3 | 3
Cout | 3 | 3 | 3
 | AB0 | AB1 | AB2
S0 |  |  | 
C1 |  |  | 
S1 |  |  | 
C2 |  |  | 
S2 |  |  | 
C3 |  |  | 
Using new prop delays, find total delay

## Slide 10: Timing with Alternate Topology
 | A | B | Cin
Sum | 3 | 3 | 3
Cout | 3 | 3 | 3
 | AB0 | AB1 | AB2
S0 | 3 | - | -
C1 | 3 | - | -
S1 | 3+3 | 3 | -
C2 | 3+3 | 3 | -
S2 | 3+3+3 | 3+3 | 3
C3 | 3+3+3 | 3+3 | 3
Using new prop delays, find total delay

## Slide 11: Growth Rates
What changes as a specific design ‘grows’
  Propagation delay
  Silicon area
Propagation Delay for an N bit adder?
  Design 1: NAND Gates
  Design 2: Small LUT

## Slide 12: Growth Rates
What changes as a specific design ‘grows’
  Propagation delay
  Silicon area
Propagation Delay for an N bit adder?
  Design 1: 2N + 4
  Design 2: 3N
Which design is faster for small adders?
Notes: 2N+4 = 3N when N = 4
When adding more than 4 bits, the NAND gate based circuit is faster than the LUT based approach

## Slide 13: Adder/Subtractor
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
3
B
3
A
2
B
2
A
1
B
1
A
0
B
0
S
3
S
2
S
1
S
0
Subtract
Add Control Line for Subtraction

## Slide 14: Adder/Subtractor
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
3
B
3
A
2
B
2
A
1
B
1
A
0
B
0
S
3
S
2
S
1
S
0
Subtract
Add Control Line for Subtraction

## Slide 15: ALU: Arithmetic Logic Unit
Computes arithmetic & logic functions based on controls
  Add, subtract
  AND, NAND, OR, NOR, XOR, ==, <, overflow, …
A
B
R
Function
Select
Controls
Zero
Negative
Overflow

## Slide 16: ALU: Easy Design
Separate units for each operation
Mux at the end

## Slide 17: ALU: Easy Design
Separate units for each operation
Mux at the end
“Default” Method
Potentially fastest method
No optimization BETWEEN components

## Slide 18: Bit Slice ALU Design
00: OR
10: Add
01: AND
11: Subtract
4:1 Mux
00 01 10 11
S1
S0
Ai
Bi
ALU Output Bit

## Slide 19: Bit Slice ALU Design (cont.)
Route Carries
Overflow, zero, negative
1-bit
Slice
1-bit
Slice
1-bit
Slice
1-bit
Slice
ALU3
ALU2
ALU1
ALU0
ALU[3:0]

## Slide 20: SLT
Set less than: if (A<B) then R = 1, else R = 0
  How do we know if (A<B)
  Interaction w/overflow?
  Interaction w/carry out?
At your Desk:
  Try 2 random examples
  Try 2 corner cases
  Do they all work?
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1

## Slide 21: ALU Construction Summary
Brute force approach is full parallel with muxes as wide as the number of operations
Re-use resources for space efficiency
  Slower, Smaller, Narrower
Make a SMALL ALU bit slice that does:
  AND, OR, NAND, NOR, XOR, Add, Subtract

## Slide 22: Do a Barrel Roll
We can multiply or divide a number by 2 by moving it left or right one position
This is called a “shift”
  b00000011 d3
  b00000110 d6
  b00001100 d12
  b00011000 d24

## Slide 23: Do a Barrel Roll
“Arithmetic” shifts obey 2’s complement
  Sign extension
“Logical” shifts do not
  Assume unsigned
  Pad zeros
Barrel Rotate “wraps” around

## Slide 24
http://bwrc.eecs.berkeley.edu/research/pico_radio/Test_Bed/Hardware/Documentation/ARM/chap3.pdf

## Slide 25: Create a Shifter
Start with Logical Shift Left (LSL) only
  Add the others maybe
Construction Options:
  Layers of Shift by R^N
  Bit slices that shift a single bit an arbitrary amount
Where in the ALU would you put it?

## Slide 26: Growing Shifters
Chain optional power-of-two shifts
  Sometimes called a logarithmic shifter
  Each Layer shifts by either zero or 2^“Layer Number”
  Each Layer shifts by R^“Layer Number”*[0..R)
Requires logR(N) layers
  N=32, R=2 -> 5 layers
How big / fast is a R=2 Logarithmic Shifter?
What R would you choose for a N=256 Shifter?

## Slide 28: As a GIANT LUT!
How expensive is a Depth by Width LUT?
  2^M = Depth
Decoder (M->D)
  M inverters
  D M-input AND gates
  2 Units of Delay
  M+MD space
Decoder -> Mux
  D*W 2 input AND gates
  W D-input OR gates
  2 Units of Delay
  3DW Space
Bussed Mux -> LUT
  Tie inputs to Constants
  Free!
Total:
  4 Units Delay
  M+MD+3DW Space
  2N+(5N+3)(2^2N) Space

## Slide 29: Multiple Bit Addition w/ LUT
How do we construct 3-bit addition as one unified LUT?
  Sum[3:0] = a[2:0]+b[2:0]
  Width?
  Depth?

## Slide 30: Multiple Bit Addition w/ LUT
How do we construct 3-bit addition as one unified LUT?
  Sum[3:0] = a[2:0]+b[2:0]
  Width? 4 (3 Sum Bits, 1 final carry out bit)
  Depth? 2^(3+3) = 64
Index into table = {a[2:0],b[2:0]}
  Rows in table = {b2,b1,b0}+{a2,a1,a0}
Notes: {a[2:0],b[2:0]} means concatenate the two busses into one bus who has a width equal to the sum of the their widths

## Slide 31: Multiple Bit Addition w/ LUT
Example: Add d3+d4 with our LUT
  a = d3 = b011
  b = d4 = b100
  LUT address = {a,b} = b011100
Look in table at that address
  Recover answer = b0111 = d7
  d3+d4=d7!
Notes: {a[2:0],b[2:0]} means concatenate the two busses into one bus who has a width equal to the sum of the their widths

## Slide 32: Multiple Bit Addition w/ LUT
Calculate the Size Growth of the LUT approach
  HINT: Build up from Decoder, Mux, etc
  How big is a 1 bit LUT adder?
  How big is a 8 bit LUT adder?
  How big is an N bit LUT adder?
Repeat for the chained Full Adder approach
Notes: Confusion of conflating LUT with Adder. Separate for this example and then recombine.

## Slide 33: LUT Growth
Theoretically, LUT speed is flat with size
  Always 3 gates Deep – Inverter, AND, OR
  Spoiler Alert – IT ISN’T
Area grows VERY quickly
Calculate the Size Growth of the LUT approach
  W = N+1
  D =
Repeat for the chained Full Adder approach
Notes: Confusion of conflating LUT with Adder. Separate for this example and then recombine.