## Slide 1: b1001 Single Cycle CPU Continued
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Today
Lab Check In
Continue Single Cycle CPU
Jumps and Branches
Instruction Encoding

## Slide 3: Single Cycle Design Process
Instructions
RTL – Register Transfer Level
  Describes how the instruction is executed
  How information flows between registers
Schematic
  Arranges building blocks to implement RTL

## Slide 4: One Possible Complete Datapath
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 5: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 6: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 7: Processor Overview
Overall Dataflow
PC fetches instructions
Instructions select operand registers, ALU immediate values
ALU computes values
Load/Store addresses computed in ALU
Result goes to register file or Data memory

## Slide 8: Fetch Instruction
Instruction = Mem[PC]; // Fetch Instruction
PC = PC + 4; // Increment Program Counter
Adder
PC
Address
Instruction
Memory
Instr[31:0]
“4”
Notes: PC is a Register composed of edge triggered D Flip Flops.
Clock is missing from the diagram.

## Slide 9: Flow Control
for(int i = 0; i<N; i++) {
a = b + c;
b *= 3;
}
Jump – Unconditionally change PC
Branch – Conditionally change PC

## Slide 10: Flow Control
for(int i = 0; i<N; i++) {
a = b + c;
b *= 3;
}
Jump – Unconditionally change PC
  Jump back to the beginning of the loop
Branch – Conditionally change the PC
  Escape loop if i<N fails

## Slide 11: Add Flow Control
Modify the Instruction Fetch Unit to Branch:
  if ((Reg[rs] – Reg[rt]) == 0)
  PC = PC +4+ SignExtend(imm)*4;
  else
  PC = PC + 4;
Write RTL for your version of Jump
  What does Jump mean to you?
Implement your RTL
  What new control lines do you need?
  Any cool money saving tricks?

## Slide 12: Difficulties In Jumping
How did you define your Jump?
  Absolute: PC = New Value
  Relative: PC += Offset
Did you have enough bits?

## Slide 13: Complete Fetch Unit
SignExtnd
PC
Addr[31:2]
Addr[1:0]
Instruction
Memory
Concatenate
Adder
Instr[31:0]
Jump
“00”
PC[31:28]
Target Instr[25:0]
imm16
“1”
Zero
Branch
Cin
“0”

## Slide 14: Jump RTL
Jump Instruction: j target
PC = { PC[31:28], target[25:0], “00” };
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address
Weirdness in the Address Field
Bottom 2 bits are always ‘00’, so drop’em
  Shift everything over by 2
That’s only 28 effective bits…
  Where are the other 4?
  How does this limit us?
  How do we compensate?

## Slide 15: Machine Code
The actual bits sent to the processor
The bits coming out of Instruction Memory

## Slide 16: Encoding Limitations
Designing an Encoding Scheme is a Game
  Best use of limited space?
  Favor some options over others
Take Available Space and divide into “Fields”
  Encoding within an Encoding (MOAR BOXES)
  Fixed width per field
  How many fields does IEEE-754 use?
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent

## Slide 17: Types of Fields
Enumerations
  No mathematical meaning, just enumerate options
Signed / Unsigned
  We know these well
Biased
  Mathematically offset by a constant

## Slide 18: Revisiting ARM’s Immediates
In Thumb state in ARMv6T2 and later the 32-bit MOV instruction can load:
  any 8-bit immediate value, giving a range of 0x0-0xFF (0-255)
  any 8-bit immediate value, shifted left by any number
  any 8-bit pattern duplicated in all four bytes of a register
  any 8-bit pattern duplicated in bytes 0 and 2, with bytes 1 and 3 set to 0
  any 8-bit pattern duplicated in bytes 1 and 3, with bytes 0 and 2 set to 0.
These values are also available as immediate operands in many data processing operations, without being loaded in a separate instruction.
Create an Encoding Scheme to generate these Immediates
Copyright © 2010-2011 ARM. http://infocenter.arm.com/help/topic/com.arm.doc.dui0473c/DUI0473C_using_the_arm_assembler.pdf
Notes: 8 bits for the pattern
5 bits for rotate
Top few values are open!

## Slide 19: Create Your Own Instruction Encodings
Create an Encoding Spec that covers:
  ALU Operations with 2 register operands
  ALU Operations with immediate for one operand
  Load from Data Memory, Store to Data Memory
  Jump (What type?)
  Branch
Consider splitting your definition in to ‘types’
Design an Instruction Decoder for it
  Probably a LUT (plus other stuff?)

## Slide 20: Our Single Cycle CPU
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Instruction
Fetch
Unit
Rs
Rt
Rs
Rt
Rd
Imm16
imm16
Instructions[31:0]
[25:21]
[20:16]
[15:11]
[15:0]
Branch
Jump
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg
Zero

## Slide 21: Complete Fetch Unit
SignExtnd
PC
Addr[31:2]
Addr[1:0]
Instruction
Memory
Concatenate
Adder
Instr[31:0]
Jump
“00”
PC[31:28]
Target Instr[25:0]
imm16
“1”
Zero
Branch
Cin
“0”

## Slide 22: MIPS Code Encoding Formats
All instructions encoded in 32 bits
Register (R-type) instructions
Immediate (I-type) instructions
Jump (J-type) instructions
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
RD
SHAMT
FUNCT
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address
(OP = 0,16-20)
(OP = any but 0,2,3,16-20)
(OP = 2,3)

## Slide 23: J-Type
Used for Unconditional Jumps
Simplest MIPS encoding
How do we encode “j 100”?
2: j (jump)
3: jal (jump and link)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address

## Slide 24: J-Type
Weirdness in the Address Field
Bottom 2 bits are always ‘00’, so drop’em
  Shift everything over by 2
That’s only 28 effective bits…
  Where are the other 4?
  How does this limit us?
  How do we compensate?

## Slide 25: I-Type
Used for operations with immediate (constant) operand
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
Op1,
L/S addr
Op2, Dest, L/S targ

## Slide 26: I-Type
Used for ops with an immediate operand
One Op Field (Enumeration)
Two register address fields
One Signed/Unsigned field
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 27: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 28: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
addi
$t1
$t0
100
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
beq
$a1
$a0
-11
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
lw
$t0
$t3
12
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 29: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
8
9
8
100
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
4
5
4
-11
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0x23
8
11
12
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 30: R-Type
Used for 3 register ALU operations
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
RD
SHAMT
FUNCT
00: sll
02: srl
03: sra
04: sllv
06: srlv
07: srav
08: jr
24: mult
26: div
32: add
33: addu
34: sub
35: subu
36: and
37: or
38: xor
39: nor
42: slt
00
(10-13 for FP)
Shift amount
(0 for non-shift)
add $8, $9, $10 # $8 = $9+$10
sll $8, $9, 6 # $8 = $9<<6
sllv $8, $9, $10 # $8 = $9<<$10
Op2
Op1
Dest
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
00
9
10
8
0
32
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
00
X
9
8
6
00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
00
10
9
8
0
04

## Slide 31: Control Signals
Func | 100000 | 100010 | N/A | N/A | N/A | N/A
Op | 000000 | 000000 | 100011 | 101011 | 000100 | 000010
 | add | sub | lw | sw | beq | j
RegDst |  |  |  |  |  | 
ALUSrc |  |  |  |  |  | 
MemToReg |  |  |  |  |  | 
RegWr |  |  |  |  |  | 
MemWr |  |  |  |  |  | 
Branch |  |  |  |  |  | 
Jump |  |  |  |  |  | 
ALUCntrl | Add | Sub | Add | Add | Sub | X