## Slide 1: b0011 Fabric
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowlegements
ARM Holdings: M3 Cortex Instruction Set
Addison Wesley Longman: Figures
Wikipedia: Figures
Asic World

## Slide 3: Today
Review from Thursday
Decoders , Muxes, LUTs
PALs, CPLDs and FPGAs
Preparation for your first Lab
Letter Writers: Tenzin Choetso, Deniz Celik

## Slide 4: Component Re-Use
You were “given” the D Flip Flop
  Assume it does what I told you it does
How do you formally re-use a component?
  Step-By-Step with _separate_ truth tables

## Slide 5: Example: JK Flip Flop
3 Inputs: Clock, J, K
2 Outputs: Q, ~Q
Clock | J | K | Q Next | Note
 | 0 | 0 | Q | Hold
 | 0 | 1 | 0 | Reset
 | 1 | 0 | 1 | Set
 | 1 | 1 | ~Q | Toggle
Clock | J | K | Q Next | Note
 | 0 | 0 | Q | Hold
 | 0 | 1 | 0 | Reset
 | 1 | 0 | 1 | Set
 | 1 | 1 | ~Q | Toggle
http://en.wikipedia.org/wiki/Flip-flop_(electronics)#JK_flip-flop

## Slide 6: Construct with a D Flip Flop
What logic can we add to a DFF to make a JKFF?
Compare Truth Tables
J
K
D Q
??

## Slide 7
Clock | J | K | Q Next
 | 0 | 0 | Q
 | 0 | 1 | 0
 | 1 | 0 | 1
 | 1 | 1 | ~Q
Clock | J | K | Q Next
 | 0 | 0 | Q
 | 0 | 1 | 0
 | 1 | 0 | 1
 | 1 | 1 | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q

## Slide 8: What goes into D to get desired Qn?
Clock | J | K | Q Next | D
 | 0 | 0 | Q | 
 | 0 | 1 | 0 | 
 | 1 | 0 | 1 | 
 | 1 | 1 | ~Q | 
Clock | J | K | Q Next | D
 | 0 | 0 | Q | 
 | 0 | 1 | 0 | 
 | 1 | 0 | 1 | 
 | 1 | 1 | ~Q | 
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q

## Slide 9: What goes into D to get desired Qn?
Clock | J | K | Q Next | D
 | 0 | 0 | Q | 
 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 
 | 1 | 1 | ~Q | 
Clock | J | K | Q Next | D
 | 0 | 0 | Q | 
 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 
 | 1 | 1 | ~Q | 
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q

## Slide 10: What goes into D to get desired Qn?
Clock | J | K | Q Next | D
 | 0 | 0 | Q | 
 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | ~Q | 
Clock | J | K | Q Next | D
 | 0 | 0 | Q | 
 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | ~Q | 
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q

## Slide 11: What goes into D to get desired Qn?
Clock | J | K | Q Next | D
 | 0 | 0 | Q | Q
 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | ~Q | ~Q
Clock | J | K | Q Next | D
 | 0 | 0 | Q | Q
 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | ~Q | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q
Clock | D | Q Next
 | 0 | 0
 | 1 | 1
 | Q | Q
 | ~Q | ~Q

## Slide 12: Construct Logic from Truth Table
Clock | J | K | Q Next | D | Phrase
 | 0 | 0 | Q | Q | (~J~K)Q
 | 0 | 1 | 0 | 0 | (~JK)0
 | 1 | 0 | 1 | 1 | (J~K)1
 | 1 | 1 | ~Q | ~Q | (JK)~Q
Clock | J | K | Q Next | D | Phrase
 | 0 | 0 | Q | Q | (~J~K)Q
 | 0 | 1 | 0 | 0 | (~JK)0
 | 1 | 0 | 1 | 1 | (J~K)1
 | 1 | 1 | ~Q | ~Q | (JK)~Q
Simplify with Boolean Logic

## Slide 13: Simplify with Boolean Logic
Split 1 into Q+~Q, Rearrange
Group and Reduce
Final Result

## Slide 14: Karnaugh Map
 | Q | ~Q
JK | 0 | 1
~JK | 0 | 0
~J~K | 1 | 0
J~K | 1 | 1
Clock | J | K | Phrase
 | 0 | 0 | (~J~K)Q
 | 0 | 1 | (~JK)0
 | 1 | 0 | (J~K)1
 | 1 | 1 | (JK)~Q
Clock | J | K | Phrase
 | 0 | 0 | (~J~K)Q
 | 0 | 1 | (~JK)0
 | 1 | 0 | (J~K)1
 | 1 | 1 | (JK)~Q

## Slide 15: Karnaugh Simplification
Is the RED box needed?
  Why? Why Not?
Resulting Equation:
  ~KQ+J~Q+J~K
 | Q | ~Q
JK | 0 | 1
~JK | 0 | 0
~J~K | 1 | 0
J~K | 1 | 1
Notes: PPT makes it hard to make truncated boxes 

## Slide 16: Final Result

## Slide 17: More Practice
If you are interested:
  Start with a JK Flip Flop, create a D Flip Flop
    Inception!
  Formally repeat last class’s examples
    SR Latch is more interesting
  Post practice problems on the Wiki later this week

## Slide 18: Muxes, AKA Multiplexor
Select or switch between inputs
Has one output, two types of inputs
  ‘Input’
  ‘Select’
#‘Select’ >= log2(# ‘Input’)
  8 inputs needs 3 select (address) bits
Notes: Figure Credit: Wikipedia

## Slide 19: (Binary) Decoder
Also called a ‘demux’
  Because it is the exact opposite.
Only one output is active at once
Usually has 2^inputs number of outputs
Sometimes has an enable input
  All Low or All Hi-Z
Notes: Figure Credit: Wikipedia

## Slide 20: Designing from Documentation
Clone the following parts from basic gates:
  DigiKey Part No 568-4448-2-ND
  568-8857-1-ND
  MC74HC164ADR2GOSTR-ND
    Hint: Use D-Flip-Flops as a black box
Do your solutions match theirs?
  Does it matter?
Notes: Picked datasheets with the “answers” in them on purpose. Good for practice and verification.
1x 3:8
2x 4:1
Shift Register – Uses Master Slave DFF!

## Slide 21: Shift Register
Chain of Flip Flops form a “Bucket Brigade”
On Clock, data proceeds one step down chain
http://en.wikipedia.org/wiki/Shift_register

## Slide 22: Programmable Logic
1969: XC157
  Mask Programmed, 12 gates 30 pins
1978: Programmable Logic Arrays
  Field Programmed by burning fuses
  Sum of Products
  Equivalent to “Dozens” of gates
1985: Generic Array Logic
  Field Reprogammable
Notes: Mask Programmed – done at the factory
Field Programmed – done

## Slide 23: Programmable Logic
Complex Programmable Logic Device:
  1000s to 10ks of Gates equivalent
  Non-volatile (typically)
  Sum of Products (typically)

## Slide 24: Field Programmable Gate Array
1985: Xilinx releases the XC2064
  Equivalent to 1000 gates
Typical Features:
  Volatile (Reprogram every time power is applied)
  Sea of Gates (Look Up Tables + Routing)
  Programmable Logic Blocks
  “Hard” Features – RAM, Multipliers, CPUs

## Slide 25: Xilinx Zynq 7000
Up to 6.6 Million Gates Equivalent
  277,400 Look Up Tables
  554,800 Flip Flops
  >2 Trillion Multiply Accumulates per second
Dual Core 1GHz ARM Cortex A9
  2.5 DMIPS/MHz
  Equivalent to 5 billion instructions per second (ish)
$5,401.26 (2013) $3,776.67 (2014)

## Slide 26: Look Up Tables
A form of Read Only Memory
Defined by Width and Depth
  Width = How many bits per word
  Depth = How many words available
Constructed as Muxes with constant inputs
  Use Select to look up the table entry

## Slide 27: Width
The width of a bus is how many bits are in that signal.
  A wire is a bus with width = 1

## Slide 28: Look Up Table as a Truth Table
A0 | A1 | A2 | Out0 | Out1 | Out2 | Out3
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
Stored Information
Depth
Address
Inputs
Width

## Slide 29: Fabric Design
FPGA ‘Fabric’ is a sea of reconfigurable logic blocks embedded in reconfigurable routing logic.
The reconfigurable logic used to be mostly look up tables with configurable constants.
Now it is LUTs + other stuff (“hard” elements)

## Slide 30: Fabric Design Example
Making an Inverter with a LUT
A | Out
0 | 1
1 | 0
Depth
Address
Inputs
Width

## Slide 31: Fabric Design Example
Making an Inverter with a LUT
A | Out
0 | 1
1 | 0

## Slide 32: Fabric Design
Design a small piece of an FPGA using:
  Decoders
  Muxes
  Basic Gates
  Programmable Bits (Ignore Construction for now)
Use your FPGA cell to create both of these:
  AB+AC+BC
  A^B^C
    ^ = XOR
Start by figuring out your requirements:
  Width? Depth?

## Slide 33: HW2
Assigned Today, due next Monday night
Create and Test Mux, Demux, Full Adder
We’ll cover Full Adder Thursday
Test Benches:
  Simplest – Enumerate entire Truth Table
  Harder – Explain how less is ok. Be very careful

## Slide 34: MP0
Assigned Thursday, Due the 29th
Install Party Thursday Night
Work in groups 2-3
Implement and Test 4 bit Adder on FPGA
  Will cover Thursday
Limited number of FPGAs

## Slide 35: Lab Preparation
Select 1 or 2 partners
Read through MP0.pdf
  Questions?
Begin paper&pencil sketching of modules
You have the rest of class to begin work
  Start Installing ModelSim Student Edition

## Slide 36: Intro to Verilog
Verilog is a Hardware Description Language
  Describes a digital logic circuit
  Syntax is like C
  Writing in verilog is not at all like writing in C
Synthesized to create:
  FPGA bitstreams
  ASICs