## Slide 2: b0000 Zero Day
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 3: Agenda
General Awkwardness
Basic Orientation Information
Course Objectives & Details
VDub‘s guide to getting an A in CompArch
Boolean Logic (?)

## Slide 4: Hi, I’m Eric
VanWyk, Class of ’07

## Slide 5: Awkwardness

## Slide 6: vanweric@gmail.com
Email and IM

## Slide 7: MH 253
Rarely… IM/Email me first.

## Slide 8: Monday & Thursday 0900-1040 1050-1230

## Slide 9: http://wikis.olin.edu/ca/ ca@lists.olin.edu
Feel free to use for discussion!

## Slide 10: Course Objectives

## Slide 11: Learn Digital Logic

## Slide 12: Learn Digital Math

## Slide 13: Build a Processor

## Slide 14: Write Programs for it
In assembly

## Slide 15: Build complex digital systems
In Verilog

## Slide 16: Course Details

## Slide 17: One Midterm
(I am so excited)

## Slide 18: One Final
(You get to write this one)

## Slide 19: Several Homeworks
Done individually.
Annotate collaboration per problem.

## Slide 20: Several Labs
Done in groups of 2 or 3

## Slide 21: One Awesome Project
Done in groups of ???

## Slide 22: Late Policy:
-10% for first 24 hours
-20% for second (30% total)
-30% for third (60% total)
After 72 hours, no credit.

## Slide 23: Unlate Policy
Talk to me first
Commit to a new due date
Email this new due date to comparch13@gmail.com
Reminder note in your submission email.

## Slide 24: Attendance Policy:
At your own risk.

## Slide 25: How To Get an A in Comp Arch
Manage your time wisely
Break big problems in to better chunks
  Black Boxes!
Learn enough C to know what a pointer is
Pick a fun AND MANAGEABLE final project
Give me constant feedback

## Slide 26: How to Seppuku CompArch

## Slide 27: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)

## Slide 28: Digital Logic

## Slide 29: Digital vs. Analog
Analog:
values vary over a range
continuously
Digital:
only assumes discrete values
Binary:
only assumes two values

## Slide 30: Example: Car Electronics
Door ajar light (driver door, passenger door):
High-beam indicator (lights, high beam selected):
Notes: Door Ajar – OR gate – if either are open, indicate the light
High-beam indicator – AND gate – only light if both are active

## Slide 31: Example: Car Electronics (cont.)
Seat Belt Light (driver belt in):
Seat Belt Light (driver belt in, passenger belt in, passenger present):
Notes: Seat Belt Light – Inverter – bother the user if the belt isn’t engaged

## Slide 32: Basic Logic Gates

## Slide 33: Basic Logic Gates
AND
XOR
(exclusive or)
NOR
OR
NAND
XNOR
NOT

## Slide 34: Boolean Equations
AND: AB A&B
OR: A+B
NOT: A̅ ~A

## Slide 35: Basic Boolean Identities:
X + 0 = X * 1 =
X + 1 = X * 0 =
X + X = X * X =
X + X̅ = X * X̅ =
X̅ =
Notes: X X
1 0
X X
1 0
X

## Slide 36: Basic Laws
Commutative Law:
X + Y = Y + X XY = YX
Associative Law:
X+(Y+Z) = (X+Y)+Z X(YZ)=(XY)Z
Distributive Law:
X(Y+Z) = XY + XZ X+YZ = (X+Y)(X+Z)

## Slide 37: Advanced Laws
Notes: X
X
X+Y
X
X
XY XY

## Slide 38: Homework for Monday
Answer these question:
  Why are you taking this class?
  What is your favorite processor? Why?
  Name at least 3 things you want to learn in this class: Be specific!
  What do you want to do with what you learn here after graduation? Prognosticate!
Email them to CompArch13@gmail.com
  Subject [HW0] Your Name

## Slide 39: Homework for Monday
Find examples of simple boolean logic
  2-4 inputs
  Well defined behavior
  Interesting to you
This portion is NOT collected
  It will be used in class

## Slide 40: Truth Tables
Algebra: variables, values, operations
In Boolean algebra, the values are the symbols 0 and 1
If a logic statement is false, it has value 0
If a logic statement is true, it has value 1
Operations: AND, OR, NOT

## Slide 41: Karnaugh Map Review
Moving one square changes only one input.
Cover all 1s with boxes.
Boxes must be power of 2 sized.
Create Sum of Products
Boxes can “wrap around” the edges of the map.
  Toroidal mapping

## Slide 42: Karnaugh Map Review
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅

## Slide 43: Karnaugh Map Review
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅
Which “advanced” law allows us to combine boxes?

## Slide 44: Why Karnaugh?
“Mechanical” method guaranteed to get something that works.
Result is only two layers deep – Fast!

## Slide 45: Why not Karnaugh?
Confusing visually for more than 4 variables
  But it still works if you squint
Optimizes for speed, not space.

## Slide 46: To the Boards!
F = (X+Y̅+XY̅)(XY+X̅Z+YZ)
Evaluate Truth Table
  Pro Tip: Build in Layers
Simplify with Karnaugh
Simplify with Boolean Law

## Slide 47: DeMorgan’s Law
(X + Y) = X * Y
(X * Y) = X + Y
Example:
Z = A B C + A B C + A B C + A B C
Z = (A + B + C) * (A + B + C) * (A + B + C) * (A + B + C)
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y

## Slide 48: DeMorgan’s Law example

## Slide 49: The Universal Gates
Karnaugh maps can frame any boolean equation in sum of products (OR of ANDs)
DeMorgan can frame any AND/OR in NAND/NORs
NAND and NOR can represent any combinatorial boolean equation.

## Slide 50: Boolean Equations to Circuit Diagrams