## Slide 1: b1100 Call Me, Maybe
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Today
Testing Strategies
Calling Simple/“Leaf” Functions
The Stack
Calling Generic Functions
Calling Conventions

## Slide 3: My Testing Strategy
List the types of problems I face
List the assumptions I make
List the cases to catch these problems
Compress list of cases using assumptions

## Slide 4: Problems
Stuck Bits / Stuck Registers
Ghosted Bits / Ghosted Registers
Broken Muxes
Stuck Write Enable
Weak Bits
Flip Flop Blow-Through

## Slide 5: Assumptions
Bits fade quickly or never at all
  Don’t have to wait 10 minutes between tests
Muxes are time invariant
  Only the flip flops care about time
  I don’t mean propagation delay

## Slide 6: Cases
I will use walking 1s and walking 0s
  31 0s and a walking one
  31 1s and a walking zero
This is 31 * 32 * 2 = 1984 test cases
This tests Stuck Bits / Registers

## Slide 7: Port Usage
Write Port
  Writes Test Case N
Read Port 1
  Checking Test Case N-31
Read Port 2
  Checks for blow through
  Is reading the register being written to

## Slide 8: Port Usage Benefits?
The Port usage strategy tests:
  Flip Flop Blow Through (Read Port 2)
  Broken Muxes (Both are in use, differently)
  Weak Bits (Wait a long time to read)
  Ghosting (All others are written in between)
What critical assumptions am I making?

## Slide 9: Orthoganality
My individual test cases are dissimilar!
  Within a certain window
Think of sequences that fail this assumption
  Write pattern A to all registers, then pattern B…
  Write all patterns to register 1, then register 2
Create an orthogonal window of testing

## Slide 10: Orthogonal Windows?
How wide in time is my test window?
  How far back in time can I be affected?
All patterns in this window must be dissimilar
  Orthogonal
Diagonal Stripe / Barber Pole?
Discrete Math can compress patterns further

## Slide 11: What is a function?
A procedure is a stored subroutine that performs a specific task based on the parameters it is provided.
  <Pattersen & Hennessy>
a = f(x,y,z); // You have seen this before
A spy on a secret mission
  Seriously, the textbook we used to use is hilarious.

## Slide 12: What is a function?
A block of code formatted in a way that allows it to be called by other code, and then returns execution to the caller
How is this similar to / different from one of our “GOTO” targets?

## Slide 13: The Life of a Called Function
The caller stores parameters “somewhere”
Control (Execution) is passed to the callee
The callee does some stuff
The callee stores the results “somewhere”
Control is passed back to the caller

## Slide 14: Calling Conventions
A Calling Convention standardizes where those “somewheres” are.
  Registers? Data Memory?
  Return values?
  How do we return control back to the caller?
It is just another type of contract
  The great thing about standards is that there are so many to choose from.

## Slide 15: Execution Flow
Lets work through a simple example
void main()
{
// do some stuff
MyFunction();
// do other stuff
}

## Slide 16: Execution Flow
Idea 1:
Jump to subroutine
Jump back when done
#Caller (main)
#do stuff j MyFunction
returnToMain:
#dootherstuff
#callee
MyFunction:
#code code code j returnToMain

## Slide 17: Execution Flow
Idea 1:
Jump to subroutine
Jump back when done
What if I want to use the function again elsewhere?
#Caller (main)
#do stuff j MyFunction
returnToMain:
#dootherstuff
#callee
MyFunction:
#code code code j returnToMain

## Slide 18: Execution Flow
Idea 2:
Store return address
Jump to subroutine
Jump back when done
#Caller (main)
#do stuff
ReturnAddr = PC+??? j MyFunction
returnToMain:
#dootherstuff
#callee
MyFunction:
#code code code jr ReturnAddr

## Slide 19: Execution Flow
In MIPS, this is called Jump And Link (jal)
jal stores the PC+4 to $31 and then jumps to the target address
$31 is also known as $ra
  Return Address
Jump Register (jr) to get back
#Caller (main)
#do stuff jal MyFunction
#dootherstuff
#callee
MyFunction:
#code code code jr $ra

## Slide 20: Execution Flow
Storing the Return Address in $ra is great!
  but only for Leaf Functions
What if a function calls another function?
  Put it in Data Memory!
  Every function has a dedicated space to shove $ra

## Slide 21: Execution Flow
Storing the Return Address in $ra is great!
  but only for Leaf Functions
What if a function calls another function?
  Put it in Data Memory!
  Every function has a dedicated space to shove $ra
What if… A FUNCTION CALLS ITSELF?!?!
  OMG Inception

## Slide 22: Stack Attack
Dedicating memory per function is limiting
  Wastes space when it isn’t active
  Can’t recurse
Instead, allocate data memory as needed
We use “The Call Stack”
  Last In, First Out
  Push stuff onto the head of the stack
  Pop stuff back off of it

## Slide 23: The Call Stack
Is a Stack of “Frames”
Each active function instantiation has a Frame
Frames hold the instance memory
  Like the return address

## Slide 24: Mechanics of the Call Stack
Architecture Decisions:
  Where is the Stack?
  How do we address it / point to it?
    Linked List? Raw Pointer?
Calling Convention Decisions:
  What stuff is put on it?
  In what order? (Frame Definition)
  By whom? (Caller? Callee?)

## Slide 25: Mechanics of the Stack
Ascending/Descending
  Ascending stacks start at address 0 and grow up
  Descending stacks start at the other end and grow down
Full / Empty
  Empty stack pointers point to the next unallocated address
  Full stack pointers point to the top item in the stack
MIPs uses a “full descending” stack
  With $29 ($sp) as the stack pointer
ARM supports all 4, usually uses full descending
  Procedure Call Standard for the ARM Architecture (AAPCS)

## Slide 26: Why Descending?
There are two dynamic memory spaces
The “Heap” handles memory dynamically allocated at run time
  malloc /free
  new / delete
Traditionally:
  Heap ascends
  Stack descends
Giovanni Gracioli

## Slide 27: Full Descension Example
PUSH $t0 onto the stack
addi $sp, $sp, -4 #allocate 1 word
sw $t0, 0($sp) #push $t0
What does the stack look like after this push?
Does order of operations matter here?
  Remember this example for next week

## Slide 28: Full Descension Example
Pop $t3, $t4 from the stack
lw $t3, 4($sp) #pop $t3
lw $t4, 0($sp) #pop $t4
addi $sp, $sp, 8 #delete 2 words
What does the stack look like after this push?
Two pops, one add

## Slide 29: Lets Do This
Write the “factorial” function two ways:
  As a leaf function
    Use algebra or a loop
  As a recursive function
    F(n) = (n<1) ? 1 : n * F(n-1)
You will have to invent parts of your own calling convention here. Take notes on what you invented.
  Where do you store parameters? Return Values? Return Addresses?
This will be easier if you write in human first
  Drawing your stacks helps too!
Bonus: Fibonacci, Greatest Common Divisor, Array Binary Search

## Slide 30: Calling Convention
We have decisions to make for registers:
  Are they used as part of the call?
  Are they preserved across the call?
  Are they reserved for other uses?
… and about passing arguments around
  In registers?
  On the stack?
  In generic data memory?

## Slide 31: Midterm
The Light that goes Blink in the Dark

## Slide 32: MIPs Specifics
Uses $vN to store results
  V for Valuetta
Uses $aN to store first 4 arguments
  A is for Argument, that’s good enough for me
  Extra are pushed to the stack

## Slide 33: MIPs Specifics
$sN are Saved Temporaries
  The callee is responsible for saving these if used
  The caller can assume they are unchanged
$tN are Volatile Temporaries
  The callee can do whatever it wants with these
  The caller can’t rely on these across a call
Advantages/Disadvantages to these?

## Slide 34: Frame Pointer
$sp can move around during a procedure
  This makes frame contents shift around
    Relative to the stack pointer
  Makes debugging hard
A Frame Pointer stays put during a procedure
  Makes debugging easier!
  Makes compiling easier too, but I don’t care

## Slide 35: Frame Pointer
Isn’t strictly necessary
  But it makes debugging so much easier
Not all implementations use it
  GNU MIPS C Compiler does
  MIPS MIPS C compiler does not

## Slide 36: A MIPS calling convention’s frame
From WinCE 5.0
Arguments at top of previous frame
$ra
Saved nonvolatiles
Locals
http://msdn.microsoft.com/en-us/library/aa448710.aspx

## Slide 37: Vocab
Blowing the Stack / Stack Overflow / Stack Smashing
  Running out of stack space
  Writes over other data! (Heap)
  Possible security vulnerability
Unwind the Stack
  Popping “frames” off the stack
  Usually in the context of exception handling
Walking the Stack
  Looking at the Stack and figuring out where you are
  Usually in the context of Debugging
  Need to be able to “see” where the frames are

## Slide 38: Vocab
Misaligning or Unbalancing the stack
  Pushing or popping a different number of times
  Catastrophic Error!
Stack Dump
  Produced when program crashes
  Helps you understand where you were when stuff went wrong

## Slide 39: Stack Dump Example
Error Message:
Value cannot be null.
Parameter name: value
Exception:
ArgumentNullException
Suggestion:
Contact National Instruments to report this error
Stack Trace:
at System.BitConverter.ToInt32(Byte[] value, Int32 startIndex)
at NationalInstruments.LabVIEW.VI.VirtualMachine.Target.ExecutionHighlighting.ProcessUpdate(Byte[] buffer)
at NationalInstruments.X3.Model.DeviceModel.OnExHighlightReadCompletedEventHandler(Object sender, ReadCompletedEventArgs e)
at NationalInstruments.X3.Model.DeviceModel.<>c__DisplayClass37.<ReadTargetMemory>b__36(Object theSender, RequestCompletedEventArgs theE)

## Slide 40: x86 Calling Conventions
Full of “gotchas”
  These are usually why calling other binaries fail
__cdecl (See-Deckle)
  Supports all C functionality
__stdcall (Standard Call) (ha)
  Win32 API uses this
__fastcall
  Uses registers more aggressively to go faster
Thiscall
  Used in C++ by member functions
The following slides based from Nemanja Trifunovic’s article “Calling Conventions Demystified”

## Slide 41: See Deckle
Expand arguments to 32 bits
All arguments are on stack, right to left
Decorated with an underscore
Caller does stack cleanup
  This allows for a variable number of arguments
    printf(const char * format, …);
  Generates bigger executables
    Each call site performs cleanup
Nemanja Trifunovic

## Slide 42: See Deckle
; Calling Add(7,19)
push 19
push 7
call _add
add esp, 8 ; clean up stack
;result is in eax
; body
; // function prolog
push ebp
mov ebp,esp
sub esp,0C0h
push ebx
push esi
push edi
lea edi,[ebp-0C0h]
mov ecx,30h
mov eax,0CCCCCCCCh
rep stos dword ptr [edi]
; // return a + b;
mov eax,dword ptr [a]
add eax,dword ptr [b]
; // function epilog
pop edi
pop esi
pop ebx
mov esp,ebp
pop ebp
ret
int __cdecl add(int a, int b);

## Slide 43: “Standard” Call
Expand Arguments to 32 bits
All arguments are on stack, right to left
Decorated with:
  Prepended underscore
  Appended @ and number of bytes stack needs
Callee does stack cleanup
  Smaller Executables
  Fixed number of arguments

## Slide 44: Standard Call
; Calling Add(7,19)
push 19
push 7
call _add@8
add esp, 8 ; clean up stack
;result is in eax
; body (nearly identical)
; // function prolog
push ebp
mov ebp,esp
sub esp,0C0h
push ebx
push esi
push edi
lea edi,[ebp-0C0h]
mov ecx,30h
mov eax,0CCCCCCCCh
rep stos dword ptr [edi]
; // return a + b;
mov eax,dword ptr [a]
add eax,dword ptr [b]
; // function epilog
pop edi
pop esi
pop ebx
mov esp,ebp
pop ebp
ret
int __stdcall add(int a, int b);

## Slide 45: Fast Call
Attempts to go fast by using registers for the first two arguments
Function decorated by:
  Prepended @
  Appended @ + number of bytes required by arguments

## Slide 46: Fast Call
; Calling Add(7,19)
mov edx, 19
mov ecx, 7
call @add@8
;result is in eax
; // function prolog push ebp
mov ebp,esp
sub esp,0D8h
push ebx
push esi
push edi
push ecx
lea edi,[ebp-0D8h]
mov ecx,36h
mov eax,0CCCCCCCCh
rep stos dword ptr [edi]
pop ecx
mov dword ptr [ebp-14h],edx
mov dword ptr [ebp-8],ecx
; // return a + b;
mov eax,dword ptr [a]
add eax,dword ptr [b]
;// function epilog pop edi pop esi pop ebx mov esp,ebp pop ebp ret
int __fastcall add(int a, int b);

## Slide 47: Why do I care?
You rarely need to know this level of detail
Helpful for understanding interop
Helpful for debugging
Understand the limitations and COSTS of functions
  Inlining is nice

## Slide 48: Further Reading
Textbook: 2.8
We only covered ONE stack per machine
  When would you need more?
  How would you implement it?

## Slide 49: With Remaining Time
More Example Programs
  Fibonacci, Greatest Common Divisor, Array Binary Search
Try creating a “Stack Poisoning Attack”
  Write code that poison’s the stack’s version of $sp
  Get it to jump elsewhere when it returns
  Bonus points for making it look like an accident