## Slide 1: b10010 Pipelining Hazards
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Today
Review Pipelined CPUs
Discuss Hazards of Pipelining

## Slide 3: Review
Pipelining allows multiple instructions to be “in flight” in the data path at the same time
Temporal Parallelism breaks instructions in to small tasks that run in multiple stages
Potential Throughput Speedup = # Stages
Hazards reduce these benefits
  Can always be “solved” with a No-Op (but that sucks)

## Slide 4: In Flight Entertainment
What does “in flight” mean in this context?
What state does each instruction need?
Where is this state stored?

## Slide 5: In Flight Entertainment
What does “in flight” mean in this context?
What state does each instruction need?
Where is this state stored?
Registers
Registers
Registers
Registers
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback

## Slide 6: In Flight Entertainment
One instruction is in stage at a time
  No “smearing” across stages
Entire instruction state is in the stage’s registers
Registers
Registers
Registers
Registers
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback

## Slide 7: Pipelined CPU w/ Controls
Montek Singh, COMPS541

## Slide 8: The Life and Death of State
Control Signals are “Born” in the Decoder
  Propagated until they are needed
Data Signals are “Born” later
  e.g. Reg File Reads, ALU Result
Signals “Die” when they are no longer needed
  Shed no tears for me. My glory lives forever.

## Slide 9: State Check
Annotate control signals on the 5 stage CPU
  Spawn Point, Usage(s), Cull Point
  Width
 | Width | IF/ID | ID/EX | EX/MEM | MEM/WB
Read Reg Addrs | 5+5 |  |  |  | 
Read Reg Data A | 32 |  |  |  | 
Read Reg Data B | 32 |  |  |  | 
Write Reg Addr | 5 |  |  |  | 
Write Reg Data | 32 |  |  |  | 
ALU Cntl | 5 |  |  |  | 
ALU Src | 1 |  |  |  | 
RegWrite | 1 |  |  |  | 
MemWrite | 1 |  |  |  | 
ALU Result | 32 |  |  |  | 
ALU Zero | 1 |  |  |  | 

## Slide 10: Jumping and Branching
When does Jump update PC?
Is this ok?
Can we do better?
Notes: Some designs were updating “late”

## Slide 11: Jumping and Branching
When does Jump update PC?
  In Instruction Decode
Is this ok?
  Derp
Can we do better?
  Push to Instruction Fetch?
A Control Hazard is when the wrong instruction gets executed because IFetch Fail

## Slide 12: Jumping and Branching
How about Branch?
Register
Register
Register
Register
PC
Data
Memory
Instr.
Memory
Register
File
Register
File

## Slide 13: Jumping and Branching
How about Branch?
Register
Register
Register
Register
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
+
test
Add hardware -> Update PC after RegFetch/Decode

## Slide 14: Branch is still a Hazard
PC is updated at the end of Reg/Dec
What does this do to this sample program?
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
beq
Ifetch
Reg/Dec
Exec
Mem
Wr
load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec

## Slide 15: Branch is still a Hazard
PC is updated at the end of Reg/Dec
What does this do to this sample program?
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
beq
Ifetch
Reg/Dec
Exec
Mem
Wr
load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec

## Slide 16: What to do?
LW is sneaking in past the branch!!
How can we solve this problem?
This is exactly why Comp Arch is so damn cool

## Slide 17: Control Hazard Solution: Go Faster
Push the branch hardware in to the first cycle
IF cycle takes much longer now
Poor Balancing
Slows down all the other instructions!

## Slide 18: Control Hazard Solution: Stall
Delay Fetch/Decoding the next instruction
What is the impact on performance?
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
beq
Ifetch
Reg/Dec
Exec
Mem
Wr
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec
Bubble
Bubble
Bubble
Bubble
Stall

## Slide 19: Control Hazard Solution: Embrace It
Re-define not as a hazard, but as a feature!
Compiler moves an instruction in to the “Branch Delay Slot”
Very common in embedded / DSP processors
  Total control over instruction set / compiler / etc
Notes: Compilers can fill that spot ~60% of the time
The information computed is useful ~80% of the time
Wave hands here

## Slide 20: Control Hazard Solution: Guess&Check
Easier to beg forgiveness than ask permission
  Make an assumption, execute accordingly
  If it was wrong, abort the speculative instructions
I shall be telling this with a sigh Somewhere ages and ages hence: Two roads diverged in a wood, and I, I took the one less traveled by, And that has made all the difference.
- Robert Frost
Notes: Two roads diverged in a yellow wood, And sorry I could not travel both And be one traveler, long I stood And looked down one as far as I could To where it bent in the undergrowth; Then took the other, as just as fair, And having perhaps the better claim Because it was grassy and wanted wear, Though as for that the passing there Had worn them really about the same, And both that morning equally lay In leaves no step had trodden black. Oh, I marked the first for another day! Yet knowing how way leads on to way I doubted if I should ever come back. I shall be telling this with a sigh Somewhere ages and ages hence: Two roads diverged in a wood, and I, I took the one less traveled by, And that has made all the difference.
Mountain Interval, 1920

## Slide 21: Control Hazard: Guess&Check
How do we pick which way to go?
Invent a scheme, apply it to example code
  How many did you get right?
  Does the nature of the code matter?
  Does the nature of the inputs matter?
How would this be implemented in HW?

## Slide 22: Control Hazard: Guess&Check
int num_positive(int[] sensor_values){
for(i =0; i< length; i++)
if(sensor_values[i] >0)
num += 1;
return num;
}
Notes: Sum instead of count? In addition to counting?

## Slide 23: Solution: Branchless Conditionals
ARM supports conditional execution
Instructions optionally update status flags
Instructions execute only if flags match
CMP r0, #'A' ; if (c == 'A'
CMPNE r0, #'B' ; || c == 'B')
MOVEQ r1, #1 ; y = 1;

## Slide 24: Solution: Branchless Conditionals
ARM supports conditional execution
Instructions optionally update status flags
Instructions execute only if flags match
CMP r0, #'A' ; if (c == 'A'
CMPNE r0, #'B' ; || c == 'B')
MOVEQ r1, #1 ; y = 1;

## Slide 25: Control Hazard Summary
Branch Penalty is Architecture Dependant
  We reduced BEQ from 3 to 1 with extra hardware
Uncertainty is expensive
  Stalling costs time
  Predicting costs power and area

## Slide 26: Data Hazards
What happens with the following code?
  add $t0, $t1, $t2
  sub $t3, $t0, $t4
  and $t5, $t0, $t7
  or $t8, $t0, $s0
  xor $s1, $t0, $s2
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
add
Ifetch
Reg/Dec
Mem
sub
Ifetch
Reg/Dec
Exec
Wr
and
Ifetch
Reg/Dec
Mem
Wr
or
Ifetch
Reg/Dec
Mem
Wr
xor
Exec
Exec
Exec

## Slide 27: Data Hazards
What happens with the following code?
  add $t0, $t1, $t2
  sub $t3, $t0, $t4
  and $t5, $t0, $t7
  or $t8, $t0, $s0
  xor $s1, $t0, $s2
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
add
Ifetch
Reg/Dec
Mem
sub
Ifetch
Reg/Dec
Exec
Wr
and
Ifetch
Reg/Dec
Mem
Wr
or
Ifetch
Reg/Dec
Mem
Wr
xor
Exec
Exec
Exec
FAIL

## Slide 28: Data Hazards: Forwarding
Result isn’t committed until Writeback!
  … but is available after Execute
  … and really only needed in time for Execute
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
add
Ifetch
Reg/Dec
Mem
sub
Ifetch
Reg/Dec
Exec
Wr
and
Ifetch
Reg/Dec
Mem
Wr
or
Ifetch
Reg/Dec
Mem
Wr
xor
Exec
Exec
Exec

## Slide 29: Data Hazards: Forwarding
Result isn’t committed until Writeback!
  … but is available after Execute
  … and really only needed in time for Execute
Mem
Wr
Exec
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
add
Ifetch
Reg/Dec
Mem
sub
Ifetch
Reg/Dec
Exec
Wr
and
Ifetch
Reg/Dec
Mem
Wr
or
Ifetch
Reg/Dec
Mem
Wr
xor
Exec
Exec
Exec

## Slide 30: Data Hazards: Forwarding
Allows immediate use of a result
Requires decoder to track where things are
Try implementing forwarding in HW
  What new registers are needed?
  New Muxes?
  Control logic?
  Can you forward with LW?

## Slide 31: In Groups
Branch Prediction
Forwarding Hardware Design
Create a program to show a hazard
  Calculate performance with ‘vanilla’ MIPS pipeline
  Improve the pipeline
  Calculate performance with ‘better’ MIPS pipeline

## Slide 32: Feedback
Give answers anonymously before class is over
How many hours per week are you spending on Computer Architecture outside of class?
How many should you be spending?
What can I do to make these numbers match?
What can you do?

## Slide 33: MP2 Post Mortem
Please submit individual work plan post mortems to Comparch13@gmail.com by the end of the day.