## Slide 1: b0001 Boolean Logic
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)

## Slide 3: Today:
Review Survey from last class
Review of Basic Boolean Laws
Clarification of a Basic Law
Truth Tables and Karnaugh Maps

## Slide 4: Most Favoritest Processors
“whatever I have in my laptop”
  Second was “what?”
ARM
  M-Cortex!
Specific Intel part number
ATMega
Zilog Z80
AMD64
Intel 4004
PIC18f4520
Apple A6
Antikythera mechanism
All processors are evil and proprietary
Microsoft Word/Food Processor
Statistics Professor

## Slide 5: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What it means to love
What do I need to know, what can be ignored
How to Robots
Communications
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Time Management
Embedded Development
Why layout a processor by hand?
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 6: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What it means to love
What do I need to know, what can be ignored
How to Robots
Communications
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Time Management
Embedded Development
Why layout a processor by hand?
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 7: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What it means to love
What do I need to know, what can be ignored
How to Robots
Communications
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Time Management
Embedded Development
Why layout a processor by hand?
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 8: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What it means to love
What do I need to know, what can be ignored
How to Robots
Communications
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Time Management
Embedded Development
Why layout a processor by hand?
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 9: Review of Boolean Algebra
1930s: Shannon applies Boole’s algebra to circuits and logic gates
Method to improve representation of a given circuit or logic
  Execution speed
  Resources consumed
Basis of modern processors

## Slide 10: Boolean Laws So Far
X + 0 = X
X * 1 = X
X + 1 = 1
X * 0 = 0
X + X = X
X * X = X X + X̅ = 1
X * X̅ = 0
~~X = X
X+Y = Y+X
XY = YX
X+(Y+Z) = (X+Y)+Z
X(YZ) = (XY)Z
X(Y+Z) = XY + XZ
X+YZ = (X+Y)(X+Z)
X+XY = X
XY+XY̅ = X
X+X̅Y = X+Y
X(X+Y) = X
(X+Y)(X+Y̅) = X
X(X̅+Y) = XY
Notes: Derived in class last week

## Slide 11: Boolean Laws
1+1 = 1
… Sorry.

## Slide 12: Clarification of a Basic Law
X + X̅Y = ?
Use Distributive Law: X+YZ = (X+Y)(X+Z)
X + X̅Y = (X+X̅)(X+Y)
X + X̅Y = (X+X̅)(X+Y)
Notes: Treat ~X as an independent variable for the use of the distributive law

## Slide 13: Mechanical Forms
Truth Table
  Good for finding the results of equations
  Build up large equations in chunks
Karnaugh Map
  Good for finding new representations of equations
  Only really useable for up to 4 inputs at a time
    ((For Humans, synthesizers do many more))

## Slide 14: Truth Tables
Inputs in left columns
Outputs on the right
Notes in the middle
Enumerate all input combinations
  Count in Binary
Calculate each Row
Equations are equivalent if they have matching truth tables
Notes: My preference is to start with 0 0 0 and increment as though counting in binary.
Do truth table for basic law on white board X+YZ = (X+Y)(X+Z)
X y z (X+Y)

## Slide 15: Example: X+YZ = (X+Y)(X+Z)
X | Y | Z | YZ | X+Y | X+Z | (X+Y)(X+Z) | X+YZ
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 

## Slide 16: Example: X+YZ = (X+Y)(X+Z)
X | Y | Z | YZ | X+Y | X+Z | (X+Y)(X+Z) | X+YZ
0 | 0 | 0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 0 | 0 | 1 |  | 
0 | 1 | 0 | 0 | 1 | 0 |  | 
0 | 1 | 1 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | 1 | 1 |  | 
1 | 0 | 1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 | 1 | 1 |  | 
1 | 1 | 1 | 1 | 1 | 1 |  | 

## Slide 17: Example: X+YZ = (X+Y)(X+Z)
X | Y | Z | YZ | X+Y | X+Z | (X+Y)(X+Z) | X+YZ
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 18: Four Input Karnaugh Map Example
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅

## Slide 19: Karnaugh Map
Moving one square changes only one input.
Cover all 1s with boxes.
Boxes must be power of 2 sized.
Create Sum of Products
Boxes can “wrap around” the edges of the map.
  Toroidal mapping
Invented in ‘52 by Maurice Karnaugh
Notes: Note: Gray coded! This means only one transition for one movement.

## Slide 20: Four Input Karnaugh Map Example
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅
Which “advanced” law allows us to combine boxes?

## Slide 21: 4 Input Karnaugh Map (WhiteBoard)
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅

## Slide 22: Why Karnaugh?
“Mechanical” method guaranteed to get something that works.
Result is only two layers deep – Fast!

## Slide 23: Why not Karnaugh?
Confusing visually for more than 4 variables
  But it still works if you squint
Optimizes for speed, not space.

## Slide 24: To The Boards!
Prove equivalency:
F=(X+Y̅+XY̅)(XY+X̅Z+YZ)
Evaluate Truth Table
  Pro Tip: Build in Layers
Simplify with Karnaugh
Simplify again with Boolean Law
Draw with Gates
(X + Y) = X * Y
(X * Y) = X + Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y

## Slide 25: To The Boards!
If you have additional time, truth table and k-map:
  The examples you brought with you
  ‘Tricky’ Boolean Laws

## Slide 26: DeMorgan’s Law
(X + Y) = X * Y
(X * Y) = X + Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
The negation of a conjunction is the disjunction of the negations.
The negation of a disjunction is the conjunction of the negations.*
* Thanks, Wikipedia!

## Slide 27: DeMorgan’s Law
Provides a way to convert AND  OR
Flip ALL the things
  Invert all the inner terms
  Swap AND  OR
  Invert the entire boolean phrase
This works for a single gate with arbitarily many inputs

## Slide 28: The Universal Gates
Karnaugh maps can frame any boolean equation in sum of products (OR of ANDs)
DeMorgan can frame any AND/OR in NAND/NORs
NAND and NOR can represent any combinatorial boolean equation.
Notes: NAND or NOR can be used as an inverter by tying the inputs together

## Slide 29: DeMorgan’s Law example
Example:
Z = A B C + A B C + A B C + A B C
Z = (A + B + C) * (A + B + C) * (A + B + C) * (A + B + C)

## Slide 30: Boolean Equations to Circuit Diagrams