## Slide 1: b1010 Assembly
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowledgements
Derek Redfern
Alethea Butler

## Slide 3: Today
Review Encodings
Context of Assembly
Your First Assembly Programs

## Slide 4: Limited Encoding Example
Create a 16 / 24 bit encoding
Needs to be able to:
  Math
  Branch if Zero
  Jump
  Load
  Store
  Load Immediate
What to trim?

## Slide 5: My Choices
Drop all immediate compound instructions
  ADD w/ Immediate becomes 2 ops:
    Load Immediate
    Add w/ 2 Registers
Reduce to 16 registers
Combine Target and Source Register Address
  A=A+B instead of A=B+C

## Slide 6: Load Immediate
OP is 00
POS indicates where IMM is placed
  00  Bottom 12 bits
  01  Next 12 Bits
  10  Top 8 bits
  11  Bottom 12 bits, preserve other 20
Always placed in register 0
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0 0
IMM12
POS

## Slide 7: Math
OP is 01
RSD is target and first operand
RT is second operand
FUNCT enumerates specific op
  Add, Sub, And, Or, etc
  Up to 64 ops
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0 1
RSD
FUNCT
RT

## Slide 8: Branch and Jump
Same encoding as Math
RSD is test register
  If equal to zero, branch
RT stores the destination
FUNCT:
  Branch, Absolute
  Branch, Relative
  Jump, Absolute
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
1 0
RSD
FUNCT
RT

## Slide 9: Load and Store
OP is 11
RSD stores address of register with data memory address
RT stores address to be read from / written to
FUNCT
  Load, Store
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
1 1
RSD
FUNCT
RT

## Slide 10: How did I do?
ADD w/ Immediate is now 4 operations
  Load first 12 bits of immediate to Reg 0
  Load next 12
  Load final 8
  Add
Might need additional moves
  Where was data before?
  Where should it end up?

## Slide 11: How did I do?
Encoding is really “loose”
  Maybe I cut too many things?
OP could be 1 bit:
  Is this load immediate?
FUNCT has 64 options, plenty of space

## Slide 12: TL;DR;
Simpler Instructions, but more of them
What is important?
  Execution Speed
  Transistor count
  Memory size
  Package pin count

## Slide 13: Thumb (1) 16 bit Encoding

## Slide 14: What is Assembly?
Assembly is the lowest level language that humans routinely deal with
Simple, regular instructions
  building blocks of C & other languages
One-to-one mapping to machine language
  … Usually

## Slide 15: What is Assembly?
It is how we feed steps 1 & 2
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 16: Why Shouldn’t I learn Assembly?
Writing in Assembly is usually slower than writing in other languages
  Time to Market!
Assembly is not portable
  Specific to a processor (family)
Modern Compilers are pretty darn good

## Slide 17: Why Should I Learn Assembly?
Someone has to write those compilers…
Hand Optimized Assembly can be wicked fast
Reading Assembly >>> Writing Assembly
Good practice for designing VMs/protocols
Initializing an embedded system
  Setting up Memory, Transitioning execution…

## Slide 18: Why Should I Learn Assembly?
It will make you a better software architect
Optimize from the top down

## Slide 19: How should I learn Assembly?
Generically!
With a cheat sheet in hand
Do Not Memorize Specifics

## Slide 20: “C is Built On Assembly”
WRONG
C is built on Machine Code
Machine Code can be decompiled to Assembly
Assembly -> Machine Code -> Assembly loses relatively little information
Notes: The only information lost in Assembly -> Machine Code -> Assembly are the human-readable location labels and comments.

## Slide 21: MIPS Assembly Language
The basic instructions have four components:
  Operator name
  Destination
  1st operand
  2nd operand
add <dst>, <src1>, <src2> # <dst> = <src1> + <src2>
sub <dst>, <src1>, <src2> # <dst> = <src1> - <src2>
Simple format: easy to implement in hardware
More complex: A = B + C + D – E

## Slide 22: Register File Allocation
Register | Name | Function | Comment
$0 | $zero | Always 0 | No-op on write
$1 | $at | Reserved for assembler | Don’t use it!
$2-3 | $v0-v1 | Function return | 
$4-7 | $a0-a3 | Function call parameters | 
$8-15 | $t0-t7 | Volatile temporaries | Not saved on call
$16-23 | $s0-s7 | Temporaries (saved across calls) | Saved on call
$24-25 | $t8-t9 | Volatile temporaries | Not saved on call
$26-27 | $k0-k1 | Reserved kernel/OS | Don’t use them
$28 | $gp | Pointer to global data area | 
$29 | $sp | Stack pointer | 
$30 | $fp | Frame pointer | 
$31 | $ra | Function return address | 

## Slide 23: Register File Allocation
STOP MEMORIZING THIS
Register | Name | Function | Comment
$0 | $zero | Always 0 | No-op on write
$1 | $at | Reserved for assembler | Don’t use it!
$2-3 | $v0-v1 | Function return | 
$4-7 | $a0-a3 | Function call parameters | 
$8-15 | $t0-t7 | Volatile temporaries | Not saved on call
$16-23 | $s0-s7 | Temporaries (saved across calls) | Saved on call
$24-25 | $t8-t9 | Volatile temporaries | Not saved on call
$26-27 | $k0-k1 | Reserved kernel/OS | Don’t use them
$28 | $gp | Pointer to global data area | 
$29 | $sp | Stack pointer | 
$30 | $fp | Frame pointer | 
$31 | $ra | Function return address | 

## Slide 24: Register File Allocation Redux
0 is $zero is 0x00000000
  The only physically special address
  Specific to MIPS!
The other 31 are all interchangeable
But we treat them differently for convenience
For today, we’ll use $t0 through $t9

## Slide 25: Basic Operations
Mathematic: add, sub, mul, div add $t0, $t1, $t2 # t0 = t1+t2
Unsigned (changes overflow condition) addu $t0, $t1, $t2 # t0 = t1+t2
Immediate (one input a constant) addi $t0, $t1, 100 # t0 = t1+100
Logical: and, or, nor, xor and $t0, $t1, $t2 # t0 = t1&t2
Immediate andi $t0, $t1, 7 # t0 = t1&b0111
Shift: left & right logical, arithmetic sllv $t0, $t1, $t2 # t0 = t1<<t2
Immediate sll $t0, $t1, 6 # t0 = t1<<6
Notes: Wikipedia has a pretty clear reference for MIPS: http://en.wikipedia.org/w/index.php?title=MIPS_architecture&oldid=521742082#MIPS_assembly_language
Also http://www.mrc.uidaho.edu/mrc/people/jff/digital/MIPSir.html is very good.

## Slide 26: Basic Operations
Mathematic: add, sub, mul, div add $t0, $t1, $t2 # t0 = t1+t2
Unsigned (changes overflow condition) addu $t0, $t1, $t2 # t0 = t1+t2
Immediate (one input a constant) addi $t0, $t1, 100 # t0 = t1+100
Logical: and, or, nor, xor and $t0, $t1, $t2 # t0 = t1&t2
Immediate andi $t0, $t1, 7 # t0 = t1&b0111
Shift: left & right logical, arithmetic sllv $t0, $t1, $t2 # t0 = t1<<t2
Immediate sll $t0, $t1, 6 # t0 = t1<<6
Use A Cheat Sheet For These

## Slide 27: Our First Assembly Program
Average Four Numbers
$t5 = ($t0 + $t1 + $t2 + $t3)/4
How do we write this in MIPS Assembly?

## Slide 28: Our First Assembly Program
$t5 = ($t0 + $t1 + $t2 + $t3)/4
add $t5, $t0, $t1 # $t5 = $t0 + $t1
add $t5, $t5, $t2 # $t5 += $t2
add $t5, $t5, $t3 # $t5 += $t3
??? $t5, $t5, 2 # $t5 /= 4
Which Shift do we use?
What assumptions are we making for the inputs?
Notes: Shift Right Logical – srl
Shift Right Arithmatic – sra
Answer: We’re assuming that the inputs are integers, and that they’re all small enough that summing them won’t cause an overflow. Also, the choice of shift indicates signed vs unsigned

## Slide 29: Jumping and Branching
Review:
  Jumps change the Program Counter, period.
  Branches check a condition and optionally jump.
  Needs a target location or offset to go to/by
Calculating jump locations by hand is boring
  Let the Assembler do it for us!
  Use Labels

## Slide 30: Jumping / Branching Example
if (a ==b)
a+=3
else
b+=7
c=a+b
A simple example to show case jumping and branching

## Slide 31: Jumping / Branching Example
if (a==b)
a+=3;
ELSEIF:
b+=7;
ENDIF:
c=a+b
Add labels to indicate our branch / jump targets

## Slide 32: Jumping / Branching Example
if (a !=b) goto ELSEIF
a+=3;
goto ENDIF
ELSEIF:
b+=7;
ENDIF:
c=a+b
Rewrite our if statements
If (x) do y becomes
If (~x) skip y

## Slide 33: Jumping / Branching Example
bne a, b, ELSEIF
a+=3;
j ENDIF
ELSEIF:
b+=7;
ENDIF:
c=a+b
Use specific jump and branch operations

## Slide 34: Jumping / Branching Example
bne a, b, ELSEIF
add a, a, 3
j ENDIF
ELSEIF:
add b, b, 7
ENDIF:
add c, a, b
Translate remaining code
Todo:
  Assign registers to a,b,c
    Human Job
  Calculate offsets
    Assembler Job

## Slide 35: Desk/Board Work
Download MARS
  http://courses.missouristate.edu/kenvollmar/mars/
  http://goo.gl/mOsZ8
Open the environment, start writing assembly
Hint: Work through the process methodically

## Slide 36: Desk/Board Work
Calculate the Sum of integers [0,N]
Calculate Nth Fibonacci Number
Hints:
  N starts in $a0, put answer in $v0
  Use $t0-$t9 as temporary storage
  Set initial conditions with add <dest>, $zero, value
  Comment with #
Bonus:
  Multiply without using mul, mult, etc
  Find Square Root (with a Nope Loop? binary search?)
  Find Nth Prime

## Slide 37: Fibonacci Solution with Loops
#assume N>=2
addi $t0, $zero, 1 #F_(n-1)
addi $t1, $zero, 1 #F_(n-2)
addi $t2, $zero, 2 #n
#t3 is F_n
loop:
add $t3,$t0,$t1 #F_n=F_(n-1)+F_(n-2)
beq $t2,$a0,breakloop #if (n==N) goto breakloop;
addi $t2,$t2,1 #n++
add $t1,$zero,$t0 #F_(n-2)=F_(n-1)
add $t0,$zero,$t3 #F_(n-1)=F_n
j loop #restart loop
breakloop:
add $v0,$zero,$t3 #return the answer

## Slide 38: Memory Organization
Lets talk to Data Memory!
Viewed as an 1-dimension array
Memory address indexes into array
Byte Addressable:
  8 bits of data per address
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 39: Memory Organization
Bytes are nice, but our registers are "words"
For MIPS, a word is 32 bits or 4 bytes.
232 bytes with byte addresses from 0 to 232-1
230 words with byte addresses 0, 4, 8, ... 232-4
...
0
4
8
12
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Our registers hold 32 bits of data

## Slide 40: Loads & Stores
Loads & Stores move words between memory and registers
  All operations on registers, but too small to hold all data
  lw $t0, $t1 # $t0 = Memory[$t1]
  sw $t2, $t3 # Memory[$t3] = $t2
Note: lbu & sb load & store bytes
Store
Load
General
Purpose
Registers
t0:
t1:
t2:
t3:
124
723
4
Memory
12:
140:
66

## Slide 41: Word Alignment
Require that objects fall on an address that is a multiple of their size
What are the last two bits of a 32-bit word aligned address?
0 1 2 3
Aligned
Not
Aligned
Notes: The last two bits of a 32-bit word aligned address will always be zero.

## Slide 42: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# Assume v in $a0,
k in $a1
Store
Load
General
Purpose
Registers
a0:
a1:
t0:
t1:
t2:
964
10
Memory
0A12170D
1000
11111111
1004
00000000
1008
FFFFFFFF
1016
0F0F0F0F
1012
FFFFFFFF
1020

## Slide 43: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
load v[k] into temp0
load v[k+1] into temp1
store temp0 into v[k+1]
store temp1 into v[k]
}
# Assume v in $a0,
k in $a1
Convert array operations in to load / store operations
Why do we need temp1?
Why wasn’t it in the C code?

## Slide 44: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
address0 = v+k*4
address1 = address0 + 4
load address0 into temp0
load address1 into temp1
store temp0 into address1
store temp1 into address0
}
# Assume v in $a0,
k in $a1
Calculate memory address of v[k] as
v + k * sizeof(int)
v + k * 4

## Slide 45: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
address0 = k*4
address0+= v
address1 = address0 + 4
load address0 into temp0
load address1 into temp1
store temp0 into address1
store temp1 into address0
}
# Assume v in $a0,
k in $a1
Expand math for calculating address0

## Slide 46: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
sll address0, k, 2
add address0, address0, v
add address1, address0, 4
lw temp0, (address0)
lw temp1, (address1)
sw temp0, (address1)
sw temp1, (address0)
}
# Assume v in $a0,
k in $a1
Replace with actual instructions
sll – shift left
lw – load word
sw – store word
Todo:
Assign Registers

## Slide 47: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
sll address0, k, 2
add address0, address0, v
add address1, address0, 4
lw temp0, (address0)
lw temp1, (address1)
sw temp0, (address1)
sw temp1, (address0)
}
# Assume v in $a0,
k in $a1
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# Assume v in $a0,
k in $a1

## Slide 48: Remainder of Class
Write one final exam question
Practice Assembly
  Can you reverse an array?
  Can you sort an array?
  How do you multiply in IQ?
    Signed? Unsigned?
  Calculate a Polynomial?
Work on Lab
Hint: Prepopulating Arrays
… code code code…
lw $t0, array1($t1)
…snip moar code…
.data
array1
0x12345678 #element0
0x23456789 #element1
…

## Slide 49: IQ in Assembly
Total number of bits is usually:
  Full Word (I+Q=32)
  Half Word (I+Q=16)
Add/Sub are very easy
  Use Integer operations unchanged
Multiplication is mildly tricky
  May require additional operations
Division is a pain

## Slide 50: IQ in Assembly
How do you Multiply?
  Integer Multiplication
  Shift it back in place
  Overflow?
For now, use I8Q8 sign extended
  Top 16 bits are all zero or all one

## Slide 51: IQ in Assembly
Multiply U8Q8 x U8Q8
  Becomes U16Q16
Shift by 8
  Becomes U16Q8 with 16 leading zero bits
And 0x0000FFFF
  Becomes U8Q8 with 16 leading zero bits