## Slide 1: b1011 Processor to Processor
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Today
Allow our Processors out into the wild!
This is an experimental lecture
Time for HW4 at End

## Slide 3: … but first
EMAIL ALL OF US
NOT JUST LYRA
IT MAKES LYRA SAD
IT MAKES YOU SLOW

## Slide 4: Check In
We’ve glanced at the full stack
  Gates -> Sub-systems -> Processor -> Code
How do we talk to the rest of the world?
Example: Analog to Digital Converter

## Slide 5: LTC1605

## Slide 6: LTC1605

## Slide 7: Timing Diagram

## Slide 8: Timing Diagram
Conversion begins when R/C goes low
  Busy is asserted
  Data becomes INVALID

## Slide 9: Timing Diagram
Conversion Finishes
  Data becomes valid
  Wait a moment
  Busy is de-asserted

## Slide 10: Timing Diagram
Invalid Data
  Recall lecture 2: Timing and Latches
Hi-Z
  Nothing asserted, line floats.

## Slide 11: Generic Parallel Access (Fast)
Master Requests Data
Slave responds with data within Access Time
Master reads Data, finishes Request
Slave ready for next request

## Slide 12: Generic Parallel Access (Slow)
Master Requests Data
Slave is too slow to respond within Access Time, Asserts WAIT
Slave deasserts wait after providing data
Master receives, stops request
Slave ready for next request

## Slide 13: Parallel Port
N Data Pins
Control Pins:
  Request Behaviors
  Indicate Readiness
What if we need more Data?
  Add More Pins 

## Slide 14: Pseudo Parallel Port
D Flip Flops to re-use existing Data Pins
Total Controlled Bits:
  D Data Pins
  L Latch Pins
  DL Total

## Slide 15: Pseudo Parallel Port
Notes: {signal: [
{name: 'DataIn', wave: 'x2.2.2.2..x', data: 'Data[7:0] Data[7:0] Data[7:0] Data[7:0] '},
{name: 'Latched[7:0]', wave: 'x.2........', data: 'Valid'},
{name: 'Latch0', wave:'0.10.......'},
{name: 'Latched[15:8]', wave: 'x...2......', data: 'Valid'},
{name: 'Latch1', wave:'0...10.....'},
{name: 'Latched[23:16]', wave: 'x.....2....', data: 'Valid'},
{name: 'Latch2', wave:'0.....10...'},
{name: 'Latched[31:24]', wave: 'xxxcxxxxx2.', data: 'Valid'},
{name: 'Latch3', wave:'0........10'},
{},
]}

## Slide 16: Serial Peripheral Interface
One data pin per direction
  MOSI – Master Out Slave In
  MISO – Master In Slave Out
One Clock Pin
  Replaces all of the Latch Pins
Chip Select
  Tells a peripheral we’re talking to it
One bit of data per clock strobe

## Slide 17
Multiple Peripherals require individual Chip Select

## Slide 18: Implementation
Basically, Shift Registers

## Slide 19: UART
Universal Asynchronous Receiver Transmitter
One Data Pin per Direction
  Inconsistently Named
  Rx? Tx?
No Clock Pin!

## Slide 20: UART Clocking
No Explicit Clock
Instead, agree on speed and hope for the best
Notes: http://www.ee.nthu.edu.tw/jcliao/mic97/chap12R/showCh12R.htm

## Slide 21: UART Clocking
Starts High
Drops low to start
  Start Bit
Data Bits are sent
Remains High to recover
  Stop Bit(s)
Receiver measures data halfway through each bit
  In case of clock error
1.5 Bit Times

## Slide 22: UART Clock Error
How many bits can be sent reliably before resynchronization?
  Clock Speed Tolerance is
  Failure once we drift half a bit width
  Each bit drifts by up to
Failure after Bit Widths
“Correct” Sampling Time
Drifted Sampling Time

## Slide 23: Serial Vs Parallel
Parallel
One Word at a time
Cheaper Logic
Fast for short distances
  Many bits per clock
Serial
One Bit at a time
Cheaper Wiring
Fast for long distances
  Faster Clock possible
Distance affects maximum clock rate:
  Capacitance affects slew time
    Slowly charge wire, delays stability
  Wire length mismatch creates skew time
    Some signals arrive sooner than others
  Parallel wires create extra capacitance
    Parallel is more affected than Serial

## Slide 24: Bi-Directionality
So far, every pin has a defined direction
  This can be done with normal gates!
To do bidirectional, we need new equipment

## Slide 25: Lets get PHYsical
PHY interfaces logic with the physical world
Needed whenever we go “off chip”
Simplest PHY is an inverter.
  Orientation determines input vs output

## Slide 26: GPIO
Input is a Buffer
  Cleans signal for internal logic
Output Tri-State Buffer
  Can “release” the line
  Only asserts when enabled

## Slide 27: TriState Buffer
http://www-mdp.eng.cam.ac.uk/web/library/enginfo/mdp_micro/lecture1/lecture1-5-4.html
When Enable is true, acts like a normal buffer
  PFET on for Input = 1
  NFET on for Input = 0
When Enable is false, doesn’t assert a state
  Neither FET is on
  Output “Floats”
  Output = Z or Hi-Z

## Slide 28: PSOC GPIO Structure
http://www.cypress.com/

## Slide 29
http://www.ti.com/lit/ug/sprueq8a/sprueq8a.pdf
Notes: TMS320DM646x GPIO structure

## Slide 30: I2C = Inter-Integrated Circuit
Two Wire Serial Protocol
  SDA = Serial DAta
  SCL = Serial Clock
7 bit addressing: Up to 127 devices per bus
  … unless capacitance kills you (400pF nom max)

## Slide 31: Whose Line is it, Anyway?
No Chip Select Lines
Each message has an address preamble
  If it isn’t for you, ignore it.

## Slide 32: Bidirectionality
Lines have Pullup Resistors
  Gently pulls it to VDD
  Default state is 1
Devices yank to ground to assert a zero
  If no one asserts 0, it is a 1
  This is called “Open Drain”

## Slide 33: I2C Bus Transfer
Multiple bytes sent in a transaction; every 8 bits has a 9th bit that is an acknowledge.

## Slide 34: I2C
Pull-Ups limit max clock frequency
  VERY sensitive to total capacitance
    400pF max
  Slower than other serial protocols
    100kHz Normal, 400kHz Enhanced
  Higher R, Slower max frequency
  Lower R, Higher power dissipation
Addresses can be a pain!
  Not all bits are definable
  Overlap happens more often than you’d expect!

## Slide 35: CAN – Controller Area Network
Typically found in Vehicles, Robots
1 Megabit per Second, 11 bit addressing
Dominant / Recessive Signalling
No Separate Clock Signal

## Slide 36: CAN - Dominance
Like I2C, Dominant vs Recessive
  Requires a separate PHY chip
To Assert:
  Pull CAN HI up
  Pull CAN LO down
  Otherwise, resistor pulls two wires back

## Slide 37: CAN - Frame
Green – Address
Yellow – Data Length in Bytes
Red – Actual Data

## Slide 38: TL;DR;
Data Width
  Parallel
  Serial
Timing:
  Explicit / Shared Clock
  Assumed Clock
  Clock Recovery
  Asynchronous (Ick)
Targets
  One to One
  Broadcast with Address
  Broadcast with Select
PHY
  GPIO?
  Explicit PHY

## Slide 39: Memory Mapped Peripherals
Pretend that Peripherals are weird Memory
Registers that control peripherals are write-only memory addresses
Registers that receive data are read-only
Following Slides are derived from http://www.ti.com/lit/ug/sprugp2a/sprugp2a.pdf

## Slide 43: HW4
Behavioral Behavioral Behavioral
First 6 Deliverables should take <2 Hour Total
  Unless you are doing them wrong 

## Slide 44: Registers
Deliverable 1
  Use DFF as a component
  Don’t draw its implementation
Deliverable 2
  Copy paste, add 14 characters
Deliverable 3
  Copy paste, “Assign _____ = 0”

## Slide 45: Test Bench
Xxxx = 42?
YUP

## Slide 46: With Remaining Time
Work On HW4

## Slide 47: ADC0803
8 Bit Differential ADC
135ns Sample Time

## Slide 48: MAX114/MAX118

## Slide 49
DB[7:0] – Data Bits
RD – Pull low to begin reading
INT – Pulled low to indicate conversion finish

## Slide 50: Timing Diagram

## Slide 51: Instruction Mapped Peripheral