## Slide 1: b1100 Finite State Machines
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Acknowledgements
BYU ECEn 224: http://ece224web.groups.et.byu.net/lectures/A3%20VERILOG.pdf
Y. N. Patt, UT Austin EE382N Verilog Manual: http://users.ece.utexas.edu/~patt/04s.382N/tutorial/verilog_manual.html
Asic World: Verilog Behavioral Modeling: http://www.asic-world.com/verilog/vbehave1.html
Nestoras Tzartzanis, USC EE577b – Verilog for Behavioral Modeling: http://www-scf.usc.edu/~ee577/tutorial/verilog/verilog_lec.pdf
Vishwani Agrawal, ELEC 2200-001 – Digital Logic Circuits
Mike Chen, Finite State Machines

## Slide 3: Today
Finite State Machines
Encodings
Behavioral
MP2

## Slide 4: Finite State Machines
A group of States and Transitions
Move from one state to another along a transition line when the transition’s conditions are met
Heater Off
Heater On
Temp <68F
Temp >72F

## Slide 5: Flying Spaghetti Monsters
In Computer Architecture, FSMs:
  Usually transition on a clock edge
  Are Complete
    All states define transitions for all inputs
  Are deterministic (Unless Quantum)
Heater Off
Heater On
Temp <68F
Temp >72F

## Slide 6: FSM Implementation
Register to hold current state
Wires to provide inputs (arguments)
Look Up Table(s) to map transitions
Current State | Inputs | Resulting State
Heater Off | Too Cold | Heater On
Heater Off | --- | Heater Off
Heater On | Too Hot | Heater Off
Heater On | --- | Heater On
Control Logic
(LUTs)
Inputs
Register
Controls
(State)

## Slide 7: Transitions -> LUT
State | Cold? | Hot? | Next State
Off | Yes | Yes | X
Off | Yes | No | On
Off | No | Yes | Off
Off | No | No | Off
On | Yes | Yes | X
On | Yes | No | On
On | No | Yes | Off
On | No | No | On
Current State | Inputs | Resulting State
Heater Off | Too Cold | Heater On
Heater Off | --- | Heater Off
Heater On | Too Hot | Heater Off
Heater On | --- | Heater On

## Slide 8: LUT -> Kmap -> Circuit
State | Cold? | Hot? | Next State
Off | Yes | Yes | X
Off | Yes | No | On
Off | No | Yes | Off
Off | No | No | Off
On | Yes | Yes | X
On | Yes | No | On
On | No | Yes | Off
On | No | No | On

## Slide 9: FSM Process Summary
Design Requirements
Define States
Define Transitions
Assign Values / Binary Codes
Calculate Widths
Make a LUT
Connect Registers
(Optional) Simplify
Logic (LUT)
REG
Outputs
Inputs
Present
state
Next
state
Clock

## Slide 10: Types of FSM
Moore
Output only depends on state
More States
“Pure” LUT Solution
Mealy
Output depends on state AND inputs
Fewer States
Additional Logic?

## Slide 11: Binary Encoding
States are stored as binary numbers
Requires registers for states
LUT requires a decoder (per usual)

## Slide 12: One Hot Encoding
States are stored as one bit being “hot”
Requires N registers for N states
LUT doesn’t require a decoder
  The encoding is like a decoder!
Binary | One Hot
00 | 0001
01 | 0010
10 | 0100
11 | 1000

## Slide 13: Encoding Comparison
Binary
Fewer Flip Flops
Slower
Wider LUTs
One Hot
More Flip Flops
Faster Clock Speeds
Simpler Logic
Many Illegal States
  What if 2 bits are hot?
  LOTS of “Don’t Cares” in logic

## Slide 14: Wait States
Typical Data Flow:
  FSM creates control signals for a clocked element
  Other element takes N cycles to finish
  FSM proceeds to next task
Wait States delay the FSM
  Very Simple  Single Transition
  One Hot  Just a D Flip Flop, no logic!

## Slide 15: Create FSMs for:
Output True if the number of 1s is a multiple of 4
  Every clock cycle, increment if input = 1
Output True if the number of pulses is a multiple of 3
  Only increment if there was a 0 between 1s.
A Soda Machine
  Inputs: Nickle Detected, Dime Detected
  Outputs: Every 25 cents, it gives you sugar water
Sequential Adder
  Inputs: 2 streams of bits, LSB first
  Output: 1 stream of bits, LSB first equal to the sum of the inputs
For Each:
  Flow Diagram
  One Hot Schematic
  Binary Schematic

## Slide 16: Hints for Board Work Slide
Output True if the number of 1s is a multiple of 4
  Use 4 states connected in a ring. Advance on 1.
  State0 outputs 1, all others output 0
Output True if the number of pulses is a multiple of 3
  Use 6 states (3 pairs). Each transition represents a positive or negative edge on the input signal.
A Soda Machine
  Use 5 states (5 cents each). Advance by 0, 1 or 2 states based on inputs (3 states depending on how you interpret reqs)
Sequential Adder
  Use your states to hold carry information.

## Slide 17: Behavioral Verilog Hints for MP2

## Slide 18: Asynchronous Logic
Stuff that happens all the time
assign DataOut = registers[Addr];
“Continuous Assignment”
  Left hand MUST be a wire
What are the dependencies?
When is DataOut re-calculated?
  In Simulation? In “Real Life”?

## Slide 19: Example: A Full Adder
{} is Concatenation
Note that a,b,cin are not the same length
“|sum” is a Reduction
More info at http://www-scf.usc.edu/~ee577/tutorial/verilog/verilog_lec.pdf
wire[15:0] sum,a,b;
wire cin, cout, zero;
assign {cout, sum} = a + b + cin;
assign zero = !(|sum);

## Slide 20: Synchronous Logic
always @(posedge clk)
if (regWE)
registers[Addr] <= DataIn;
Stuff that happens when triggered
  Trigger list in the @(______) section
When is this re-calculated?
Notes: Every positive edge of the clock

## Slide 21: Example: A counter
Is this synchronous or asynch?
What does WID do?
How would this look in structure?
module upCnt(cnt, clk, clr);
parameter WID=4;
input clk, clr;
output reg[WID-1:0] cnt;
always @(posedge clk)
if (clr)
cnt <= 0;
else
cnt <= cnt + 1;
endmodule

## Slide 22: = vs <=
= is a blocking assignment
  Evaluate right hand side, assign to left immediately
<= is a non-blocking assignment
  Evaluate right hand side
  Schedule assignment for the end of the time step

## Slide 23: = vs <=: Swap Fest
What are the values of the registers after each clock period?
Which block swaps?
Which block stomps?
always @(posedge clk)
begin
a = b;
b = a;
end
always @(posedge clk)
begin
c <= d;
d <= c;
end
Notes: <= swaps

## Slide 24: = vs <= : Timing
reg a, b, c, d, e, f, g, h, i;
initial begin
#10 a = 1; // a assigned at time 10
#2 b = 0; // b assigned at time 12
#4 c = 1; // c assigned at time 16
end
initial begin
#10 d <= 1; // d assigned at time 10
#2 e <= 0; // e assigned at time 12
#4 f <= 1; // f assigned at time 16
end
initial begin
g <= #10 1; // g assigned at time 10
h <= #2 0; // h assigned at time 2
i<= #4 1; // i assigned at time 4
end
Blocking Assignments
  Each line blocks the next line
Non Blocking Assigments
  Wait statement in scheduling
  The waits cause the blocking
Non Blocking Assignments
  Wait statement in assignment

## Slide 25: = vs <= : TL;DR;
I prefer using <=
  Converts from circuits more naturally
  How regs actually work
You can use =
  Converts from C code more naturally
  Synthesizer has more work to do

## Slide 26: Setting Defaults
Good for “rare” signals
always @(posedge clk) begin
  outputsignal <= 0;
  Case(state)
    State0:
    State1:
      outputsignal <= 1;
    …
    StateN:
  endcase

## Slide 27: Behavioral Verilog Hints and Tricks
Binary Encoding
case(state)
State0: begin
  // do stuff
end
State1: begin
// do stuff
end
endcase
“Normal Case Statement”
One Hot Encoding
case(1’b1)
State[0]: begin
// do stuff
end
State[1]: begin
// do stuff
end
endcase
“Reversed Case Statement”

## Slide 28: 3 to 8 Decoder
// 8 output decoder with 3 select (in) bits.
module decoder3to8(in,out);
input [2:0] in;
output [7:0] out;
reg [7:0] out;
always @ (in) begin
case (in)
3'b000 : out = 8'b0000_0001;
3'b001 : out = 8'b0000_0010;
3'b010 : out = 8'b0000_0100;
3'b011 : out = 8'b0000_1000;
3'b100 : out = 8'b0001_0000;
3'b101 : out = 8'b0010_0000;
3'b110 : out = 8'b0100_0000;
3'b111 : out = 8'b1000_0000;
endcase
end
endmodule
Notes: Yell about buffers for a bit here

## Slide 29: Lets Break the 3 to 8 Decoder
module decoder3to8(in,out);
input [2:0] in;
output [7:0] out;
reg [7:0] out;
always @ (in) begin
case (in)
3'b000 : out = 8'b0000_0001;
3'b001 : out = 8'b0000_0010;
3'b010 : out = 8'b0000_0100;
3'b011 : out = 8'b0000_1000;
3'b100 : out = 8'b0001_0000;
3'b101 : out = 8'b0010_0000;
3'b110 : out = 8'b0100_0000;
3'b111 : out = 8'b1000_0000; endcase
end
endmodule
Forget one case
Now case b111 remembers the previous state of the decoder!
Extra IMPLIED DFFs!!

## Slide 30: Lets Break the 3 to 8 Decoder
module decoder3to8we(in,out, en);
input [2:0] in;
input en;
output [7:0] out;
reg [7:0] out;
always @ (in) begin
out = 0;
if(en) begin
case (in)
3'b000 : out = 8'b0000_0001;
3'b001 : out = 8'b0000_0010;
3'b010 : out = 8'b0000_0100;
3'b011 : out = 8'b0000_1000;
3'b100 : out = 8'b0001_0000;
3'b101 : out = 8'b0010_0000;
3'b110 : out = 8'b0100_0000;
3'b111 : out = 8'b1000_0000;
endcase
end
end
endmodule
Add an Enable Signal
The out = 0 is never overwritten
What did I forget to do?

## Slide 31: Lets Break the 3 to 8 Decoder
module decoder3to8we(in,out, en);
input [2:0] in;
input en;
output [7:0] out;
reg [7:0] out;
always @ (in, en) begin
out = 0;
if(en) begin
case (in)
3'b000 : out = 8'b0000_0001;
3'b001 : out = 8'b0000_0010;
3'b010 : out = 8'b0000_0100;
3'b011 : out = 8'b0000_1000;
3'b100 : out = 8'b0001_0000;
3'b101 : out = 8'b0010_0000;
3'b110 : out = 8'b0100_0000;
3'b111 : out = 8'b1000_0000;
endcase
end
end
endmodule
What did I forget to do?
  Update Sensitivities!
Synthesises a DFF for en
  Updates only on (in)
TL;DR
  Sensitive to sensitivities

## Slide 32: Behavioral FSM
Use parameter for state names
  parameter state_GETTING_ADDRESS = 0;
  parameter state_GOT_ADDRESS = 1;
  parameter state_READ = 2;
  parameter state_READ_WAIT = 3;
Better than define
  Locally Scoped

## Slide 33: Virtual
Only affects GUI in ModelSim
  No impact on actual simulation
Virtual Type
  Allows you to define an enumeration
  Again, only in the GUI
Virtual Function
  Allows you to define a new signal calculated from simulation information into the GUI kernel
  Again, doesn’t propagate back to the simulation

## Slide 34: Virtual Example
virtual type {list of names} type_name
virtual function {(type) source_signal} new_signal_name
virtual type {{0 GET} {1 GOT} {2 READ} {3 READ2} {4 DONE}} state_type
virtual function {(state_type) /spiMemoryTest/spim/state} state_virtual
add wave -position insertpoint \
sim:/spiMemoryTest/spim/state_virtual

## Slide 35: Loading Memories from Files
module memory(clk, regWE, Addr,
DataIn, DataOut);
input clk, regWE;
input[9:0] Addr;
input[31:0] DataIn;
output[31:0] DataOut;
reg [31:0] mem[1023:0];
always @(posedge clk)
if (regWE)
mem[Addr] <= DataIn;
initial $readmemb(“file.dat”, mem);
assign DataOut = registers[Addr];
endmodule
$readmemb and $readmemh allow you to load a memory from a file
  b for Binary
  h for Hexadecimal
Done in an initial block
Examples are in the lab3 starter package on the wiki

## Slide 36: With Remaining Time
Work on Lab 2 Planning with your group

## Slide 37
 |  |  | Out | 
State | Input | Next | Moore | Mealy
00 | 0 | 00 | 1 | 1
00 | 1 | 01 | 1 | 0
01 | 0 | 01 | 0 | 0
01 | 1 | 10 | 0 | 0
10 | 0 | 10 | 0 | 0
10 | 1 | 11 | 0 | 0
11 | 0 | 11 | 0 | 0
11 | 1 | 00 | 0 | 1

## Slide 38: Pulse Counting