## Slide 1: b1101 Multi-Cycle CPUs
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Microchip Technology Inc (Datasheet)
A. Sahu, Indian Institute of Technology

## Slide 3: Today
Clocks
Recall Single-Cycle CPUs
Single-Cycle Shortcomings
Multi-Cycle CPUs
Instruction Decoding with an FSM

## Slide 4: Execution Overview
Fetch instruction from memory
Decode instruction into actions/controls
Fetch/Decode operands
Compute result value or status
Push result(s) to storage
Determine next instruction
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 5: Execution Overview
Fetch instruction from memory
Decode instruction into actions/controls
Fetch/Decode operands
Compute result value or status
Push result(s) to storage
Determine next instruction
Reference Lecture b100x
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 6: Clocks and Stability
The clock is a massive, chip wide signal
  All timing slaves to it
  Huge buffers to keep everyone in line
Usually a Crystal (XTAL / XO) as a time base
  Very precise – Easily tens of parts per million
Sometimes an RC oscilator
  ModCon all over again

## Slide 7: Types of Oscillators w/ DigiKey Pricing
Crystals:
  50ppm  16 cents @ 1kU
  10ppm  24 cents (for common frequencies)
XO (Crystal + Support Circuitry)
  50ppm  53 cents
  10ppm  84 cents
  0.5ppm  $1.12
TCXO (Temperature Compensated X0)
  0.5ppm  $1.20
  280ppb  $10.41
OCXO (Oven Compensated XO)
  50ppb  $39
  5ppb  $112
  0.1ppb  $1,798
Notes: These are drift specs, not initial accuracy.

## Slide 8: Clocks and Instability
Specialized systems can change clock freq
Phase Locked Loop to multiply / divide freq
  Some can change this multiplier during operation
Spread Spectrum Oscillator:
http://www.mecxtal.com/clk_hm.php

## Slide 9: Clocks Change Slowly
Spread Spectrum effects are slow!
How many clock cycles is 0.01ms?
http://www.minicircuits.com/app/VCO15-20.pdf
Notes: 10 Cycles per MHz

## Slide 10: Clock Changes Slower than Instructions
For our processors, clock isn’t adjustable
  Decided at Manufacture Time
For modern processors, clock adjusts:
  Very explicitly. Processor pauses during change.
  Dynamic Frequency Scaling  Power Save
Ben has been working on changing this

## Slide 11: Information Rippling
Each Clock Cycle “ripples” left to right
  Elements emit garbage values until they stabilize
Elements on the leading edge of cycle (LEFT)
  Spend most of the time “bored” (stable)
  Under-utilized
Elements on the lagging edge of cycle (RIGHT)
  Spend most of the time twitching as things settle
  Spend unnecessary dynamic power

## Slide 12: Performance of Single-Cycle Machine
Clock speed is set by the slowest instruction
Arithmetic & Logic
Load
Store
Branch
Jump
Instr. Memory
PC
mux
Reg Read
ALU
mux
Reg Setup
Data Memory
Instr. Memory
PC
Reg Read
ALU
mux
Data Memory
Adder
PC setup
Instr. Memory
PC
Reg Read
ALU
mux
mux
Instr. Memory
PC
Reg Read
ALU
mux
mux
Reg Setup
Instr. Memory
PC
PC setup
mux

## Slide 13: Clock TL;DR;
Unable to change for each instruction
Slow instruction slows EVERY instruction
Harrison Bergeron applied to Transistors

## Slide 14: Reducing Cycle Time
Cut combinational dependency graph and insert register / latch
Do same work in N fast cycles, rather than one slow one
storage element
Acyclic
Combinational
Logic (A)
storage element
storage element
Acyclic
Combinational
Logic (B)
storage element
Acyclic
Combinational
Logic
storage element

## Slide 15: Goals
Free up fast instructions from slow clock curse
  Load Word is Super Slow
Make better use of available resources
  Reuse components (2 Memories, 2 or 3 Adders)
Free up space to speed up components
  One big fast ALU, not multiple slow ALU/adders

## Slide 16: Multi-Cycle CPUs in the Wild
Common in small embedded spaces
  PIC16, PIC18
  4 bit micros (watches)
Marketing will try to confuse you
  Advertise MHz
  Hide CPI, Instructions per second, etc
http://ww1.microchip.com/downloads/en/DeviceDoc/41213D.pdf

## Slide 17: Preview of White Boards to Come
We will go to the white boards “soon”.
You will create the schematic necessary to run the RTL design I’m about to give you.
I’m “cheating” and giving you parts of MY answer, to make your reinvention smoother
There is nothing sacred about MY answer,
  You’re usually on the hook for the whole shebang
  If it fulfils the contract and is small/fast, awesome.

## Slide 18: Strategy
Enumerate all the stuff we have to do
  Per Instruction
  Highlight Common Features
Break tasks in to N phases
  N is different for different instructions
Balance work done in each phase

## Slide 19: “Typical” Phases
IF: Instruction Fetch
ID: Instruction Decode (& register fetch)
EX: Execute
MEM: Read from Memory
WB: Write Back to Memory
Other Architectures make different divisions!

## Slide 20: New Registers
Instruction Register (IR)
  Instruction fetched from Data Memory
Data Register (MDR)
  Data fetched from Data Memory
Operands (A, B)
  Fetched from Register File
Result (Res)
  Result of the ALU calculation
Some of these may need write enable controls!
MDR
ALU RES
B
A
IR
Rs
Rt
Rd
Imm16

## Slide 21: Old Friends
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Aw Aa Ab Da
Dw Db
Register
WrEn File
PC
Concatenate

## Slide 22: Phases: Load Word
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[IR[16:20]]
EX: Result = A + sign extended immediate
MEM: DataReg = Mem[Result]
WB: RegFile[rt] = DataReg
Notes: We don’t use B later, so this doesn’t matter. We don’t care if it gets executed or not

## Slide 23: Phases: ADD
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
EX: Result = A + B
MEM:
WB: RegFile[rd] = Result

## Slide 24: Phases: Store Word
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
EX: Result = A + sign extended immediate
MEM: Mem[Result] = B
WB:

## Slide 25: Phases: Branch if Equal
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
Res = PC + sign extended immediate
EX: if(A==B) PC = Res
MEM:
WB:

## Slide 26: Phases: Jump
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
EX:
MEM:
WB:

## Slide 27: Example Control Diagram
OP | Cycle | Phase Type | PC Enable | A Enable | ALU Control | IR Enable
AND | 0 | IF | 1 | X | Add4 | 1
 | 1 | ID | 0 | 1 | X | 0
 | 2 | EX | 0 | X | AND | 0
 | 3 | WB | 0 | X | X | 0
LW | 0 | IF | 1 | X | Add4 | 1
 | 1 | ID | 0 | 1 | X | 0
 | 2 | EX | 0 | X | Add Immed | 0
 | 3 | MEM | 0 | X | X | 0
 | 4 | WB | 0 | X | X | 0

## Slide 28: Lets Make It
Create a Multi-Cycle CPU that can do the instructions on prior pages
  Jump, Branch, R-type, I-type, LW, SW
  Show everything except the actual decode logic
  Reference Lecture b1001, but put everything on one “page”
Sketch a Schematic for your Multi Cycle CPU
  ALU, Register File, Unified Instruction/Data Memory
  Sign Extender, (Optional) Shift by Two
  IR, DR, A, B, Res Registers
  OMG MUXES EVERYWHERE
Create a control chart (to show the actual decode logic)
  Show each cycle of each instruction
  Mux selects, ALU Control Lines, Register Enables
  Use “X” for “Don’t Care”
Create a One Hot FSM to generate control signals
  Flow Diagram First, then push to DFF and Logic
  Then do the ALUsrcB control signal in its entirety
  Then the other control signals as time allows
Send to CompArch14@gmail.com “[MultiCycle] Names”
Notes: Used to include following text:
  Turn this in to CompArch13@gmail.com (Group HW/ClassWork)

## Slide 30: This Page Intentionally Left Blank
Except for that text up there
And some more over here
But really, it is so you don’t accidentally see one possible answer.
But… if you are stuck, go for it.

## Slide 31: Multi Cycle w/ Controls
SignExtnd
PC
<<2
MDR
ALU RES
B
A
WrEn
Addr Dout
Memory
Din
IR
Rs
Rt
Rd
Imm16
Aw Ab Aa
Da
Registers
Dw WrEn Db
4
MemIn
Mem_WE
IR_WE
PC_WE
RegIn
Dst
Reg_WE
ALUSrcA
ALUSrcB
ALUOp
PCSrc
Concat
A_WE
B_WE

## Slide 32: Preview of things to Come
How to control a Multi-Cycle CPU
Timing Concerns and Explicit Balancing
Modern CPUs: Pipelining

## Slide 33: Desk Work
Time your Multicycle design from Monday
  Do symbolically first, then substitute real numbers
  Remember parallel paths!
Component | Symbol | Delay
ALU | tALU | 5ns
Register File | tRF | 3ns
Instruction/Data Memory | tMEM | 6ns
Muxes | 0 | 0
Registers | 0 | 0

## Slide 34: Summary
Split Single Cycle in to multiple cycles
Use variable number of cycles per instruction
  No More Harrison Bergeron-ing
Most Instructions become Faster
Longest Instruction gets Longer
  From unbalanced phases
Costs: Registers, control logic

## Slide 36
Notes: These states have identical outputs. We can merge them.