## Slide 1: b1110 Multicycle (Continued)
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Today
Balancing MicroOps
Review Multicycle Board work so far
Generate FSM controllers
Complete Multicycle Rev 1

## Slide 3: Balance
An unbalanced design has some operations doing more “work” (time) than the others
  Wastes time in fast cycles
Moving work between operations is Balancing
  Reduce the global clock period by leveling
Balance adjacent ops by register positioning
  Some ops are hard to “slice”

## Slide 4: Example
Instruction has 5 components:
  1, 2, 3, 4, and 5 nanoseconds long
  In that order
Divide optimally in to 3 cycles:
  Minimum Clock Period?
  How much time is wasted per instruction?

## Slide 5: Example
Instruction has 5 components:
  1, 2, 3, 4, and 5 nanoseconds long
  In that order
Divide optimally in to 3 cycles:
  Minimum Clock Period? 6ns
  How much time is wasted per instruction? 3ns
  {1,2,3}{4}{5}

## Slide 6: Balancing
Not all resources are fungible
  Some micro-operations are hard to subdivide
  Order of operations matters sometimes
The slowest unit sets the pace for everything
Compare “Optimal” time to Reality
  Measure of Balance

## Slide 7: Example Timings
Instr/Cycle | RTL | Symbolic | Numeric
LW:0 | IR = Mem[PC] | tX1 + tMEM | 10
LW:0 | PC=PC+4 | tX1+tALU+tX2 In Parallel with tX2+tALU+tX2 | 5 5
LW:1 | AB = RegFile[_] | tRF | 3
LW:2 | Res = A + SEI | tALU | 5
LW:3 | DR = Mem[Res] | tX1 + tMEM | 10
LW:4 | RegFile[rt] = DR | tRF+tX1 | 3
Component | Symbol | Delay
ALU | tALU | 5ns
Register File | tRF | 3ns
Instruction/Data Memory | tMEM | 10ns
Muxes (Optional) | tXn | 0ish
Registers | 0 | 0
Notes: Why are muxes ZERO???
Mostly to make the slide go better, but it isn’t as terrible as it sounds.
Muxes towards at the end of the cycle have time for their decoders to settle, and then its just a simple 2AND to go through – super fast.

## Slide 8: Rebalance: Combine Stages 1 and 2
Instr/Cycle | RTL | Symbolic | Numeric
LW:0 | IR = Mem[PC] | tX1 + tMEM | 10
LW:0 | PC=PC+4 | tX1+tALU+tX2 In Parallel with tX2+tALU+tX2 | 5 5
LW:1/2 | Res = RegFile[]+SEI | tRF+tALU | 8
LW:3 | DR = Mem[Res] | tX1 + tMEM | 10
LW:4 | RegFile[rt] = DR | tRF+tX1 | 3
Component | Symbol | Delay
ALU | tALU | 5ns
Register File | tRF | 3ns
Instruction/Data Memory | tMEM | 10ns
Muxes (Optional) | tXn | 0ish
Registers | 0 | 0
Notes: Why are muxes ZERO???
Mostly to make the slide go better, but it isn’t as terrible as it sounds.
Muxes towards at the end of the cycle have time for their decoders to settle, and then its just a simple 2AND to go through – super fast.

## Slide 9: Balancing Penalty
Total time wasted per cycle from poor balance
Instr/Cycle | Time | Penalty
LW:IF | 10 | 0
LW:ID | 3 | 7
LW:EX | 5 | 5
LW:MEM | 10 | 0
LW:WB | 3 | 7
 | 31 | 19
Instr/Cycle | Time | Penalty
LW:IF | 10 | 0
LW:ID/EX | 8 | 2
LW:MEM | 10 | 0
LW:WB | 3 | 7
 | 21 | 9

## Slide 10: Back to Review!

## Slide 11: Multi Cycle w/ Controls
SignExtnd
PC
<<2
MDR
ALU RES
B
A
WrEn
Addr Dout
Memory
Din
IR
Rs
Rt
Rd
Imm16
Aw Ab Aa
Da
Registers
Dw WrEn Db
4
MemIn
Mem_WE
IR_WE
PC_WE
RegIn
Dst
Reg_WE
ALUSrcA
ALUSrcB
ALUOp
PCSrc
Concat

## Slide 12: Phases: Jump
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
EX:
MEM:
WB:

## Slide 13: Phases: Jump
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Data
Memory
PC

## Slide 14: Phases: Jump
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4

## Slide 15: Phases: Jump
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00

## Slide 16: Resolve Conflicts
Muxes for conflicting inputs
Enables for conflicting outputs
  Or put them on every register and remove later
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 17: Control Diagram
 |  | Signals |  | 
Instruction | Phase | PCSrc | PCEn | IREn
Jump | IF |  |  | 
 | ID |  |  | 
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 18: Control Diagram
 |  | Signals |  | 
Instruction | Phase | PCSrc | PCEn | IREn
Jump | IF |  |  | 1
 | ID |  |  | 
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 19: Control Diagram
 |  | Signals |  | 
Instruction | Phase | PCSrc | PCEn | IREn
Jump | IF | ALU | 1 | 1
 | ID |  |  | 
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 20: Control Diagram
 |  | Signals |  | 
Instruction | Phase | PCSrc | PCEn | IREn
Jump | IF | ALU | 1 | 1
 | ID | Concat | 1 | 
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 21: Control Diagram
 |  | Signals |  | 
Instruction | Phase | PCSrc | PCEn | IREn
Jump | IF | ALU | 1 | 1
 | ID | Concat | 1 | 0? X?
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 22: Control Diagram
 |  | Signals |  | 
Instruction | Phase | PCSrc | PCEn | IREn
Jump | IF | ALU | 1 | 1
 | ID | Concat | 1 | 0? X?
PC Enable is Always High
Remove it!
Only valid for an “Only Jumps” Processor
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
PCEn
IREn

## Slide 23: Control Diagram
 |  | Signals | 
Instruction | Phase | PCSrc | IREn
Jump | IF | ALU | 1
 | ID | Concat | 0
PC Enable is Always High
Remove it!
Only valid for an “Only Jumps” Processor
IR
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Memory
PC
4
Concat
b00
PCSrc
IREn

## Slide 24: Finite State Machine
Create Transition Diagram
  This one is “silly” because it is only one instruction
  Yours will be “real”
 |  | Signals | 
Instruction | Phase | PCSrc | IREn
Jump | IF | ALU | 1
 | ID | Concat | 0

## Slide 25: One Hot Encoding
Replace States with DFF
  Input is an OR gate of all incoming transitions
  Each transition is an AND gate:
    “Sending State” AND “Transition Criteria”
  Again, silly in our example 

## Slide 26: One Hot Encoding
Replace States with DFF
  Input is an OR gate of all incoming transitions
  Each transition is an AND gate:
    “Sending State” AND “Transition Criteria”
  Again, silly in our example 

## Slide 27: Add Control Outputs
Add Control Outputs
Outputs are an OR gate
  From each State the signal is high
 |  | Signals | 
Instruction | Phase | PCSrc | IREn
Jump | IF | ALU=0 | 1
 | ID | Concat=1 | 0

## Slide 28: Add Control Outputs
Add Control Outputs
Outputs are an OR gate
  From each State the signal is high
Simplify?
 |  | Signals | 
Instruction | Phase | PCSrc | IREn
Jump | IF | ALU=0 | 1
 | ID | Concat=1 | 0

## Slide 30: FSM Reduction
Return to IF suppressed for diagram clarity
Every terminal state returns to IF.

## Slide 31
These states have identical outputs
They do not have identical transitions
We can still merge them
Notes: These states have identical outputs. We can merge them.

## Slide 32
Tada!

## Slide 33: Multi Cycle w/ Controls
SignExtnd
PC
<<2
MDR
ALU RES
B
A
WrEn
Addr Dout
Memory
Din
IR
Rs
Rt
Rd
Imm16
Aw Ab Aa
Da
Registers
Dw WrEn Db
4
MemIn
Mem_WE
IR_WE
PC_WE
RegIn
Dst
Reg_WE
ALUSrcA
ALUSrcB
ALUOp
PCSrc
Concat

## Slide 34: Resume Board Work!
Finish Structure Schematic (or use mine)
Create Control Diagram
  Google Doc Spreadsheet?
Create Finite State Machine
Create One Hot Encoding

## Slide 35: Example Control Diagram
OP | Cycle | Phase Type | PC Enable | A Enable | ALU Control | IR Enable
AND | 0 | IF | 1 | X | Add4 | 1
 | 1 | ID | 0 | 1 | X | 0
 | 2 | EX | 0 | X | AND | 0
 | 3 | WB | 0 | X | X | 0
LW | 0 | IF | 1 | X | Add4 | 1
 | 1 | ID | 0 | 1 | X | 0
 | 2 | EX | 0 | X | Add Immed | 0
 | 3 | MEM | 0 | X | X | 0
 | 4 | WB | 0 | X | X | 0

## Slide 36: Phases: Load Word
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[IR[16:20]]
EX: Result = A + sign extended immediate
MEM: DataReg = Mem[Result]
WB: RegFile[rt] = DataReg
Notes: We don’t use B later, so this doesn’t matter. We don’t care if it gets executed or not

## Slide 37: Phases: ADD
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
EX: Result = A + B
MEM:
WB: RegFile[rd] = Result

## Slide 38: Phases: Store Word
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
EX: Result = A + sign extended immediate
MEM: Mem[Result] = B
WB:

## Slide 39: Phases: Branch if Equal
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
Res = PC + sign extended immediate
EX: if(A==B) PC = Res
MEM:
WB:

## Slide 40: Phases: Jump
IF: Instruction Register = Memory[PC]
PC=PC+4
ID: PC = PC[31:28],IR[25:0],b00
EX:
MEM:
WB: