## Slide 1: b0001 Boolean Logic
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)

## Slide 3: Today:
Review Survey from last class
Review of Basic Boolean Laws
Clarification of a Basic Law
Truth Tables and Karnaugh Maps

## Slide 4: Most Favoritest Processors
“whatever I have in my laptop”
  Second was “what?”
Specific Intel part numbers
ARM
  M-Cortex!
DSP
ATMega (328)
TM4C1294NCPDT (M4F)
AIC3254 (MiniDSP)
Knight’s Landing (Septuagintaduple cores)
Snapdragon
Raspberry Pi (BCM2835 -> ARM1176JZF-S + GPU)
IBM TrueNorth (Synaptic Processor)
AMD64
Pentium M
Intel 4004
Image Processor / GPU
PIC18f4520
Microsoft Word/Food Processor

## Slide 5: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What do I need to know
  what can be ignored?
Communications
  SPI
  Ethernet
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Embedded Development
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 6: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What do I need to know
  what can be ignored?
Communications
  SPI
  Ethernet
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Embedded Development
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 7: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What do I need to know
  what can be ignored?
Communications
  SPI
  Ethernet
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Embedded Development
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 8: I want to learn:
Why NAND/NOR is ‘universal’
Boolean Logic
How math happens
  2’s compliment
  Endian
  Floats
What makes an architecture ‘good’ or ‘elegant’
How to Debug / Test / Fix / Analyze large systems
What else is in a computer
How to program in assembly
What do I need to know
  what can be ignored?
Communications
  SPI
  Ethernet
Memory Hierarchy and Distribution
Do I actually want to be an ECE/SparkE? (YES)
Embedded Development
Clock speed * # of cores = goodness?
Future of Comp Arch?
GPUs
FPGAs

## Slide 9: Review of Boolean Algebra
1930s: Shannon applies Boole’s algebra to circuits and logic gates
Method to improve representation of a given circuit or logic
  Execution speed
  Resources consumed
Basis of modern processors

## Slide 10: Boolean Laws
1+1 = 1
… Sorry.

## Slide 11: Boolean Laws So Far
X + 0 = X
X * 1 = X
X + 1 = 1
X * 0 = 0
X + X = X
X * X = X X + X̅ = 1
X * X̅ = 0
~~X = X
X+Y = Y+X
XY = YX
X+(Y+Z) = (X+Y)+Z
X(YZ) = (XY)Z
X(Y+Z) = XY + XZ
X+YZ = (X+Y)(X+Z)
X+XY = X
XY+XY̅ = X
X+X̅Y = X+Y
X(X+Y) = X
(X+Y)(X+Y̅) = X
X(X̅+Y) = XY
Notes: Derived in class last week

## Slide 12
(next slide)

## Slide 13
X+X(1)
X

## Slide 14: X + X̅Y = X+Y
Use Distributive Law: X+YZ = (X+Y)(X+Z)
  Treat as an independent variable (Z)
X + X̅Y = (X+X̅)(X+Y)
X + X̅Y = (X+X̅)(X+Y)
Notes: Treat ~X as an independent variable for the use of the distributive law

## Slide 15: Proving Distributive Law
  Apply X+XY=X
  Apply again, but for Z
X+YZ = X+YZ
  

## Slide 16: Mechanical Forms
Truth Table
  Good for finding the results of equations
  Build up large equations in chunks
Karnaugh Map
  Good for finding new representations of equations
  Only really useable for up to 4 inputs at a time
    ((For Humans, synthesizers do many more))

## Slide 17: Times Tables
X | 1 | 2 | 3 | 4
1 | 1 | 2 | 3 | 4
2 | 2 | 4 | 6 | 8
3 | 3 | 6 | 9 | 12
4 | 4 | 8 | 12 | 16

## Slide 18: Boolean Tables
AND Operator
OR Operator
X | 0 | 1
0 | 0 | 0
1 | 0 | 1
+ | 0 | 1
0 | 0 | 1
1 | 1 | 1 2

## Slide 19: Truth Tables
AND Operator
OR Operator
A | B | AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 20: Truth Tables
NAND Operator
NOR Operator
A | B | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 21: Truth Tables
Inputs in left columns
Outputs on the right
Notes in the middle
Enumerate all input combinations
  Count in Binary
Calculate each Row
Equations are equivalent if they have matching truth tables
Notes: My preference is to start with 0 0 0 and increment as though counting in binary.
Do truth table for basic law on white board X+YZ = (X+Y)(X+Z)
X y z (X+Y)

## Slide 22: Example: X+YZ = (X+Y)(X+Z)
X | Y | Z | YZ | X+Y | X+Z | (X+Y)(X+Z) | X+YZ
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 

## Slide 23: Example: X+YZ = (X+Y)(X+Z)
X | Y | Z | YZ | X+Y | X+Z | (X+Y)(X+Z) | X+YZ
0 | 0 | 0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 0 | 0 | 1 |  | 
0 | 1 | 0 | 0 | 1 | 0 |  | 
0 | 1 | 1 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | 1 | 1 |  | 
1 | 0 | 1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 | 1 | 1 |  | 
1 | 1 | 1 | 1 | 1 | 1 |  | 

## Slide 24: Example: X+YZ = (X+Y)(X+Z)
X | Y | Z | YZ | X+Y | X+Z | (X+Y)(X+Z) | X+YZ
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 25: Truth Table -> Equation
Just used a truth table to prove equivalency
  Start with two equations
Used for Equation Transformations?
  Start with one equation, create another

## Slide 26: Truth Table -> Equation
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 27: Truth Table -> Equation
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 28: Truth Table -> Equation
+
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 29: Truth Table -> Equation
+
… Good job, Eric
Now it is bigger!
…and more confusing!
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 30: Karnaugh Map
Moving one square changes only one input.
Cover all 1s with boxes.
Boxes must be power of 2 sized.
Create Sum of Products
Boxes can “wrap around” the edges of the map.
  Toroidal mapping
Invented in ‘52 by Maurice Karnaugh
Notes: Note: Gray coded! This means only one transition for one movement.

## Slide 31: +
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | X | ~X
YZ | XYZ | ~XYZ
~YZ | X~YZ | ~X~YZ
~Y~Z | X~Y~Z | ~X~Y~Z
Y~Z | XY~Z | ~XY~Z

## Slide 32
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | X | ~X
YZ | 1 | 
~YZ |  | 
~Y~Z |  | 
Y~Z |  | 

## Slide 33
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | X | ~X
YZ | 1 | 
~YZ |  | 0
~Y~Z |  | 0
Y~Z |  | 0

## Slide 34
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | X | ~X
YZ | 1 | 1
~YZ | 1 | 0
~Y~Z | 1 | 0
Y~Z | 1 | 0

## Slide 35
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | X | ~X
YZ | 1 | 1
~YZ | 1 | 0
~Y~Z | 1 | 0
Y~Z | 1 | 0

## Slide 36: X+YZ
X | Y | Z | (X+Y)(X+Z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 | X | ~X
YZ | 1 | 1
~YZ | 1 | 0
~Y~Z | 1 | 0
Y~Z | 1 | 0
YZ
X

## Slide 37: Karnaugh Map
Moving one square changes only one input.
Cover all 1s with boxes.
Boxes must be power of 2 sized.
Create Sum of Products
Boxes can “wrap around” the edges of the map.
  Toroidal mapping
Invented in ‘52 by Maurice Karnaugh
Notes: Note: Gray coded! This means only one transition for one movement.

## Slide 38: Four Input Karnaugh Map Example
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅
Which “advanced” law allows us to combine boxes?

## Slide 39: Four Input Karnaugh Map Example
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅
Which “advanced” law allows us to combine boxes?

## Slide 40: 4 Input Karnaugh Map (WhiteBoard)
 | AB | A̅B | A̅B̅ | AB̅
CD | ABCD | A̅BCD | A̅B̅CD | AB̅CD
C̅D | ABC̅D | A̅BC̅D | A̅B̅C̅D | AB̅C̅D
C̅D̅ | ABC̅D̅ | A̅BC̅D̅ | A̅B̅C̅D̅ | AB̅C̅D̅
CD̅ | ABCD̅ | A̅BCD̅ | A̅B̅CD̅ | AB̅CD̅

## Slide 41: Why Karnaugh?
“Mechanical” method guaranteed to get something that works.
Result is only two layers deep – Fast!

## Slide 42: Why not Karnaugh?
Confusing visually for more than 4 variables
  But it still works if you squint
Optimizes for speed, not space.

## Slide 43: To The Boards!
Prove equivalency:
F=(X+Y̅+XY̅)(XY+X̅Z+YZ)
Evaluate Truth Table
  Pro Tip: Build in Layers
Simplify with Karnaugh
Simplify again with Boolean Law
Draw with Gates
(X + Y) = X * Y
(X * Y) = X + Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y

## Slide 44: DeMorgan’s Law
(X + Y) = X * Y
(X * Y) = X + Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
X
0
0
1
1
Y
0
1
0
1
X
1
1
0
0
Y
1
0
1
0
X
+
Y
X•Y
The negation of a conjunction is the disjunction of the negations.
The negation of a disjunction is the conjunction of the negations.*
* Thanks, Wikipedia!

## Slide 45: DeMorgan’s Law
Provides a way to convert AND  OR
Flip ALL the things
  Invert all the inner terms
  Swap AND  OR
  Invert the entire boolean phrase
This works for a single gate with arbitarily many inputs

## Slide 46: The Universal Gates
Karnaugh maps can frame any boolean equation in sum of products (OR of ANDs)
DeMorgan can frame any AND/OR in NAND/NORs
NAND and NOR can represent any combinatorial boolean equation.
Notes: NAND or NOR can be used as an inverter by tying the inputs together

## Slide 47: DeMorgan’s Law example
Example:
Z = A B C + A B C + A B C + A B C
Z = (A + B + C) * (A + B + C) * (A + B + C) * (A + B + C)

## Slide 48: Boolean Equations to Circuit Diagrams

## Slide 49: HW1 is Posted
Due September 15th Midnight
  But you submit by showing a NINJA
  They have sleep schedules