## Slide 1: b0010 Time for Time
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)
Texas Instruments Data Sheets

## Slide 3: Today
The ravages of time
Latches, Flip Flops, Sandals

## Slide 4: Combinational vs. Sequential Logic
Combinational logic
no feedback among inputs and outputs
outputs are a pure function of the inputs
e.g., seat belt light:
(Dbelt, Pbelt, Passenger) mapped into (Light)
Network implemented from logic gates.
The presence of feedback
distinguishes between sequential
and combinational networks.
-
-
-
X
1
X
2
X
n
Logic
Network
Z
1
Z
2
Z
m
-
-
-
Logic Circuit
Driver_belt
Passenger_belt
Passenger
Seat Belt Light

## Slide 5: Circuit Timing Behavior
Simple model: gates react after fixed delay
A
B
C
D
E
F
0
1
0
1
A
B
C
D
E
F
Notes: Why not immediately?
Parasitic Capacitance * Output Impedence forms an RC low pass (simple model)

## Slide 6: Circuit Timing Behavior
Simple model: gates react after fixed delay
A
B
C
D
E
F
0
1
0
1
A
B
C
D
E
F

## Slide 7: Hazards/Glitches
Circuit can temporarily go to incorrect states
Copilot Autopilot Request
Pilot Autopilot Request
Pilot in Charge?
Autopilot Engaged
A
B
C
CAR
PIC
PAR
A
B
C
AE
Must filter out temporary states

## Slide 8: Hazards/Glitches
Circuit can temporarily go to incorrect states
Copilot Autopilot Request
Pilot Autopilot Request
Pilot in Charge?
Autopilot Engaged
A
B
C
CAR
PIC
PAR
A
B
C
AE
Must filter out temporary states
OH NO

## Slide 9: Safe Sequential Circuits
Clocked elements on feedback, perhaps outputs
  Clock signal synchronizes operation
  Clocked elements hide glitches/hazards
Clock
-
-
-
X
1
X
2
X
n
Logic
Network
Z
1
Z
2
Z
m
-
-
-
Clock
Data
Valid
Compute
Compute
Valid
Compute

## Slide 10: Safe Sequential Circuits
Clocked elements on feedback, perhaps outputs
  Clock signal synchronizes operation
  Clocked elements hide glitches/hazards
Clock
-
-
-
X
1
X
2
X
n
Logic
Network
Z
1
Z
2
Z
m
-
-
-
Clock
Data
Stable
GLITCHES
GLITCHES
Stable
GLITCHES

## Slide 11: “Clocked” Elements
Two main categories:
  Flip Flops and Latches
“Hold on” to state until triggered to update.
Many kinds

## Slide 12
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 13
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf
Notes: What does X mean? It means we don’t care what the input is

## Slide 14
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 15
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 16: Vocab!
Setup – Required stability before
Hold – Required stability after
Propagation Delay – Until outputs update

## Slide 17: Reinventing the SR Latch
http://en.wikipedia.org/wiki/File:R-S_mk2.gif
“SR” for “Set Reset”
Cross-coupled NOR/NAND
S | R | Q Next
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 18: Reinventing the SR Latch
http://en.wikipedia.org/wiki/File:R-S_mk2.gif
“SR” for “Set Reset”
Cross-coupled NOR/NAND
S | R | Q Next
0 | 0 | Q
0 | 1 | 0
1 | 0 | 1
1 | 1 | X

## Slide 19: SR Latch Timing
S
R
Q
Q ̅

## Slide 20: SR Latch Timing
S
R
Q
Q ̅

## Slide 21: SR Latch Timing
S
R
Q
Q ̅

## Slide 22: Design Time!
Invent new types of latches by adding control logic around a SR or latch
Treat the SR as a magic box
Create a truth table to translate your requirements to the SR’s inputs
  Use to make a complete circuit

## Slide 23: Boreds
Gated SR latch
  Inputs “work” only while Enable is True
  When Enable is false, S/R have no effect
Design a Gated D Latch
  One Data input instead of Set Reset.
  Output follows input while enabled
  When Enable is false, Output holds last value
Smallest design? Fastest?

## Slide 24: You promised a Flop
Confusing vocab – they are similar
A latch is typically Enabled
  Updates continuously or holds value
A Flip Flop is typically Clocked
  Updates only at a specific moment
All are forms of ‘Bistable Multivibrators’

## Slide 25: Master Slave D-Flip Flop
Two D-Latches in series with opposite polarity Enable lines
Pulse Triggered
  Capture on one edge
  Display on the other
http://en.wikipedia.org/wiki/File:Negative-edge_triggered_master_slave_D_flip-flop.svg

## Slide 26: Edge Triggered D-Flip Flop
Functionally similar to Master Slave
Edge Triggered, not Pulse
  Don’t waste half your clock period!
Construction highly process dependent
  Can be roughly three SR Latches
  Can be “Dynamic Logic” – Learn in VLSI

## Slide 27: Edge Triggered D-Flip Flop
Always has:
  Clk, D, Q
May also have:
  S, R, ~Q
  Set and Reset are asynchronous (ignore clock)
    Can be used to define initial conditions (e.g. at boot)
http://en.wikipedia.org/wiki/File:D-Type_Flip-flop.svg
Clk | D | Q
↑ | 0 | 0
↑ | 1 | 1
Other | X | Q

## Slide 28: Common Uses
In between processing stages
“Debounce” inputs
  Hide external noise / uncertainty from the inputs
Synchronization

## Slide 29: Other Flops
Ternary: Flip-Flap-Flop.
T Flip Flop
  Toggles on each clock strobe
  Good for cutting frequency in half
JK Flip Flop
  Clocked SR flip flop that also supports toggling

## Slide 30: Final Bord
Create a T Flip Flop from an D Flip Flop
Create 16x frequency divider from T Flip Flops
  10x?
Design an Elevator Controller
  Start with a two story building
  What Inputs?
  What Outputs?
  What Memory?
  Don’t worry if you don’t finish

## Slide 31: Edge Triggered D-Flip Flop

## Slide 32: Elevator
Request Floor 1, Request Floor 2, At Floor 1, At Floor 2
Moving, Direction

## Slide 33: Possible Circuit?

## Slide 34: Possible Circuit?