## Slide 1: b0100 Number Systems
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Acknowledgements
Revised by
  George Herring
  Lisa Park
  Juliana Nazaré
  Keely Haverstock

## Slide 3: Today
Radix R Numbers
Negative Numbers
Fixed Point
Homework
Letters: Dimitar Dimitrov, Thomas Chen

## Slide 4: There are 10 types of people
Those that understand binary
Those that do not

## Slide 5: There are 10 types of people
Those that understand binary
Those that do not
And those who do not presume Radices…

## Slide 6: Rebasing and Reradixing
123 = 1*(10^2) + 2*(10^1) + 3*(10^0)
This is true for all Radices!
h123 = 1*(h10^2) + 2*(h10^1) + 3*(h10^0)
  1*d16^2 + 2*d16^1 + 3*d16^0 = d291
o123 = 1*(o10^2) + 2*(o10^1) + 3*(o10^0)
  1*d8^2 + 2*d8^1 + 3*d8^0 = d83
Notes: This is true for all Radices – That are high enough to be able to represent 3

## Slide 7: Innocence Lost
You can not assume to know the base of a number without context or indication.
Be Explicit.

## Slide 8: Radices in Other Cultures
Decimal is most common
Base 8 – Native Americans
Base 20 – Mayan
Base 60 – Babylonians
  Mixed 6 & 10
Base 12 – Nigeria, Various Mathematicians
Base 24 – Kaugel (Papa New Guinnea)
  In groups of 4
Notes: Mathematicians keep trying to push for base 12

## Slide 9: Base 27 in Telefol
Fingers (1-5) (Left hand first)
Wrist, forearm, elbow, bicep, shoulder (6-10)
Neck, Ear, Eye (11-13)
Nose (14)
Eye, Ear, Neck (15-17)
Shoulder, bicep, elbow, forearm, wrist (18-22)
Fingers (23-27)

## Slide 10: Common Indicators
Hexadecimal
  D = 0123456789ABCDEF
  0x1234
  h1234
  123416
Octal
  D = 01234567
  01234
  o1234
  12348
Decimal(10)
  D = 0123456789
  1234
  d1234
  123410
Binary (Base 2)
  D = 01
  0b1010
  b1010
  10102

## Slide 11: Radix Conversion
General Conversion to base N
  Digit = (Input) % (N)
  Input = (Input) / (N)
  Repeat until Input is exhausted (zero) writing digits ‘right to left’.
Or, left to right.
  Digit = (Input) / (N^ position)
  Input = (input) – Digit * (N ^ position)
Picking arbitrary digits?
Notes: Integer division “floors” or “truncates” the result back to an integer automatically
i = index of digit, 0 based.
d = (input / r^i) % r
-- Right to left script:
def binary(input_num, n):
bin = []
while (input_num > 0):
d = input_num % n
i = input_num / n
bin.insert(0,d)
input_num = i
return bin
print binary(4, 2)

## Slide 12: Easy Radix Conversion
When converting between bases that are powers of each other, the division operation becomes trivial.
  1 Hex digit = 4 binary digits (bits)
  3 Binary digits = 1 Octal digit (octets)
  1 R=r^n digit = n R=r digits
Example
b100111111011101011011
Notes: Do the “hand trick” for this one on the board.
Write random string of zeros and ones. Move hands to only show 4 bits at a time, stress that this is equivalent to the divide / modulo operators. Draw 4 bit chunk boundaries, parse to hex quickly.

## Slide 13: Easy Radix Conversion Trick
b100111111011101011011
b100 111 111 011 101 011 011
o 4 7 7 3 5 3 3
To Hex
b 1 0011 1111 0111 0101 1011
h 1 3 F 7 5 B

## Slide 14: BOARDS
Truth Table for Binary Adder
  Inputs: A, B, Carry In
  Output: Sum, Carry Out
Convert to Decimal
  b101100 o325 hE32
Convert 79 from Decimal to Bin, Oct, and Hex
20123 + 11123 + 2223 + 10123 = ???9
Multiply d29 by hf
  In Binary
  In Quaternary (R=4)
  In Hex
Pay close attention to the carry logic…
  When do you have to carry two places over? Try adding one more row in the ternary problem.
Notes: 44, 213, 3634
b100 1111, o117, h4F
185 base 9, 158 base 10
Binary Multiplication will require several double carries!
Binary and quaternary can be done on the boards relatively easily. Hex requires a calculator.
1 1011 0011 <- Watch the “carry the 2”, which is actually a “carry the 10” !
1 23 03
1b3

## Slide 15: Additional Radix Carrying
Food for Thought -
A Radix R adder uses a single carry out digit for 11 inputs.
One of those is used by the carry in.
That leaves us with 10 (R) inputs.
  In Binary, this is sad.
R
Notes: 11 is in base R!

## Slide 16: Negative Numbers
Three Possible Options:
Sign / Magnitude
  One bit denotes sign, rest denotes magnitude
1’s Complement (Inverse)
  Negative is the inverse of Positive
2’s Complement
  Negative is the complement w.r.t. R^N (2^N)
Notes: Inverse – 0 9, 1 8, 2 7, 3 6, 4 5
Complement – 1 9, 2 8, 3 7, 4 6

## Slide 17: Negative Numbers
Three Possible Options:
Sign / Magnitude
  One bit denotes sign, rest denotes magnitude
(R-1)’s Complement (Inverse)
  Negative and Positive add to (R^N)-1
R’s Complement
  Negative and Positive add to R^N
Notes: Complement : add to get to a number
R-1’s complement in base 5:
0 4
1 3
2 2
3 1
R’s complement in base 5
0 5  Can’t actually be done
1 4
2 3
3 2
4 1

## Slide 18: R’s Compliment
A + -A = R^N
Example: R = 10, N=1, Calculate 6+(-3)=3
  Find Representation for -3:
    R^N – A = -A
    10^1 – 3 = 7
  Calculate with addition:
    6+7 = 13
  Truncate to N=1
    13  3
  Adding 7 is like subtracting 3, but carry magic.
Truncation is the key
  What is -3 in R=10, N=3?
Notes: Hint at N>1
997

## Slide 19: 2’s Compliment
Shortcut: Invert, add 1.
2: b0010
: b1101
: b1110
-2: b1110
Note: ‘Extra’ negative number!
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
Notes: Invert in Decimal:
1->9 2->8 3->6 etc…
Show that the trick still works.

## Slide 20: Addition in Two’s Complement
1 1 1 0 ( -2)
+ 0 1 0 0 (+4)
0 0 1 0 (+2)
+ 0 1 0 0 (+4)
1 1 1 0 (-2)
+ 1 1 0 0 (-4)
0 0 1 0 (+2)
+ 1 1 0 0 ( -4)
Notes: Do together
0110 (1)1010
1110 (1)1110

## Slide 21: Addition in Two’s Complement
1 1 1 0 ( -2)
+ 0 1 0 0 (+4)
(1) 0 0 1 0
0 0 1 0 (+2)
+ 0 1 0 0 (+4)
0 1 1 0
1 1 1 0 (-2)
+ 1 1 0 0 (-4)
(1) 1 0 1 0
0 0 1 0 (+2)
+ 1 1 0 0 ( -4)
1 1 1 0
1
1
1
1
Notes: Do together
0110 (1)1010
1110 (1)1110

## Slide 22: Subtraction in Two’s Complement
A - B = A + (-B) = A + B̅ + 1
0010 - 0110
1011 - 1001
1011 - 0001
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
Notes: Do on Boards

## Slide 23: Sign Extension in R’s Compliment
Positive numbers
  Left pad with 0
Negative Numbers
  Left Pad with (R-1)s
2’s Compliment
  Left Duplicate the most significant (sign) bit.
Notes: Do quick example on board

## Slide 24: Overflows in Two’s Complement
Add two positive numbers to get a negative number
or two negative numbers to get a positive number
5 + 3 = -8
-7 - 2 = +7
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
Notes: Saturation = make dotted line “solid”, saturating to max pos or min neg

## Slide 25: Overflow Detection in 2’s Complement
5
3
-8
0 1 0 1
0 0 1 1
-7
-2
7
1 0 0 1
1 1 1 0
5
2
7
0 1 0 1
0 0 1 0
-3
-5
-8
1 1 0 1
1 0 1 1
Overflow
Overflow
No overflow
No overflow
Overflow when carry in to the most significant column does not equal carry out

## Slide 26: Fixed Point Numbers
Integer scaled by a fixed factor.
Fixed number of digits before and after the radix point.
  b0101.1100 = 2^2 + 2^0 + 2^-1 + 2^-2 = 5.75
IQ Notation
  I8Q24 Signed, 8 bits before, 24 bits after
  U16Q16 Unsigned, 16 before, 16 after
Notes: Show maximum possible value on board.
I8Q24 = 2^(8-1) – 2^-24
U16Q16 = 2^16-2^-16
Link back to number circle – it is I4. Show that its max value is 2^(4-1)-2^0

## Slide 27: Fixed Point Options

## Slide 28: MOAR BOARDS
For Each:
  What IQ should you use?
  Convert to binary IQ
  Do the math in binary
    Maintaining decimal place
    Fixing it later
3.375 – 1.5
4.125 * 2.25
3 * -0.5
Notes: 1.875 = +1.111
9.28125
Sign extension is the key here.
Feels natural to do 3*-.5 as |3|*|.5| with sign correction later, like sign magnitude notation.

## Slide 29: Notes for MP0
Teams of 3 or 4
  Your choice of team mates
  Yes, across sections
Pairs of teams will share an FPGA