## Slide 1: b0100 Floating Point
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)
http://docs.oracle.com/cd/E19957-01/806-3568/ncg_goldberg.html

## Slide 3: Today
Better IQ representation example
Review Multiplication in Fixed Point
Signed/Unsigned and Multiplication
Invent Floating Point Numbers
Letters: Nicholas Eyre, Yun-Hsin Chen

## Slide 4: Final Exam
You are writing your own Final Exams
Details are posted on the Wiki
Today’s board work should help you get in the mood.
Main Point: Collaborative material review
Anti Main Point: Angst

## Slide 5: Better IQ example

## Slide 6: IQ Multiplication
We ended last class with 3.0 *-0.5 in binary.
3 -> 00110000 I4Q4
-0.5 -> 11111000 I4Q4
-1.5 -> 11101000 I4Q4…?

## Slide 7: Its just like Algebra, right?
  11111000 -0.5 in I4Q4
  * 00110000 3.0 in I4Q4
  00000000
  00000000
  00000000
  00000000
  11111000
  11111000
  00000000
  00000000
  0010111010000000 ??? In I?Q?

## Slide 8: Its just like Algebra, right?
  1111.1000 -0.5 in I4Q4
  * 0011.0000 3.0 in I4Q4
  .00000000
  0.0000000
  00.000000
  000.00000
  1111.1000
  11111.000
  000000.00
  0000000.0
  00101110.10000000 46.5 In I8Q8

## Slide 9: Its just like Algebra, right?
  1111.1000 -0.5 in I4Q4
  * 0011.0000 3.0 in I4Q4
  .00000000
  0.0000000
  00.000000
  000.00000
  1111.1000
  11111.000
  000000.00
  0000000.0
  00101110.10000000 46.5 In I8Q8
Correct!
Incorrect?

## Slide 10: Its just like Algebra, right?
  1111.1000 -0.5 in I4Q4
  * 0011.0000 3.0 in I4Q4
  0000000.00000000
  0000000.00000000
  0000000.00000000
  0000000.00000000
  1111111.10000000  I8Q8!!
  1111111.00000000
  0000000.00000000
  0000000.00000000
  11111110.10000000 -1.5 In I8Q8

## Slide 11: Negative Second Operand?
  01.11 I2Q2 d1.75
  * 11.10 I2Q2 –d0.50
  .0000
  0.111
  01.11
  011.1
  0111.
  0111 .
  0111 .
  0111 .
  0111 .
  01101111.0010 I4Q4 -d0.875

## Slide 12: Negative Second Operand?
  01.11 I2Q2 d1.75
  * 11.10 I2Q2 –d0.50
  .0000
  0.111
  01.11
  011.1
  0111.  From sign extension!
  0111 .
  0111 .
  0111 .
  0111 .  No effect on output
  01101111.0010 I4Q4 -d0.875
Notes: Sign extend your second operand vertically until it doesn’t affect the output.
The first four bits are unaffected by sign extension.
The next four need to be valid, which prompts the sign extension vertically.
The last four are unnecessary, and are there just to show the ‘debris’ from the calculation

## Slide 13: Observations
The product is wider than the inputs
  InQx*ImQy=I(n+m)Q(x+y)
Sign extend the inner terms and the multiplicand

## Slide 14: Side Note…
The wikipedia article on binary multipliers is awful.
Prove and rewrite the “More advanced approach: signed integers” section instead of any two homework assignments this semester.

## Slide 15: Implications
3 categories of integer (or IQ) multiply instructions:
  MUL N*N->N, sign agnostic (only for Q=0)
  SMUL N*N->2N, signed
  UMUL N*N->2N, unsigned
Multiplication uses ever increasing amounts of memory….?
Notes: The N*N->N sign agnosticism is a neat ‘trick’. I believe it is valid for the first bits up to the lesser of the two input lengths. E.g. I13*I33 are sign agnostic for 13 bits.

## Slide 16: Operations with outputs > inputs
Addition uses 1 extra bit
  I4+I4 -> I5
  [-8,7]+[-8,7]  [-16,14]
Multiplication needs twice as many bits (-1)
  I4*I4 -> I7
  [-8,7]*[-8,7]  [-64,56]
Notes: Minimum format to represent most positive value:
Log2((R^(N-1)-1)^2)+1
~~2(N-1)+1= 2N-1

## Slide 17: Finite Memory
We can not expand every time.
Usually, output format is input format.
LSBs dropped are lost precision
  Always a little bad
MSBs dropped are occasional catastrophes.
  Totally fine or absolutely terrible
  Overflow Errors

## Slide 18: How to Handle?
Overflow
  Catastrophic value change
Saturate
  Wrong, but closer than Overflow
Make the programmer deal with it
  They know their needs better than we do

## Slide 19: Precision vs Max Magnitude
Humans handle this with scientific notation.
  Lose precision to handle memory constraints
  Like choosing IQ format after each calculation(ish)
1.234*10^2
Significand * R^Exponent
Significand in I?Q?, Exponent in I?

## Slide 20: Lets Design Binary Scientific Notation
Need to store:
  Sign
  Exponent
  Signficand
Nice to be able to:
  Fit in memory conveniently
  Sort easily
  Accommodate bad things happening

## Slide 21: Attempt 1
Store Significand in 2’s complement I1Q22
Store Exponent in 2’s complement I9
Most Positive:
Smallest Positive:
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Significand
exponent

## Slide 22: Attempt 1
Store Significand in 2’s complement I1Q22
Store Exponent in 2’s complement I9
Store Decimal -3.5
  Exponent = d1 = b000000001
  Significand = -d0.875 = b1.0011111…
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Significand
exponent
Notes: 0.11100000
1.00011111
1.00100000

## Slide 23: Attempt 1
Store Significand in 2’s complement I1Q22
Store Exponent in 2’s complement I9
Store Decimal -3.5
  Exponent = d2 = b000000010
  Significand = -d0.875 = b1.0011111…
  Hex: 0x004FFFFF
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
10011111111111111111111
0 0 0 0 0 0 0 1 0
Notes: 0.11100000
1.00011111
1.00100000

## Slide 24: Attempt 1
Store Signficand in 2’s complement I1Q22
Store Exponent in 2’s complement I9
Does not sort well
  Bit #22 is the sign bit?!
Many duplicated representations
  .5*2^0 = .25*2^1
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
Significand
exponent

## Slide 25: Renormalization
We use 0<= Significand < R
  12.34*10^5 looks funny – it is in U2Q2(R10)
  Scientific Notation is U1Q?R10.
What is Engineering Notation?
  123.456*10^6
TLDR: Pick a significand format, stick with it
Notes: U1Q?R1000

## Slide 26: Exponent Format
Could use 2’s compliment.
  But that doesn’t sort well
Use ‘biased’ notation instead.
  Signed value ‘biased’ to be unsigned.
  Biased means add a fixed value
  Most negative number becomes 0.
Makes sorting floats easy!

## Slide 27: IEEE-754 Single Precision Float
Floating Point (Float) = (-1)s * (1.fraction) * 2(exponent-127)
Alternative Name: binary32
Significand = 1.fraction
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
fraction
s
exponent
1 bit 8 bits 23 bits

## Slide 28: IEEE-754 Single Precision Float
Floating Point (Float) = (-1)s * (1.significand) * 2(exponent-127)
Record Sign bit
Convert Significand to U1Q23
  Track changes to Exponent!
Drop the MSB of Significand, record the rest
  Significand = leading one + Fraction
Bias Exponent by +127, record
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
Notes: Do one on the board:
2.25 -> 10.01 *2^0 -> 1.001 * 2^1
Sign = 0. Expont = 1+127 = 128 = b10000000. Significand = .001
x40100000

## Slide 29: Multiplication in Floating Point
Easy!
Multiply Significands, Add Exponents
5*10^2 * 4*10^4 = (5*4)*10^(2+4)
= 20*10^6 -> 2.0*10^7

## Slide 30: Addition in Floating Point
Almost Easy!
Operands must have same exponent
  Normalize to most positive exponent
9.8*10^13 + 4*10^12 -> (9.8+0.4)*10^13
  = 10.2*10^13 -> 1.02*10^14

## Slide 31: IEEE-754 Single Precision Board Work
Floating Point (Float) = (-1)s * (1.fraction) * 2(exponent-127)
Convert to fp hex:
  0.75 -10 .3
Convert from fp: 0x40410100 0xC0FFEE00
Find & prove flaws in my original float design
  Sorting, Packing efficiency, others?
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
fraction
s
exponent
Notes: 3F400000 C1200000 3E99999A 3F333333
3.015686 -7.9978027
http://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 32: Special Cases
Exponent b00000000
  Fraction = 0: Zero
  Fraction!=0: Subnormal
Exponent b11111111
  Fraction = 0: Infinity
  Fraction!= 0: Not a Number

## Slide 33: When things go wrong
Overflow – it too big
Underflow – it too small
Non-Associative – Can’t reorder operations
  Still commutative
  Order determines end precision!
Humans like R10, but it is not representable

## Slide 34: When things go wrong
Catastrophic Cancellation
  Loss of precision from subtracting close numbers
    A-B = C when |A| >>> |C|, C will be imprecise
Comparison Failures
  float f = 3.0/7.0;
  bool b = f == 3.0/7.0;
http://docs.oracle.com/cd/E19957-01/806-3568/ncg_goldberg.html

## Slide 35: Break my code!
float mean(float nums[])
{
float total = 0;
for(int i=0;i<length(nums);i++)
{
total += nums[i];
}
return total/length(nums);
}
Notes: Length(nums) is very large. How large? Hint, 2^24…

## Slide 36: If you remember nothing else…
Precision: ~7 decimal digits
Relative Error is constant, absolute error varies
Exponent Range: 10^38 10^-38
Represent all integers up to 2^24
Sortable with integer operations
Notes: Relative / absolute error – nano tech vs astronomy

## Slide 37: When you are debugging:
Zero is 0x00000000
Infinity is h7F800000, -Infinity is hFF800000
NaN: h7FC00000 is most common I’ve seen.
  Other NaNs exist, ish.

## Slide 38: IEEE-754 Double Precision Float
AKA Binary64
11 exponent bits, 52 explicit significand bits
~16 decimal digits, 10^308 10^-308
All Integers to 2^53
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand (continued)

## Slide 39: Clever Hacks or Total BS?
Using integer operations on floats
union intfloat { int i; float f; } x;
  Access like an integer with x.i;
  Access like a float with x.f;
What does this do:
  x.i = x.i | 0x80000000;
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
Notes: Sets bit 31 = makes it represent a negative number

## Slide 40: Story Time
These ‘clever hacks’ are terrible on x86 arch
  “Separate” floating point unit
  Forces conversion
  Doesn’t take advantage of hardware
These ‘clever hacks’ are terrible in general
  Corner cases
  Legibility

## Slide 41: Clever Hacks or Total BS?
Float multiply by -1
Float divide by 8 using integer subtraction
Rounded log base 2 of a float
Notes: ^0x80000000
Subtract 3 from the exponent (shift 3 over the right number of bits and subtract)
Just grab the exponent part and unbias it

## Slide 42: Create your own Pain
Create your own math problems that highlight the basic problems with floating point math.
You can use decimal or binary
  Pick a format. 2 exponent digits, 7 significand?