## Slide 1: b0111 Growth and Performance
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Acknowledgements
Alyssa Bawgus
Orion Taylor

## Slide 3: Today
Growth – Size
Homework and Lab Assigned
Verilog Tricks
Computational Performance

## Slide 4: Size in Silicon
Physical Area drives manufacturing cost
  # Chips per silicon wafer
Number of inputs drives gate size
  Two transistors per input
  Slightly worse than linear growth
Total Gate Inputs  Rough Cost Estimate

## Slide 5: Decoder Growth
For a decoder with S select bits and D outputs
  D = 2^S
Need
  S Inverters
  D AND Gates with S inputs
Total Size:

## Slide 6: Decoder Growth Review
For a decoder with S select bits and D outputs
  D = 2^S
Need
  S Inverters (S)
  D AND Gates with S inputs (DS)
Total Size: DS+S = +1)=(D+1)log2(D)

## Slide 7: Look Up Table w/Decoder

## Slide 8: Look Up Table w/Decoder

## Slide 9: Growth Characteristics
This has 12 Gate Inputs
  4 AND2 (8)
  1 OR4 (4)
Per decode line:
  1 AND2
  1 input of the OR
(#Decode Lines)*3

## Slide 10: LUT Growth Review
For a LUT with Depth D and Output Width W
Need
  1 Decoder
  W Output Structures
Total Size:

## Slide 11: LUT Growth Review
For a LUT with Depth D and Output Width W
Need
  1 Decoder (D+1)log2(D)
  W Output Structures W(3D)
  Total Size: (D+1)log2(D) + W(3D)

## Slide 12: Adder Comparison
LUT for 32bit + 32bit = 32bit addition
  S = (32+32) = 64
  W = 32
  D=2^S = 18446744073709551616
Total Size = (D+1)log2(D) + W(3D)
  2951479051793528258624
Notes: This is calculated for a LUT with modifiable inputs. If the inputs are hardcoded it changes the “3” to about a half. Not a huge impact for large D.

## Slide 13: Adder Comparison
LUT for 32bit + 32bit = 32bit addition
  Size
Chained Full Adder
  9 NAND2 Gates per bit
  Size = 32 * 18 = 576
Apollo Guidance Computer:
  4100 NOR3 ( 12,300 gate inputs)

## Slide 14: Homework and Labs
HW3 – Due this Thursday
  Simple review of CompArch math
  Alone
MP1 – Due next Thursday
  Create and test an ALU
  In groups

## Slide 15: Major Goals
Understand propagation delay
Finalize mastery of Structural Verilog
Effective Testing through:
  Design Reuse
  Test set reduction (Orthoganality)

## Slide 16: Minor Goals
Optimized Structures
  Alternative Adders?
    Carry Look Ahead / Carry Select / Kogge Stone
  ALU shrinkage?
    How small can you go?
    Speed penalty?
These are not worth any grade points
  Only do them if you’re interested

## Slide 17: Hint: `define
Use `define syntax to avoid magic numbers
      `define ADD 3'd0
      `define SUB 3'd1
      `define XOR 3'd2
      `define SLT 3'd3
Makes for more readable code

## Slide 18: Hint: LUT
Explicitly break out control logic to make a LUT
Design Flow:
  Create main structure, ignore control logic
  Label all control logics
  Make a table and assign values per Operation
  Generate LUT from this table
  Delay unnecessary decisions as long as possible
Notes: On Board, run following:
Draw Adder, mux, a couple logic gates
Don’t label anything
Add inv mux combos on B input and R output

## Slide 19: Hint: LUT
Use human words:
  Describe Intent
  Less “Magic”
  Teammates will thank you
Late Bind
  Using `define?
  Using enum? (Nope)
  Hardcoding?
Operation | Mux | InvB | InvOutput
ADD | ADDSUB | NO | NO
SUB | ADDSUB | YES | NO
AND | AND | NO | NO
NOR | OR | NO | YES
Operation | Mux | InvB | InvOutput
ADD | MUX_ADD | 0 | 0
SUB | MUX_ADD | 1 | 0
AND | MUX_AND | 0 | 0
NOR | MUX_OR | 0 | 1

## Slide 20: Hint: LUT
Behavioral only allowed for this LUT
  Just to save on repetitive boolean logic practice
Don’t forget to add delays!
  You know what the underlying structure is

## Slide 21: Hint: Generate
This lab can get repetitive
  Instantiating 32 instances of everything
Good Hierarchical design helps
  e.g. Bitslice
Generate does some of this for you
generate
genvar i;
for (index = 0;
index<32;
index = index + 1)
begin
// Repeated Code
end
endgenerate

## Slide 22: Hint: Param
Modules can have parameters
  One design, many variants
  Must be known at synthesis time
Test a smaller variant
  Combine Generate and Param
  Exhaustively test a 4 bit ALU?
    Be careful! What did you leave untested?

## Slide 24: Computer “Performance”
MIPS (Million Instructions Per Second) vs. MHz (Million Cycles Per Second)
Throughput (jobs/seconds) vs. Latency (time to complete a job)
Measuring, Metrics, Evaluation – what is “best”?
The PowerBook G4 outguns Pentium
III-based notebooks by up to 30 percent.*
* Based on Adobe Photoshop tests
comparing a 500MHz PowerBook G4 to
850MHz Pentium III-based portable computers
3.09 GHz
Pentium 4
Hyper
Pipelined
Technology

## Slide 25: Performance Example: Planes
Airplane | Passenger Capacity | Cruising Range (miles) | Cruising Speed (mph) | Passenger Throughput (passengermile/hour)
Boeing 777 | 375 | 4630 | 610 | 228,750
Boeing 747 | 470 | 4150 | 610 | 286,700
Concorde | 132 | 4000 | 1350 | 178,200
Douglas DC8 | 146 | 8720 | 544 | 79,424
Which is the “best” plane?
  Which gets one passenger to the destination first?
  Which moves the most passengers?
  Which goes the furthest?
Which is the “speediest” plane (between Seattle and NY)?
  Latency: how fast is one person moved?
  Throughput: number of people per time moved?

## Slide 26: Computer Performance
Primary goal: execution time (time from program start to program completion)
To compare machines, we say “X is n times faster than Y”
Example: Machine Orange and Grape run a program Orange takes 5 seconds, Grape takes 10 seconds
Orange is _____ times faster than Grape

## Slide 27: Execution Time
Elapsed Time
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes
CPU time
  doesn't count I/O or time spent running other programs
  can be broken up into system time, and user time
Example: Unix “time” command fpga.olin.edu> time javac CircuitViewer.java 3.370u 0.570s 0:12.44 31.6%
Our focus: user CPU time
  time spent executing the lines of code that are "in" our program

## Slide 28: CPU Time
Application example: A program takes 10 seconds on computer Orange, with a 400MHz clock. Our design team is developing a machine Grape with a much higher clock rate, but it will require 1.2 times as many clock cycles. If we want to be able to run the program in 6 second, how fast must the clock rate be?
CPU execution time
for a program
CPU clock cycles
for a program
Clock period
=
*
CPU execution time
for a program
CPU clock cycles
for a program
1
Clock rate
=
*

## Slide 29: CPI
How do the # of instructions in a program relate to the execution time?
CPU clock cycles
for a program
Instructions
for a program
Average Clock
Cycles per Instruction
(CPI)
=
*
CPU execution time
for a program
Instructions
for a program
=
*
1
Clock rate
*
CPI

## Slide 30: CPI Example
Suppose we have two implementations of the same instruction set (ISA).
For some program Machine A:
  clock cycle time of 10 ns
  CPI of 2.0 Machine B:
  clock cycle time of 20 ns
  CPI of 1.2
What machine is faster for this program, and by how much?
Notes: A = 20ns / instruction
B = 24ns / instruction

## Slide 31: Computing CPI
Different types of instructions can take very different amounts of cycles
Memory accesses, integer math, floating point, control flow
Instruction Type | Type Cycles | Type Frequency | Cycles * Freq
ALU | 1 | 50% | 
Load | 5 | 20% | 
Store | 3 | 10% | 
Branch | 2 | 20% | 
 |  | CPI: | 
Notes: CPI = .5 + 1 + .3 + .4 = 2.2

## Slide 32: Computing CPI
Different types of instructions can take very different amounts of cycles
Memory accesses, integer math, floating point, control flow
Instruction Type | Type Cycles | Type Frequency | Cycles * Freq
ALU | 1 | 50% | .5
Load | 5 | 20% | 1
Store | 3 | 10% | .3
Branch | 2 | 20% | .4
 |  | CPI: | 2.2
Notes: CPI = .5 + 1 + .3 + .4 = 2.2

## Slide 33: CPI & Processor Tradeoffs
How much faster would the machine be if:
A data cache reduced the average load time to 2 cycles?
Branch prediction shaved a cycle off the branch time?
Two ALU instructions could be executed at once?
Instruction Type | Type Cycles | Type Frequency
ALU | 1 | 50%
Load | 5 | 20%
Store | 3 | 10%
Branch | 2 | 20%
Notes: CPI = .5 + .4 + .3 + .4 = 1.6 -> 2.2 / 1.6 = 1.375x
CPI = .5 + 1 + .3 + .2 = 2.0 -> 2.2 / 2.0 = 1.1x
CPI = .25 + 1 + .3 + .4 = 1.95 -> 2.2 / 1.95 = 1.22x

## Slide 34: Warning 1: Amdahl’s Law
The impact of a performance improvement is limited by what is NOT improved:
Example: Assume a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to speed up multiply to make the program run 4 times faster?
5 times faster?
Execution time
after improvement
Execution time
of unaffected
=
*
1
Amount of improvement
+
Execution time affected
Notes: 100/4 = 25
25 – 20 = 5
80/5 = 16 times faster
INFINITY

## Slide 35: Warning 2: MIPs, MHz  Performance
Higher MHz (clock rate) doesn’t always mean better CPU
Orange computer: 1000 MHz, CPI: 2.5, 1 billion instruction program
Grape computer: 500MHz, CPI: 1.1, 1 billion instruction program
Higher MIPs (million instructions per second) doesn’t always mean better CPU
1 MHz machine, with two different compilers/instruction sets
Compiler A on program X: 10M ALU, 1M Load
Compiler B on program X: 5M ALU, 1.5M Load
  Execution Time: A ____ B ____
  MIPS: A ____ B ____
Instruction Type | Type Cycles
ALU | 1
Load | 5
Store | 3
Branch | 2
Notes: 15M cycles / 1MHz = 1.5 seconds
5+7.5 = 12.5M cycles = 1.25 seconds
MIPS
1.5 seconds / 1.1M instructions = 7.3MIPS
1.25 s / 6.5M instr = 5.2MIPS

## Slide 36: Processor Performance Summary
Machine performance:
Better performance:
_____ number of instructions to implement computations
_____ CPI
_____ Clock rate
Improving performance must balance each constraint
Example: RISC vs. CISC
CPU execution time
for a program
Instructions
for a program
=
*
1
Clock rate
*
CPI
Notes: Lower is better
Lower is better
Higher is better

## Slide 37: Common Comparison Metrics
Whetstone MWIPS
  Specific program profile stressing Floating Point
  Minimal memory stress
  AM386 developed 5.68MWIPS @ 40MHz (1991)
  I7 930 develops 2496MWIPS @ 2800MHz

## Slide 38: Common Comparison Metrics
Dhrystone
  Specific program stressing integer and string ops
LINPACK
  Solve linear equation Ax=b
  Common calculation in engineering

## Slide 39: Common Comparison Metrics: The Gibson Mix
Gibson Mix
Fixed Point Add/Subtract | 0.330
Fixed Point Multiply | 0.006
Fixed Point Divide | 0.002
Branch | 0.065
Compare | 0.040
Transfer 8 characters | 0.175
Shift | 0.046
Logical | 0.017
Modification | 0.190
Floating Point Add | 0.073
Floating Point Multiply | 0.040
Floating Point Divide | 0.016

## Slide 40: Remaining Time?
Begin Homework