## Slide 1: b10100 Numerical Accuracy
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)

## Slide 3: Today
Fast = Expensive
Slow = Cheap
Computer Architecture = Best of Both Worlds
Because we are awesome

## Slide 4: Recap
So far, we have three types of memory:
  Registers (between pipeline stages)
  Register File
  Giant Magic Black Box for lw and sw
Inside the box is CompArch’s favorite thing:
  More Black Boxes

## Slide 5: Recap
So far, we have three types of memory:
  Registers (between pipeline stages)
  Register File
  Giant Magic Black Box for lw and sw
Inside the box is CompArch’s favorite thing:
  More Black Boxes
  WITH KNOBS ON THEM WE CAN ADJUST

## Slide 6: Cost vs Speed
Faster Memories are more expensive per bit
  Slow and Expensive technologies are phased out
  Expensive means chip area, which means $$$
Technology | Access Time 2004 | $/GB in 2004 | $/GB in 2013
SRAM | 0.5-5 ns | $4000-$10,000 | $1400
DRAM | 50-70 ns | $100-$200 | >$3 (Nov ‘12) >$6 (Nov ‘13)
Disk (HDD) | (5-20)x106ns | $0.50-$2 | >$.05
Disk (SSD) | >100ns |  | $0.60

## Slide 7: Static Random Access Memory
Like a register file, but:
  Only one Port (unified read/write)
  Many more words (Deeper)
  Several of you accidentally invented it
Different Cell Construction
  Smaller than a D-Flip Flop
Different Word Select Construction
  Much fancier to allow for poorer cells
  Hooray for VLSI

## Slide 8: SRAM Cell
M1-M3 store bit weakly
Word Line accesses cell
  Open M5, M6
Bit Lines
  Read bit (weak signal)
  Write bit (strong signal)
Squint to see SR latch!

## Slide 9: DRAM Cell
Capacitor stores bit
  For a while
  Must be “refreshed”
FET controls access
Smaller than SRAM
Slower than SRAM
http://www.emrl.de/imagesArticles/DRAM_Emulation_Fig2.jpg
Notes: On 65 nanometer process:
SRAM takes .57um^2
DRAM takes .12um^2

## Slide 10: Technology Trends
Processor-DRAM Memory Gap (latency)
µProc
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Time
“Moore’s Law”
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 11: The Problem
The Von Neumann Bottleneck
  Logic gets faster
  Memory capacity gets larger
  Memory speed is not keeping up with logic
How do we get the full Daft Punk experience?
  Faster, Bigger, Cheaper, Stronger?

## Slide 12: Fast, Big, Cheap: Pick 3
Design Philosophy
  Use a hybrid approach that uses aspects of both
  Lots of Slow’n’Cheap
  Small amount of Fast’n’Costly
“Cache”
  Make the common case fast
  Keep frequently used things in a small amount of fast/expensive memory

## Slide 13: The Solution
By taking advantage of the principle of locality:
  Provide as much memory as is available in the cheapest technology.
  Provide access at the speed offered by the fastest technology.
Control
Datapath
Secondary
Storage
(Disk)
Processor
Registers
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
On-Chip
Cache
Name Register Cache Main Memory Disk Memory
Speed <1ns <10ns 60ns 10 ms Size 100 Bs KBs MBs GBs

## Slide 14: Cache Terminology
Hit: Data appears in that level
  Hit rate – percent of accesses hitting in that level
  Hit time – Time to access this level
    Hit time = Access time + Time to determine hit/miss
Miss: Data does not appear in that level and must be fetched from lower level
  Miss rate – percent of misses at that level = (1 – hit rate)
  Miss penalty – Overhead in getting data from a lower level
    Miss penalty = Lower level access time + Replacement time + Time to deliver to processor
Miss penalty is usually MUCH larger than the hit time

## Slide 15: Cache Access Time
Average access time
  Access time = (hit time) + (miss penalty)x(miss rate)
  Want high hit rate & low hit time, since miss penalty is large
Average Memory Access Time (AMAT)
  Apply average access time to entire hierarchy.

## Slide 16: Handling A Cache Miss
Data Miss
  Stall the pipeline (freeze following instructions)
  Instruct memory to perform a read and wait
  Return the result from memory and allow the pipeline to continue
Instruction Miss
  Send the original PC to the memory
  Instruct memory to perform a read and wait (no write enables)
  Write the result to the appropriate cache line
  Restart the instruction

## Slide 17: Cache Access Time Example
Note: Numbers are local hit rates – the ratio of access that go to that cache that hit (remember, higher levels filter accesses to lower levels)
Level | Hit Time | Hit Rate | Access Time
L1 | 1 cycle | 95% | 
L2 | 10 cycles | 90% | 
Main Memory | 50 cycles | 99% | 
Disk | 50,000 cycles | 100% | 

## Slide 18: Cache Access Time Example
Note: Numbers are local hit rates – the ratio of access that go to that cache that hit (remember, higher levels filter accesses to lower levels)
Level | Hit Time | Hit Rate | Access Time
L1 | 1 cycle | 95% | 
L2 | 10 cycles | 90% | 
Main Memory | 50 cycles | 99% | 
Disk | 50,000 cycles | 100% | 50,000

## Slide 19: Cache Access Time Example
Note: Numbers are local hit rates – the ratio of access that go to that cache that hit (remember, higher levels filter accesses to lower levels)
Level | Hit Time | Hit Rate | Access Time
L1 | 1 cycle | 95% | 
L2 | 10 cycles | 90% | 
Main Memory | 50 cycles | 99% | 50 + .01 * 50000 = 550
Disk | 50,000 cycles | 100% | 50,000

## Slide 20: Cache Access Time Example
Note: Numbers are local hit rates – the ratio of access that go to that cache that hit (remember, higher levels filter accesses to lower levels)
Level | Hit Time | Hit Rate | Access Time
L1 | 1 cycle | 95% | 
L2 | 10 cycles | 90% | 10 + .1 * 550 = 65
Main Memory | 50 cycles | 99% | 50 + .01 * 50000 = 550
Disk | 50,000 cycles | 100% | 50,000

## Slide 21: Cache Access Time Example
Note: Numbers are local hit rates – the ratio of access that go to that cache that hit (remember, higher levels filter accesses to lower levels)
Level | Hit Time | Hit Rate | Access Time
L1 | 1 cycle | 95% | 1 + .05 * 65 = 4.25
L2 | 10 cycles | 90% | 10 + .1 * 550 = 65
Main Memory | 50 cycles | 99% | 50 + .01 * 50000 = 550
Disk | 50,000 cycles | 100% | 50,000

## Slide 22: How do we get those Hit Rates?
There ain’t no such thing as a free lunch
  If access was totally random, we’d be hosed
  But we have knowledge a priori about programs
Locality
  Temporal Locality – If an item has been accessed recently, it will tend to be accessed again soon
  Spatial Locality – If an item has been accessed recently, nearby items will tend to be accessed soon

## Slide 23: Example
What does this code do?
What type(s) of locality does it have?
char *index = string; while (*index != 0) { /* C strings end in 0 */ if (*index >= ‘a’ && *index <= ‘z’) *index = *index +(‘A’ - ‘a’); index++; }
Notes: Temporal Locality: *index points to the same char several times per loop. Hopefully this compiles to a single load!
Spatial Locality: index increments by 1 each loop

## Slide 24: Exploiting Locality
Temporal locality
  Keep more recently accessed items closer to the processor
  When we must evict items to make room for new ones, attempt to keep more recently accessed items
Spatial locality
  Move blocks consisting of multiple contiguous words to upper level

## Slide 25: Basic Cache Design
2^n Blocks of Data 2^M bytes wide
Tag indicates what block is being stored
0
1
2
3
4
5
6
7
2n-1
…
…
…
…
Valid Bit
Tag (Address)
Data
…
…
…

## Slide 26: Whose Line is it, Anyway?
How do we map System Memory into Cache?
Idea One: Direct Mapping
  Each address maps to a single cache line
  Lower M bits are address within a block
  Next N bits are the cache line address
  Remainder are the address Tag
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
N bits
M bits
Address Tag
Notes: 64 byte line size
32kbyte total size

## Slide 27: Direct Mapped Cache
0
1
2
3
4
5
6
7
8
9
A
B
C
E
D
F
0
1
2
3
Cache Address

## Slide 28: Direct Mapped Cache
0
1
2
3
4
5
6
7
8
9
A
B
C
E
D
F
0
1
2
3
Cache Address

## Slide 29: Direct Mapped Cache
0
1
2
3
4
5
6
7
8
9
A
B
C
E
D
F
0
1
2
3
Cache Address
M[C]
Tag
C / 4 = 3

## Slide 30: Cache Access Example
Assume 4 byte cache (N=2, M=0)
Access pattern:
00001
00110
00001
11010
00110
0
1
2
3
Valid Bit
Tag
Data

## Slide 31: Cache Access Example
Assume 4 byte cache (N=2, M=0)
Access pattern:
000 01
001 10
000 01
110 10
001 10
0
1
2
3
Valid Bit
Tag
Data
M[00001]
000
1
0
0
0

## Slide 32: Cache Access Example
Assume 4 byte cache (N=2, M=0)
Access pattern:
000 01
001 10
000 01
110 10
001 10
0
1
2
3
Valid Bit
Tag
Data
M[00001]
000
1
1
0
0
M[00110]
001

## Slide 33: Cache Access Example
Assume 4 byte cache (N=2, M=0)
Access pattern:
000 01
001 10
000 01
110 10
001 10
0
1
2
3
Valid Bit
Tag
Data
M[00001]
000
1
1
0
0
M[00110]
001

## Slide 34: Cache Access Example
Assume 4 byte cache (N=2, M=0)
Access pattern:
000 01
001 10
000 01
110 10
001 10
0
1
2
3
Valid Bit
Tag
Data
M[00001]
000
1
1
0
0
M[00110]
001 != 110

## Slide 35: Direct Mapping
Simple Control Logic
Great Spatial Locality
Awful Temporal Locality
When does this fail in a direct mapped cache?
char *image1, *image2;
int stride; for(int i=0;i<size;i+=stride) { diff +=abs(image1[i] - image2[i]); }
Notes: When image1 and image2 map in to the same cache line (thrashing)
When stride is the block size or larger (no spatial locality benefits)

## Slide 36: Block Size Tradeoff
With fixed cache size, increasing Block size(M):
  Worse Miss penalty: longer to fill block
  Better Spatial Locality
  Worse Temporal Locality
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Block Size
Notes: 32 – log2(M) if the blocks are aligned

## Slide 37: N-Way Associative Mapping
Like N parallel direct map caches
= =?
…
Valid
…
Tag
Block
…
…
Valid
…
Tag
Block
…
= =?
Addr Cache Tag
Addr Cache Tag
Hit
Cache Block
Notes: Use the “other” one in case of conflict

## Slide 38: Associative Mapping
Can handle up to N conflicts without eviction
Better Temporal Locality
  Assuming good Eviction policy
More Complicated Control Logic
  Slower to confirm hit or miss
  Slower to find associated cache line

## Slide 39: Fully Associative Cache
0
1
2
3
4
5
6
7
2n-1
…
…
…
…
Valid Bit
Tag
Data
…
…
…
0
1
2m-1
= =?
= =?
= =?
= =?
= =?
= =?
= =?
= =?
= =?
Full Associative = 2^N Way Associative
  Everything goes Anywhere!

## Slide 40: What gets evicted?
Approach #1: Random
  Just arbitrarily pick from possible locations
Approach #2: Least Recently Used (LRU)
  Use temporal locality
  Must track somehow – extra bits to recent usage
In practice, Random ~12% worse than LRU

## Slide 41: Cache Arrangement
Direct Mapped – Memory addresses map to particular location in that cache
  1-Way Associative Set
Fully Associative – Data can be placed anywhere in the cache
  2^n-Way Associative Set
N-way Set Associative – Data can be placed in a limited number of places in the cache depending upon the memory address

## Slide 43: My L1 Data Cache
M = ?
N = ?
Tag Size = ?

## Slide 44: My L1 Data Cache
M = 6 bits
  64-byte line size
  64 byte blocks
  2^6 = 64
N = 6 bits
  32kByte -> 15 bits
  8 way -> 3 fewer bits
  M=6 -> 6 fewer bits
Tag Size = 52 bits
  64 bit address space
  Whatever is left over

## Slide 45: 3 C’s of Cache Misses
Compulsory/Coldstart
  First access to a block – basically unavoidable
  For long-running programs this is a small fraction of misses
Capacity
  Had been loaded, evicted by too many other accesses
  Can only be mitigated by cache size
Conflict
  Had been loaded, evicted by mapping conflict
  Mitigated by associativity

## Slide 46: Cache Miss Example
8-word cache, 8-byte blocks. Determine types of misses (CAP, COLD, CONF).
Byte Addr | Block Addr | Direct Mapped | 2-Way Assoc | Fully Assoc
0 |  |  |  | 
4 |  |  |  | 
8 |  |  |  | 
24 |  |  |  | 
56 |  |  |  | 
8 |  |  |  | 
24 |  |  |  | 
16 |  |  |  | 
0 |  |  |  | 
 | Total Miss: |  |  | 

## Slide 47: Cache Miss Example
8-word cache, 8-byte blocks. Determine types of misses (CAP, COLD, CONF).
Byte Addr | Block Addr | Direct Mapped | 2-Way Assoc | Fully Assoc
0 | 0 | Cold |  | 
4 | 0 | Hit (in 0’s block) |  | 
8 | 1 | Cold |  | 
24 | 3 | Cold |  | 
56 | 7 | Cold |  | 
8 | 1 | Conf (w/56) |  | 
24 | 3 | Hit |  | 
16 | 2 | Cold |  | 
0 | 0 | Hit |  | 
 | Total Miss: | 6 |  | 

## Slide 48: Split Caches
Often separate Instruction and Data Caches
  Harvard Architecture: Split I & D
  von Neumann Architecture: Unified
Higher bandwidth
Optimize to usage
Slightly higher miss rate: each cache is smaller

## Slide 49: With Remaining Time
Finish Cache Example (Answers Below)
Find out what your computer’s caches are
Write your own “Pop Quiz” on Caching
We will exchange & take quizes
  Not graded
  Then discuss

## Slide 50: Quiz Ideas
Describe a specific Cache:
  How big is the tag? Where does address X map?
Describe an access pattern:
  Hit Rate? Average Access Time?

## Slide 51: Cache Summary
Software Developers must respect the cache!
  Usually a good place to start optimizing
    Especially on laptops/desktops/servers
  Cache Line size? Page size?
Cache design implies a usage pattern
  Very good for instruction & stack
  Not as good for Heap
  Modern languages are very heapy

## Slide 52: Matrix Multiplication
for (k = 0; k < n; k++){ for (i = 0; i < n; i++){
for (j = 0; j < n; j++){
c[k][i] = c[k][i] + a[k][j]*b[j][i];
}}}
Vs
for (k = 0; k < n; k++){ for (i = 0; i < n; i++){
for (j = 0; j < n; j++){
c[i][j] = c[i][j] + a[i][k]*b[k][j];
}}}
Which has better locality?

## Slide 53: Cache Miss Comparison
Fill in the blanks: Zero, Low, Medium, High, Same for all
 | Direct Mapped | N-Way Set Associative | Fully Associative
Cache Size: Small, Medium, Big? |  |  | 
Compulsory Miss: |  |  | 
Capacity Miss |  |  | 
Conflict Miss |  |  | 
Invalidation Miss |  |  | 

## Slide 54: Cache Miss Comparison
Fill in the blanks: Zero, Low, Medium, High, Same for all
 | Direct Mapped | N-Way Set Associative | Fully Associative
Cache Size: Small, Medium, Big? | Big (Few comparators) | Medium | Small (lots of comparators)
Compulsory Miss: | Same | Same | Same
Capacity Miss | Low | Medium | High
Conflict Miss | High | Medium | Zero
Invalidation Miss | Same | Same | Same

## Slide 55: Cache Miss Example
8-word cache, 8-byte blocks. Determine types of misses (CAP, COLD, CONF).
Byte Addr | Block Addr | Direct Mapped | 2-Way Assoc | Fully Assoc
0 | 0 | Cold | Cold | Cold
4 | 0 | Hit (in 0’s block) | Hit (in 0’s block) | Hit (in 0’s block)
8 | 1 | Cold | Cold | Cold
24 | 3 | Cold | Cold | Cold
56 | 7 | Cold | Cold | Cold
8 | 1 | Conf (w/56) | Conf (w/56) | Hit
24 | 3 | Hit | Conf (w/8) | Hit
16 | 2 | Cold | Cold | Cold
0 | 0 | Hit | Hit | Cap
 | Total Miss: | 6 | 7 | 6

## Slide 56: Replacement Methods
If we need to load a new cache line, where does it go?
Direct-mapped
Only one possible location
Set Associative
N locations possible, optimize for temporal locality?
Fully Associative
All locations possible, optimize for temporal locality?

## Slide 57: Cache Access Example
Assume 4 byte cache
Access pattern:
00001
00110
00001
11010
00110
0
1
2
3
Valid Bit
Tag
Data

## Slide 58: Cache Access Example
Assume 4 byte cache
Access pattern:
00001
00110
00001
11010
00110
0
1
2
3
0
1
1
0
000
001
M[00001]
M[00110]
Valid Bit
Tag
Data
Compulsory/Cold Start miss

## Slide 59: Cache Access Example (cont.)
Assume 4 byte cache
Access pattern:
00001
00110
00001
11010
00110
0
1
2
3
0
1
1
0
000
110
M[00001]
M[11010]
Valid Bit
Tag
Data
Compulsory/Cold
Start miss

## Slide 60: Cache Access Example (cont. 2)
Assume 4 byte cache
Access pattern:
00001
00110
00001
11010
00110
0
1
2
3
0
1
1
0
000
001
M[00001]
M[00110]
Valid Bit
Tag
Data
Conflict Miss