## Slide 1: b0101 Time for Time
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)
Texas Instruments Data Sheets

## Slide 3: Today
Review Approximation Hacks from Yesterday
Review Boolean Design Process
The ravages of time
Latches, Flip Flops, Sandals

## Slide 4: Its Log
From lecture b0010:
  1 R=r^n = n R=r digits
1 RA Digit is ‘worth’ logRBRA
Hex: RA = 16, RB = 2
  log2 (16) = 4
  1 Hex digit is ‘worth’ 4 binary digits

## Slide 5: Its Log
24 binary digits ≈ 7 decimal digits
  log10(2) * 24 ≈ 7.2247198…
log10(2)≈ 0.3 log2(10)≈ 3.3
2^ ± 126 ≈ +/-10^ ± 38
  126 * .3 ≈ 37.929…
How many digits does 2^24 have in decimal?
Notes: 2^24 = 16777216 => 8 digits

## Slide 6: Its Log
How many Digits should I display?
  ADS1292 is a 24bit ADC, 19.34ENOB
  ICL7106 is a 2000 Count ADC
  AS5048 is a 14 bit rotary hall effect encoder
How good is the ADC in your multimeter?
  Harbor freight 3 digit ($5.29)
  Agilent 34460A 6.5 digit ($945)
  Agilent 3458A 8.5 digit ($9,267)
Notes: log10(2^24) = 7.2
log10(2^19.34) = 5.8
log10(2000) = 3.3
log10(2^14) = 4.2
Log2(10^3) = 9.9
Log2(10^6.3) = 21
Log2(10^3) = 27.5

## Slide 7: Combinational Logic Design Process
Understand the problem
  what is the circuit supposed to do?
  write down inputs (data, control) and outputs
  draw block diagram or other picture
Break problem down in to manageable, convenient chunks
Formulate the problem in terms of a truth table or other suitable design representation
  truth table, boolean algebra, etc.
Choose implementation Target
  PAL, PLA, Mux, FPGA, Discrete Gates
Follow Implementation Procedure
  K-maps, Boolean algebra, algorithmic simplification
Notes: PAL – Programmable Array Logic (ANDs programmable)
PLA – Programmable Logic Array (ANDs and ORs programmable)
FPGA – Field Programmable Gate Array

## Slide 8: Process Example: 2’s Comp Adder Understand the Problem
what is the circuit supposed to do?
  Add two numbers in 2’s complement
write down inputs (data, control) and outputs
  Operands: A[n], B[n], Carry In
  Outputs: S[n], Overflow, Carry Out
draw block diagram or other picture

## Slide 9: Process Example: 2’s Comp Adder Break problem down
Pieces I already know how to make:
  Overflow detect = XNOR
Repeated pieces:
  Each bit is handled similarly

## Slide 10: Process Example: 2’s Comp Adder Formulate a Solution
Generate a truth table
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
CO
S

## Slide 11: Process Example: 2’s Comp Adder Formulate a Solution
Generate a truth table
Generate Equation
Simplify
Create Circuit
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
CO
0
0
0
1
0
1
1
1
S
0
1
1
0
1
0
0
1

## Slide 12: Combinational vs. Sequential Logic
Combinational logic
no feedback among inputs and outputs
outputs are a pure function of the inputs
e.g., seat belt light:
(Dbelt, Pbelt, Passenger) mapped into (Light)
Network implemented from logic gates.
The presence of feedback
distinguishes between sequential
and combinational networks.
-
-
-
X
1
X
2
X
n
Logic
Network
Z
1
Z
2
Z
m
-
-
-
Logic Circuit
Driver_belt
Passenger_belt
Passenger
Seat Belt Light

## Slide 13: Circuit Timing Behavior
Simple model: gates react after fixed delay
A
B
C
D
E
F
0
1
0
1
A
B
C
D
E
F

## Slide 14: Circuit Timing Behavior
Simple model: gates react after fixed delay
A
B
C
D
E
F
0
1
0
1
A
B
C
D
E
F

## Slide 15: Hazards/Glitches
Circuit can temporarily go to incorrect states
Copilot Autopilot Request
Pilot Autopilot Request
Pilot in Charge?
Autopilot Engaged
A
B
C
CAR
PIC
PAR
A
B
C
AE
Must filter out temporary states

## Slide 16: Hazards/Glitches
Circuit can temporarily go to incorrect states
Copilot Autopilot Request
Pilot Autopilot Request
Pilot in Charge?
Autopilot Engaged
A
B
C
CAR
PIC
PAR
A
B
C
AE
Must filter out temporary states
OH NO

## Slide 17: Safe Sequential Circuits
Clocked elements on feedback, perhaps outputs
  Clock signal synchronizes operation
  Clocked elements hide glitches/hazards
Clock
-
-
-
X
1
X
2
X
n
Logic
Network
Z
1
Z
2
Z
m
-
-
-
Clock
Data
Valid
Compute
Compute
Valid
Compute

## Slide 18: Safe Sequential Circuits
Clocked elements on feedback, perhaps outputs
  Clock signal synchronizes operation
  Clocked elements hide glitches/hazards
Clock
-
-
-
X
1
X
2
X
n
Logic
Network
Z
1
Z
2
Z
m
-
-
-
Clock
Data
Stable
GLITCHES
GLITCHES
Stable
GLITCHES

## Slide 19: A what-ed wholement?
Clocked or Enabled Elements
  Flip Flops and Latches
“Hold on” to state until triggered to update.
Many kinds

## Slide 20
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 21
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 22
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 23
http://www.ti.com/lit/ds/symlink/sn74lvc1g374.pdf

## Slide 24: Vocab!
Setup – Required stability before
Hold – Required stability after
Propagation Delay – Until outputs update

## Slide 25: Reinventing the SR Latch
http://en.wikipedia.org/wiki/File:R-S_mk2.gif
“SR” for “Set Reset”
Cross-coupled NOR/NAND
S | R | Q Next
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 26: Reinventing the SR Latch
http://en.wikipedia.org/wiki/File:R-S_mk2.gif
“SR” for “Set Reset”
Cross-coupled NOR/NAND
S | R | Q Next
0 | 0 | Q
0 | 1 | 0
1 | 0 | 1
1 | 1 | X

## Slide 27: SR Latch Timing
S
R
Q
Q ̅

## Slide 28: Design Time!
Invent new types of latches by adding control logic around a SR or S ̅R̅ latch
Treat the SR as a magic box
Create a truth table to translate your requirements to the SR’s inputs
  Use to make a complete circuit

## Slide 29: Boreds
Gated SR latch
  Inputs “work” only while Enable is True
  When Enable is false, S/R have no effect
Design a Gated D Latch
  One Data input instead of Set Reset.
  Output follows input while enabled
  When Enable is false, Output holds last value
Smallest design? Fastest? Weirdest?

## Slide 30: You promised a Flop
Confusing vocab – they are similar
A latch is typically Enabled
A Flip Flop is typically Clocked
All are forms of ‘Bistable Multivibrators’

## Slide 31: Master Slave D-Flip Flop
Two D-Latches in series with opposite polarity Enable lines
Pulse Triggered
  Capture on one edge
  Display on the other
http://en.wikipedia.org/wiki/File:Negative-edge_triggered_master_slave_D_flip-flop.svg

## Slide 32: Edge Triggered D-Flip Flop
Functionally similar to Master Slave
Edge Triggered, not Pulse
  Don’t waste half your clock period!
Construction highly process dependent
  Can be roughly three SR Latches
  Can be “Dynamic Logic” – Learn in VLSI

## Slide 33: Edge Triggered D-Flip Flop
Always has:
  Clk, D, Q
May also have:
  S, R, ~Q
  Set and Reset are asynchronous (ignore clock)
http://en.wikipedia.org/wiki/File:D-Type_Flip-flop.svg
Clk | D | Q
↑ | 0 | 0
↑ | 1 | 1
Other | X | Q

## Slide 34: Common Uses
In between processing stages
“Debounce” inputs
  Hide external noise / uncertainty from the inputs
Synchronization

## Slide 35: Other Flops
Ternary: Flip-Flap-Flop.
T Flip Flop
  Toggles on each clock strobe
  Good for cutting frequency in half
JK Flip Flop
  Clocked SR flip flop that also supports toggling

## Slide 36: Final Bord
Create a T Flip Flop from an D Flip Flop
Create 16x frequency divider from T Flip Flops
Create 10x frequency divider from ???

## Slide 37: Edge Triggered D-Flip Flop