## Slide 1: b0110 Fabric and Trust
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Acknowlegements
ARM Holdings: M3 Cortex Instruction Set
Addison Wesley Longman: Figures
Wikipedia: Figures
Asic World

## Slide 3: Today
Decoders , Muxes, LUTs, Oh My
My PALs, CPLDs and FPGAs
Do a Barrel Roll
Trust Issues
Preparation for your first Lab

## Slide 4: Muxes, AKA Multiplexor
Select or switch between inputs
Has one output, two types of inputs
  ‘Input’
  ‘Select’
#‘Select’ >= log2(# ‘Input’)
  8 inputs needs 3 select (address) bits
Notes: Figure Credit: Wikipedia

## Slide 5: (Binary) Decoder
Also called a ‘demux’
  Because it is the exact opposite.
Only one output is active at once
Usually has 2^inputs number of outputs
Sometimes has an enable input
  All Low or All Hi-Z
Notes: Figure Credit: Wikipedia

## Slide 6: Width
The width of a bus is how many bits are in that signal.
  A wire is a bus with width = 1
Width of I4Q4?

## Slide 7: Look Up Tables
A form of Read Only Memory
Defined by Width and Depth
  Width = How many bits per word
  Depth = How many words available
Constructed as Muxes with constant inputs
  Use Select to look up the table entry

## Slide 8: Designing from Documentation
Clone the following parts from basic gates:
  DigiKey Part No NC7SZ157P6XTR-ND
  568-4448-2-ND
  568-8857-1-ND
  MC74HC164ADR2GOSTR-ND (Optional)
    Hint: Use D-Flip-Flops as a black box
Do your solutions match theirs?
Notes: 1x 2:1
1x 3:8

## Slide 9: Programmable Logic
1969: XC157
  Mask Programmed, 12 gates 30 pins
1978: Programmable Logic Arrays
  Field Programmed by burning fuses
  Sum of Products
  Equivalent to “Dozens” of gates
1985: Generic Array Logic
  Field reprogammable

## Slide 10: Programmable Logic
Complex Programmable Logic Device:
  1000s to 10ks of Gates equivalent
  Non-volatile (typically)
  Sum of Products (typically)

## Slide 11: Field Programmable Gate Array
1985: Xilinx releases the XC2064
  Equivalent to 1000 gates
Typical Features:
  Volatile (Reprogram every time power is applied)
  Sea of Gates (Look Up Tables + Routing)
  Programmable Logic Blocks
  “Hard” Features – RAM, Multipliers, CPUs

## Slide 12: Xilinx Zynq 7000
Up to 6.6 Million Gates Equivalent
  277,400 Look Up Tables
  554,800 Flip Flops
  >2 Trillion Multiply Accumulates per second
Dual Core 1GHz ARM Cortex A9
  2.5 DMIPS/MHz
$5,401.26

## Slide 13: Fabric Design
FPGA ‘Fabric’ is a sea of reconfigurable logic blocks embedded in reconfigurable routing logic.
The reconfigurable logic used to be mostly look up tables with configurable constants.
Now it is LUTs + other stuff too

## Slide 14: Fabric Design
Design a small piece of an FPGA using:
  Decoders
  Muxes
  Basic Gates
  Programmable Bits (Ignore Construction for now)
Use your FPGA cell to create:
  AND
  XOR
  Adder (Half? Full?)
Start by figuring out your requirements:
  Width? Depth?

## Slide 15: Do a Barrel Roll
We can multiply or divide a number by 2 by moving it left or right one position
This is called a “shift”

## Slide 16: Do a Barrel Roll
“Arithmetic” shifts obey 2’s complement
  Sign extension
“Logical” shifts do not
  Assume unsigned
  Pad zeros
Barrel Rotate “wraps” around

## Slide 17
http://bwrc.eecs.berkeley.edu/research/pico_radio/Test_Bed/Hardware/Documentation/ARM/chap3.pdf

## Slide 18: What could possibly go wrong?
Sketch a shifter to do at least one type of shift
  Hint: Layers of Muxes
List possible ways it could be busted
  Specific errors in the design of the component
Come up with a test plan for your shifter
How can you achieve full coverage without exhaustion?

## Slide 19: Intro to Verilog
Verilog is a Hardware Description Language
  Describes a digital logic circuit
  Syntax is like C
  Writing in verilog is not at all like writing in C
Synthesized to create:
  FPGA bitstreams
  ASICs

## Slide 20: Structural Verilog Design Flow
Start with a circuit diagram
Give names to all wires and gates

## Slide 21: Structural Verilog Design Flow
Start with a circuit diagram

## Slide 22: Structural Verilog Design Flow
Start with a circuit diagram
Give names to all wires and gates

## Slide 23: Structural Verilog Design Flow
Start with a circuit diagram
Give names to all wires and gates
List wires and gates in code
wire wire1, A, B, C, Out;
or U1
and U2

## Slide 24: Structural Verilog Design Flow
Start with a circuit diagram
Give names to all wires and gates
List wires and gates in code
Connect gates to wires, Outputs first
wire wire1, A, B, C, Out;
or U1(wire1, A, B);
and U2(Out, wire1, C);

## Slide 25: Structural Verilog Design Flow
Start with a circuit diagram
Give names to all wires and gates
List wires and gates in code
Connect gates to wires, Outputs first
Add Delays
wire wire1, A, B, C, Out;
or U1 #(50) (wire1, A, B);
and U2 #(50) (Out, wire1, C);

## Slide 26: Lab Preparation
Select 1 or 2 partners
Read through MP0.pdf
  Questions?
Begin paper&pencil sketching of modules
You have the rest of class to begin work
  Start Installing ModelSim Student Edition