## Slide 1: b10110 Retrospective Planning
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Today
Reminder: Final Projects
Mp3 Checkin
An Olin Tradition
Focused review of material to date

## Slide 3: Initial Project Proposal
Project Name
Team Members
1-3 paragraphs description of project
Red / Yellow / Green Feature sets
2 potential things that can go wrong, with mitigations
What are your two next steps?
1-2 Pages Total
Due Wednesday after Turkeys Get Ate

## Slide 4: MP3 Checkin
Work Plan updates were very sparse!
  We use these
Confusion Points:
  Deliverable 4: Millions of Instructions Per Second
  Memory Map
  Ending Execution

## Slide 5: Ending Execution
EXTREMELY rare to actually end execution
  OS regains control in typical scenario
Exceptions:
  This Lab
  Error situations
  Interruptible Waits

## Slide 6: Ending Execution: Ignore It
main:
#do stuff
j end
other_functions:
#more stuff
end:

## Slide 7: Ending Execution: Fall off the End
main:
#do stuff
j end
other_functions:
#more stuff
end:
MARs:
-- program is finished running (dropped off bottom) --

## Slide 8: Ending Execution: Fall off the End
main:
#do stuff
j end
other_functions:
#more stuff
end:
MARs:
-- program is finished running (dropped off bottom) --
ModelSim:
Executes the rest of memory like it was code

## Slide 9: Ending Execution: Jump Trap
main:
#do stuff
j end
other_functions:
#more stuff
end:
j end
MARs:
Runs forever
ModelSim:
Doesn’t Execute the rest of memory like it was code

## Slide 10: MARS Breakpoints

## Slide 11: Ending Execution: Syscall 10
main:
#do stuff
#end
li $v0, 10
syscall
other_functions:
#more stuff
MARs:
-- program is finished running --
ModelSim:
No idea what Syscall is

## Slide 12: Ending Execution: Syscall 10
main:
#do stuff
#end
li $v0, 10
syscall
other_functions:
#more stuff
MARs:
-- program is finished running --
ModelSim:
No idea what Syscall is
WHY $v0?!?!?!? BFYTW

## Slide 13: Ending Execution: $stop
If you’d like, use $stop to make debugging easier
Not required
Maybe $stop when the decoder sees syscall?
  FANCY SCHMANCY

## Slide 14: Memory Map

## Slide 15: Memory Map
Defines how data memory is split up and used
We care about:
  Stack pointer
  Program Counter
  Memory Size(s)
  Memory Location(s)

## Slide 16: Memory Map: Stack Pointer
Initialize in your own code explicitly
  li $sp 0x3ffc
Starts at top of data
  0x3ffc
  =0x4000-4 (word size)
Ends at 0x3000
  Hopefully

## Slide 17: Memory Map: Program Counter
Initialize in Verilog
  Initial pc=0
“Text” means code
Starts at 0
Ends at 0x1000 (-4)

## Slide 18: Memory Map: Size
Compact is 0x4000
Highest of:
  User Space
  Stack
  Heap
  Data
  Text

## Slide 19: Memory Map: Size
Compact is 0x4000
  BYTES
16kB

## Slide 20: An Olin Tradition
We are hopping in the way-back machine
  To a simpler time
  To a time of innocence and confusion
Welcome to 2004

## Slide 21: Retrospective
Deep look back in to the course
  For personal review
  For the good of the next class
Generate two distinct deliverables
  Outline of Main Ideas for review
  Hindsight tweaks to the course flow

## Slide 22: Organization
In teams, select specific lecture(s)
  Organize at: http://goo.gl/HKwjft
First pass:
  Clean slides for errors
  Put answers to prompts in the “notes” section
    Or as duplicate slides at the end of the deck
  Put comments on effectiveness in the “notes”
    Example: [Eric ‘07] – Confused by XYZ, perhaps try __?
  comparch14@gmail.com [Retrospective] Deck Title

## Slide 23: Second Pass
Create an outline for lessons learned
  Collaboratively: http://goo.gl/HKwjft
Include:
  Main ideas
  Vocabulary
  Reference links
Suggestion: Do this in a separate doc to avoid edit-time conflicts of 25 people

## Slide 24: Third Pass
Prepare a 5 minute wrap-up lecture
  Speech & Whiteboard, PPT not necessary
Intended Audience:
  Took CompArch 5 years ago
  Just got a new job that uses Topic X
  Needs to bone up real fast
These will happen Thursday

## Slide 25: Thursday
Recreate board work for first 30 minutes
  Take photos of results
  Take notes of what makes sense now that didn’t before
Give prepared lightning lectures

## Slide 26: By Monday
Read http://www.emulators.com/docs/pentium_1.htm
  Skim / skip the assembly
  Take with a grain of Salt
  Just that page, don’t continue to part 2
Is the Pentium 4 really that bad?
What happened in the 14 years in between?
  Did Intel learn from its mistakes?
  Were they actual mistakes?
What more do you want to know?
We will discuss in class.